## Slide 1: Multi-link Policy Framework
Date: 2019-11-11
Authors:
Name | Affiliations | Address | Phone | Email
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Das Dibakar |  |  |  | das.dibakar@intel.com
Chittabrata Ghosh |  |  |  | chittabrata.ghosh@intel.com
Carlos Cordeiro |  |  |  | carlos.Cordeiro@intel.com
Notes: September 2012

## Slide 2: Abstract
Multi-link operation is a feature agreed in EHT PAR.
  Multi-link/multi-channel aggregation and operation.
Multi-link operation is applicable to address many different use cases. Depending on the specific characteristics and requirements of these use cases, we need to configure different rules for Multi-link operation.
In this presentation, we call this set of rules the Multi-link policy, and propose the fundamental framework for Multi-link policy.

## Slide 3: Multi-link framework as shown in [1]
Example 2
Example 1

## Slide 4: Multi-link operations
Multi-link operations between an AP MLD and STA MLDs can be divided into several aspects:
  Pre-association
  Post-association management plane
  Post-association data plane
For each aspect, depending on the requirements of use cases, different Multi-link operation rules need to be enforced to regulate the behaviors of AP MLD and STA MLDs.
In the following, we use two specific use cases, load balancing and traffic separation & prioritization, to show how Multi-link operation rules vary with different scenarios.

## Slide 5: Load Balancing
AP1 operating on 2.4 GHz
AP2 operating on 5 GHz
AP3 operating on 6 GHz
STA1
STA2
STA3
STA4
STA5
AP1 operating on 2.4 GHz
AP2 operating on 5 GHz
AP3 operating on 6 GHz
STA1
STA2
STA5
STA4
STA6
STA3
AP MLD
AP MLD
AP MLD recommends link switch for
STA MLDs for load balancing
Example requirements for Multi-link operations for load balancing:
Should enable frequent link transitions
Maintain balanced load across multiple links and avoid congestion in any link
Admission control may be enforced if one link is already heavily loaded
We therefore need to define the following rules:
Link transition: A way to enable the AP MLD to recommend link transitions for STA MLDs.
Pre-association: A way to enable the AP MLD to designate specific links for STA MLDs to perform Multi-link setup.
STA6
No !
Yes
X
AP MLD implements admission control
for unassociated STA MLDs in each link to
avoid congestion

## Slide 6: Traffic Separation & Prioritization
AP1 operating on 2.4 GHz
AP2 operating on 5 GHz
AP3 operating on 6 GHz
STA1
STA2
STA3
AP MLD
STA5
STA4
STA MLDs with mainly
Voice traffic
STA MLDs with mainly
Video traffic
STA MLD 7
STA MLD 8
2.4/5 GHz links serve
voice traffic
6 GHz link serves
video traffic.
New STA MLDs perform Multi-link
Setup based on their traffic type
STA6
Main requirements for Multi-link operations for traffic separation and prioritization:
TID-to-link mapping: different TIDs are mapped to different links
Admission control can be enforced based on traffic types of unassociated STA MLDs
Restrictions on link transition and aggregation due to TID-to-link mapping
EDCA parameters can be adjusted to prioritize certain types of traffic in certain links (for example, use Trigger-based only channel access)
We therefore need to define the following rules:
TID-to-link mapping: A way to map TIDs across different links.
EDCA parameters: A way to adjust EDCA parameters in certain link(s).
Pre-association: A way to enable the AP MLD to designate specific links for STA MLDs to perform Multi-link setup.
STA MLD 9

## Slide 7: Multi-link policy
As shown, different use cases require Multi-link operations be used in different manners, therefore a set of operating rules between the AP MLD and STA MLDs need to be determined and imposed to regulate AP/STA behaviors based on specific requirements of use cases . We call this set of rules the Multi-link policy.
We propose to define a way to specify and advertise the Multi-link policy negotiated and enforced between an AP MLD and STA MLDs.
  The Multi-link Policy could be included in broadcast frames like Beacon frame and Probe Response frame, or unicast frames addressed to each STA MLD individually.
  AP MLD can dynamically adjust certain parameters of Multi-link Policy according to specific use cases it currently focuses, by negotiating with STA MLDs and updating the Multi-link Policy and advertising it to STA MLDs.
  This Multi-link Policy could be signaled by a separate element, or part of other elements, as long as the functions are covered.
We therefore establish a unified framework that is flexible enough to apply multi-link operations to address different use cases.

## Slide 8: Example of Multi-link Policy element
If defined as a separate element, we can introduce a new Multi-link Policy element.
  However, we can also consider reusing/extending existing elements, as long as the functions are covered.
Since some aspects of the Multi-link policy apply across different links (like band transition and aggregation), while some can be link-dependent (like TIDs allowed, channel access), we propose to define the Multi-link Policy element as follows:
  The Common Policy subelement defines the policy applied across all enabled links.
  Each Link Specific Policy subelement defines the policy that only applies to one specific link.
  This is similar to the 11ax Trigger frame which consists of a Common Info field and several User Info fields.
Element ID | Length | Element ID Extension | Common Policy | Link Specific Policy | Link Specific Policy | … | Link Specific Policy
1 | 1 | 1 | TBD | TBD | TBD | … | TBD

## Slide 9: Illustration of Multi-link Policy element
Common Policy | Link Specific Policy (Link 1, 2.4 GHz) | Link Specific Policy (Link 2, 5 GHz) | Link Specific Policy (Link 3, 6 GHz)
TBD | TBD | TBD | TBD

## Slide 10: Conclusions
We proposed the concept of Multi-link policy, which is a set of rules regulating multi-link operations between an AP MLD and STA MLDs.
The Multi-link policy enables a unified framework that is flexible to apply multi-link operations to address different use cases.

## Slide 11: References
[1] 11-19-0773-07-00be-multi-link-operation-framework