## Slide 1: Precoding performance using implicit channel estimation
Date: 2019-11-08
Authors:

## Slide 2: Introduction
Current 802.11 sounding protocols are based on sounding followed by explicit sounding feedback
These explicit protocols can potentially take up a lot of airtime
Implicit sounding [1, 2] has been suggested as a way to reduce sounding overhead
Overhead of different schemes (implicit vs. explicit) was compared in [4]

## Slide 3: Introduction
An important question is how well implicit channel estimation (CE) performs when used with precoding
This submission looks at precoding performance using either implicit or explicit channel estimates
We use a combination of measured and simulation results

## Slide 4: Implicit channel estimation
Channel estimate obtained for “reverse” channel
Beamformer may request BFee to send NDP
  Or wait for an ad-hoc opportunity …
BFer estimates reverse channel from the NDP (or other packet)
BFer adjusts reverse channel with calibration coefficients and uses it as an approximation of the forward channel

## Slide 5: Experimental & simulation setup
Channel measurements were taken in different environments
  Shield Box
  Office environment
BFer: 4x4 AP
BFee: 2x2 STA
H matrix collected using NDP on both ends
  2x4 AP→STA channels
  4x2 STA→AP channels

## Slide 6: Experimental & simulation setup (2)
Calibration was performed off-line on the measured (reverse) channels (MATLAB)
Calibration coefficients were determined using MMSE criterion
Precoding based on explicit DL channel was compared with precoding based on calibrated UL channel
  Using the measured channels in simulation
  Both BF and MU

## Slide 7: Setup

## Slide 8: Results for BF
Three different scenarios are considered
  Performance without BF
  Performance with BF using explicit channel information
  Performance with BF using calibrated implicit channel information
Channel measurements were taken in shielded environment and in office environment
  As recorded by the Wi-Fi devices
Measured and calibrated channels were used in MATLAB simulation to find performance

## Slide 9: SU BF performance - shieldbox
MCS 7, 2 SS
Setup in shielded environment
Virtually no difference between Implicit CE with and explicit CE

## Slide 10: SU BF performance – over the air
MCS 7, 2 SS
Measurements taken in office environment
Minor degradation from implicit feedback

## Slide 11: Calibration coefficients
amplitude
phase

## Slide 12: Results for MU
Three different scenarios considered
  MU with 4-stream feedback
  MU with 8-stream feedback
  MU with implicit (calibrated) channel feedback
AP is 8x8, STA is 2x2
Channels are simulated channel D with added impairments to model front-end
  Amplitude offset
  Random phase offsets

## Slide 13: MU performance
Simulated Channel D with various amplitude offsets
Random phase offsets
Major improvement relative to 4SS feedback
1 – 1.5 dB difference relative to 8SS feedback

## Slide 14: Summary
Presented results for precoding based on implicit channel estimation
Simple calibration algorithm used
  More advanced algorithms could be considered
SU performance
  Little to no degradation
MU performance
  Major improvement over 4-stream feedback
  Minor degradation relative to 8-stream feedback
NOTE: impact of overhead not considered in assessing performance

## Slide 15: Conclusion
Implicit channel estimation with calibration is a good candidate method for reducing sounding overhead

## Slide 16: References
[1] MU sounding improvements, IEEE 802.11-18/1191
[2] Implicit Channel Sounding in IEEE 802.11, IEEE 802.11-19/0768
[3] Implicit Channel Sounding in IEEE 802.11 (Feasibility Study), IEEE 802.11-19/0767
[4] Implicit sounding overhead analysis, IEEE 802.11-19/1268