## Slide 1: Multi-link Management
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Motivation
Some key usage cases are proposed with multi-band capability [1-3]
  Steering/load balancing, aggregation, AP power save, coexistence with other stds, QoS, etc.
In this contribution, we suggest some procedures for the above-mentioned usage cases for multi-band and address some considerations

## Slide 3: Recap on Terminologies [1-2]
AP multi-link device (AP MLD)
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Non-AP multi-link device (Non-AP MLD)
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
Disabled
multi-link set
Enabled
multi-link set

## Slide 4: Turning off links
A non-AP MLD can turn off some of its operating links
  A non-AP MLD can turn off its radio to save the power with existing disassociation procedure
  When the STA wants to turn on Link 1 again, existing association procedure may or may not be required
    If parameter update is needed, a certain procedure can be performed on Link 2 or Link 3 in advance
AP MLD
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Non-AP MLD
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
AP MLD
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Non-AP MLD
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3

## Slide 5: Alternating active links
An MLD can alternate its active link among the supported multi-link set
  This can be achieved by turning on a link among disabled multi-link set and then turning off a link among enabled multi-link set
AP MLD
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Non-AP MLD
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
AP MLD
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Non-AP MLD
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
Establish Link 3
Disconnect
Link 2

## Slide 6: Switching band of STA with a common radio [3]
A STA can operate with a common radio among the supportable links
  Antennas of the STA with shared radio can use either 5 GHz or 6 GHz
  Adopting this shared radio can allow the STA to support both bands
  To this end, link switching procedure needs to be defined
    Existing channel switching procedure can be reused for this: Extended channel switch announcement element can support channel switch mode (forcing STAs to stop transmissions), new operating class, new channel number, and channel switch count (time period until the channel switch event)
    Else, a new procedure for link switching can be newly defined
AP MLD
AP 1
on 2.4 GHz
AP 2
on 5 GHz
Non-AP MLD
STA 1
on 5 GHz
Link
1
Link
2
AP 3
on 6 GHz
Link
3
AP MLD
AP 1
on 2.4 GHz
AP 2
on 5 GHz
Non-AP MLD
STA 1
on 6 GHz
Link
1
Link
2
AP 3
on 6 GHz
Link
3

## Slide 7: Switching band of STA with a common radio
For some APs with spatial limitation (e.g., Soft AP), an AP may operate with a common radio as well
  Antennas attached to MLDs can operate either 5 GHz or 6 GHz
  It can be achieved by existing channel switching procedure
  With this band switching, crowded channel can be avoided and traffic load can also be balanced
  However, in this case, legacy 5 GHz stations would loss their connection
AP MLD
AP 1
on 2.4 GHz
AP 2
on 5 GHz
Non-AP MLD
STA 1
on 2.4 GHz
STA 2
on 5 GHz
Link
1
Link
2
AP MLD
AP 1
on 2.4 GHz
AP 2
on 6 GHz
Non-AP MLD
STA 1
on 2.4 GHz
STA 2
on 6 GHz
Link
1
Link
2

## Slide 8: Switching band of STA with a common radio
Non-AP MLD B (Shared radio support)
Non-AP MLD B (Shared radio support)
STA B1
on 6 GHz
To overcome this disconnection problem of legacy STAs, a subset of links may remain in the frequency band where they originally existed
  For instance, assuming AP 1 has 4 antennas, the AP 1 is split into AP 1 and AP 2, and they are allocated on 5GHz and 6GHz, respectively
  STAs supporting shared radio concept (non-AP MLD B) can selectively move to a new AP (AP 2)
  Legacy STA can maintain its connection with the AP
AP MLD
AP 1
on 5 GHz
AP MLD
Link
2
AP 2
on 6 GHz
AP 1
on 5 GHz
Non-AP MLD A (No shared radio support)
STA A1
on 5 GHz
Link
1
Non-AP MLD A (No shared radio support)
STA A1
on 5 GHz
Link
1
STA B1
on 5 GHz

## Slide 9: Considerations
When it comes to turning off the link to save the power, any explicit signaling may not be needed
  If an MLD has a common queue, the MLD has only to re-map between TID and link
  On the other hand, if an MLD has seperated queues over links, seamless transfer may not be possible
In case of alternating links, existing reassociation procedure can be used
  This case is same with the above-mentioned turning off cases
If some radios can change its frequency band, this procedure is analogous to existing (extended) channel switching
  In this case, legacy devices may not be supported due to the switched band
To support the legacy devices, a subset of links may remain on the link where they existed
  To this end, some additional information can be included in addition to existing channel switching
  Since a BSS is newly created, information regarding the BSS can be announced such as Band Information, NSS, BSSID, Beacon Interval, and so on
  Some attributes, e.g., NSS, for the remaining AP may be changed and they needs to be announced

## Slide 10: Straw Poll 1
Do you agree to add the following text to the TGbe SFD?
  TGbe shall support that an MLD can support a non-AP STA which can switch its operating band (e.g., 5 GHz and 6 GHz)

## Slide 11: Straw Poll 2
Do you agree to add the following text to the TGbe SFD?
  TGbe shall support that an MLD can support an AP STA which can switch its operating band (e.g., 5 GHz and 6 GHz)

## Slide 12: References
[1] 19/0822r9, “Extremely efficient multi-band operation”
[2] 19/1358r0, “Multi-link operation management”
[3] 19/1528r2, “Multi-link: Link management”