## Slide 1: Constrained Multi-link Operation
Date: 2020-03-13
Authors:

## Slide 2: Recap: Constrained Multi-Link Device (MLD)
A Constrained MLD is a MLD with which in-device coexistence (IDC) interference occurs when more than one STA within the MLD simultaneously transmits and receives frames on multiple links.
  When simultaneous Tx and Rx occur on 2.4 GHz band and 5 GHz links, the IDC interference is probably negligible.
  But, the IDC interference caused by simultaneous Tx and Rx on 5 GHz band and 6 GHz band links may be significantly worse depending on some implementation factors such as RF filter performance.

## Slide 3: Motivation
It is necessary that a constrained MLD avoids transmitting and receiving frames on multiple links simultaneously.
This contribution proposes that a STA in a constrained MLD should exchange RTS/MU-RTS and CTS frames to protect frame exchange of other STAs in the MLD.

## Slide 4: RTS/CTS procedure in the constrained MLD Case 1: a TXOP responder is a constrained MLD
When a STA within a MLD that obtains a TXOP sends a frame to a peer STA within a constrained MLD, the STA should initiate the RTS/MU-RTS and CTS frame exchange with the peer STA.
  But, different from the baseline rule,
    “If the NAV indicates idle, the STA shall respond with a CTS frame after a SIFS. Otherwise, the STA shall not respond with a CTS frame.”
  The peer STA may not respond with a CTS frame even though the NAV is idle, if the constrained MLD determines that the frame exchange with the STA is not feasible due to IDC interference.
    Such determination by the constrained MLD is an implementation issue.

## Slide 5: RTS/CTS procedure in the constrained MLD Case 1: a TXOP responder is a constrained MLD
When a STA within a constrained MLD responds with the CTS frame to the received RTS/MU-RTS frame, other STAs within the constrained MLD should not access a channel during the time indicated by the Duration information in the received RTS/MU-RTS frame.
  But, before the Duration time expires, if the STA determines that no more frames will be sent to itself, other STAs in the constrained MLD can resume the medium access.
    For example, a frame having the EOSP subfield set to 1 means this is the last frame transmitted to the STA within the same TXOP.

## Slide 6: RTS/CTS procedure in the constrained MLD Case 1: a TXOP responder is a constrained MLD
As in the below figure, the MU-RTS frame sent on the Link 1 prevents the channel access on the Link 2 from the MLDs addressed by the MU-RTS frame.
  While receiving a PPDU, a channel access availability determination on other links may be not necessary.
L1 STA in MLD1
L2 STA in MLD1
L1 STA in C-MLD2
L2 STA in C-MLD2
MU-RTS
CTS
A-MPDU (to MLD2 and 3)
BA
A-MPDU (only to MLD2)
BA
Channel access on Link 2 is not available.
L1 STA in C-MLD3
L2 STA in C-MLD3
CTS
BA
Channel access on Link 2 is not available.
Backoff
RTS
CTS
Busy
When the MLD1 indicates that there is no more frames addressed to the MLD3,
the MLD3 may resume the channel access on the Link 2 after the BA.

## Slide 7: RTS/CTS procedure in the constrained MLD Case 2: a TXOP holder is a constrained MLD
When a STA within a constrained MLD that obtains a TXOP sends a frame to a peer STA within another MLD, the STA should initiate the RTS/MU-RTS and CTS frame exchange with the peer STA.
  The peer STA may not respond with a CTS frame even though the NAV is idle, if it determines that the frame exchange with the STA within the constrained MLD is not feasible due to IDC interference.
    Such determination by the constrained MLD is an implementation issue.

## Slide 8: RTS/CTS procedure in the constrained MLD Case 2: a TXOP holder is a constrained MLD
When a STA within a MLD responds with the CTS frame to the RTS/MU-RTS frame received from a peer STA within another constrained MLD, other STAs in the MLD should not send a frame to any STA within the constrained MLD during the time indicated by the Duration field in the received RTS/MU-RTS frame.
  Otherwise, the STA that received the RTS/MU-RTS frame may not respond with a CTS frame even though the NAV is idle.

## Slide 9: RTS/CTS procedure in the constrained MLD Case 2: a TXOP holder is a constrained MLD
As in the below figure, the MLD1 does not schedule a frame to the MLD2 during the time indicated by the Duration field in the received RTS frame from the MLD2.
  The MLD1 can still schedule a frame to other MLDs (e.g., the MLD 3 in the figure).
L1 STA in MLD1
L2 STA in MLD1
L1 STA in C-MLD2
L2 STA in C-MLD2
RTS
CTS
A-MPDU (to MLD1)
BA
A-MPDU (to MLD3)
L1 STA in C-MLD3
L2 STA in C-MLD3
CTS
BA
Backoff
RTS
RTS
CTS
During this duration, the MLD1 should not schedule a frame to MLD2.
Busy

## Slide 10: Conclusion
Internal interface among the STAs within the constrained MLD can be implementation specific.
Since the normative behavior of a peer STA in a constrained MLD is not described in much detail in the spec, it can cause the compatibility issue between each different vendors.
  Also, it is very hard to describe all possible issues and scenarios.
Under such limit, the most appropriate solution to protect frame exchange on different links is using the RTS/MU-RTS and CTS procedure in the constrained multi-link operation.

## Slide 11: Straw Poll 1
Do you support the following constrained multi-link operation?
  When a STA in a non-STR MLD receives an RTS addressed to itself, if the NAV of the STA indicates idle but another STA in the same MLD is either a TXOP holder or a TXOP responder, the STA may not respond with a CTS frame.

## Slide 12: Straw Poll 2
Do you support the following constrained multi-link operation?
  When a STA within a constrained MLD responds with the CTS frame to the received RTS/MU-RTS frame, other STAs within the constrained MLD should not access a channel during the time indicated by the Duration information in the received RTS/MU-RTS frame.

## Slide 13: Straw Poll 3
Do you support the following constrained multi-link operation?
  When a STA within a MLD responds with the CTS frame to the RTS/MU-RTS frame received from a peer STA within another constrained MLD, other STAs in the MLD should not send a frame to any STA within the constrained MLD during the time indicated by the Duration field in the received RTS/MU-RTS frame.