## Slide 1: Phase Rotations Design for EHT
Date: 2019-xx-xx
Authors:
Name | Affiliations | Address | Phone | email
Dandan Liang | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | Dandan.liang@Huawei.com
Ming Gan |  |  |  | 
Jian Yu |  |  |  | 

## Slide 2: Abstract
Lower PAPR of symbols is required in 802.11n/ac/ax because of lower PA backoff as well as lower dynamic range in digital domain algorithms.
In 802.11n/ac/ax, phase rotations of various degrees were applied in various bandwidth for reducing the PAPR [1].
In this contribution, we propose phase rotations for 320MHz and 240MHz.

## Slide 3: Introduction
In 11n, the phase rotations are:
0
-64
63
is (L-STF, L-LTF, L-SIG, etc) subcarrier symbol vector for the XMHz packet

## Slide 4: Introduction
In 11ac/ax, the phase rotations are:
0
-64
64
-128
127
For a non-contiguous 80+80 MHz packet transmission, each 80 MHz frequency segment uses the phase rotation for the 80 MHz packet transmission.

## Slide 5: Introduction
320MHz is one of main features in EHT, 240MHz is also one potential bandwidth in EHT [2].
Phase Rotations design shall be considered for 320MHz and 240MHz.
Following 11ax phase rotations design guidelines, 11be phase rotations design does not consider preamble puncturing cases as well.
Design considerations of 11be phase rotation:
  Bandwidth candidates: 320MHz, 240MHz
  Phase rotations candidate values: [1 -1 j -j]
  Metric: Low PAPR [3]
  Maintain compatibility with 80 (160) MHz legacy devices
  w/o CP

## Slide 6: Phase Rotations (320MHz)
Phase Rotations for 320MHz
Method 1: Design phase rotations by [PR80 C1PR80 C2PR80 C3PR80], where PR80=[1 -1 -1 -1] and the candidate value of phase rotations Ci belongs to [1 -1 j -j], i=1,2,3.
Method 2: Design phase rotations by [PR80 C1 C2 …C12], where PR80=[1 -1 -1 -1] and the candidate value of phase rotations Ci belongs to [1 -1 j -j]. Considering a phase factor is applied to each 20MHz segment of subcarriers, so here i=1,2,…12.
Method 3: Design phase rotations by [1 C1 C2 …C15], where Ci belongs to [1 -1 j -j]

## Slide 7: Phase Rotations (240MHz)
Phase Rotations for 240MHz
Method 1: Design phase rotations by [PR80 C1PR80 C2PR80], where PR80=[1 -1 -1 -1] and the candidate value phase rotations Ci belongs to [1 -1 j -j], i=1,2.
Method 2: Design phase rotations by [PR80 C1 C2 …C8], where PR80=[1 -1 -1 -1] and Ci belongs to [1 -1 j -j]. Considering a phase factor is applied to each 20MHz segment of subcarriers, so here i=1,2,…,8.
Method 3: Design phase rotations by [1 C1 C2 …C11], where Ci belongs to [1 -1 j -j], i=1,2,…,11.

## Slide 8: Conclusions
Phase Rotations are designed for 320MHz and 240MHz.

## Slide 9: References
[1] <Part 11: Wireless LAN Medium Access Control (MAC) and Physical
Layer (PHY) Specifications>, 802.11-2016.
[2] Bin Tian etc, <Further Thoughts on 11be Tone Plan>, IEEE 802.11-19/1521r0
[2] Eunsung Park etc, <Phase Rotation for 320MHz> , IEEE 802.11-19/1493r0