## Slide 1: Ranging Protocol in 11bd
Date: 2019-11-12
      November 2019

## Slide 2: Introduction
In [1] and [2], ranging performance of C2C channel model and free-space LOS path loss model are simulated/analyzed
  Results shows sub-meter accuracy is possible
11bd supports round-trip-time (RTT) ranging for 10 MHz and 20 MHz bandwidth PPDUs
This submission proposes ranging protocol for 11bd
  RTT based
  Reuse 11az ranging protocol
[1] IEEE 802.11-19/0859 Ranging Performance in 11bd
[2] IEEE 802.11-19/0788 Considerations on Ranging in NGV
      November 2019

## Slide 3: 11az Ranging Overview
11az ranging includes three parts:
  Capability discover
    Responder advertise ranging capability in beacon (secured or non-secured, bi-directional measurement report feedback or not, trigger based or non-trigger based)
  Ranging parameter negotiation
    Initiator and responder use FTM request/response to negotiate number of spatial time streams, bandwidth, LTF format and location measurement report (LMR) feedback type, etc.
  Measurement sequence exchange
    Responder and Initiator exchange NDP frames and the location measurement report(LMR) using trigger-based sequence (MU scenario) or non-trigger based sequence (SU scenario)
      November 2019

## Slide 4: Non-trigger Based Ranging Sequence
11az non-trigger based (NTB) measurement sequence with bidirectional LMR is shown below
  Applied to peer-to-peer ranging scenario (initiator and responder)
  The measurement sequence is initiated by initiator STA
  After measurement report exchange, both of initiator and responder obtain range estimation
  LMR feedback type: delayed or immediate
NDPA
Initiator
Responder
SIFS
SIFS
NDP1
NDP2
LMR1
(t2, t3)
SIFS
LMR2
(t1, t4)
SIFS
      November 2019

## Slide 5: RTT Calculation
Time stamps of NDP1 and NDP2
After Initiator/Responder receiving LMR1/LMR2, RTT is derived as
RTT = t4 – t1 – (t3 – t2)
Range is calculated as
R = RTT*c/2, where c is the light speed
Responder
Initiator
NDP1
NDP2
t1 (ToD)
t2 (ToA)
t3 (ToD)
t4 (ToA)
NDPA
LMR1 (t2, t3)
LMR2 (t1, t4)
      November 2019

## Slide 6: Ranging in 11bd (1)
11az ranging protocol can be maximally reused for 11bd
  Implementation simplicity
  11bd device operates in OCB mode
  Needs new capability discovery and ranging parameter negotiation
For measurement sequence exchange, 11az NTB measurement sequence can be directly used for peer-to-peer ranging between two 11bd devices
      November 2019

## Slide 7: Ranging in 11bd (2)
Capability discovery: a broadcast ranging advertisement frame can be used
  Sent periodically by 11bd ranging device A
  Carries the ranging parameters supported/required by this device, e.g. bandwidth, number of spatial streams, LMR feedback type, etc.
Ranging parameter negotiation: 11bd device B can decode the ranging advertisement frame from device A to learn the device’s capability and requirement
  If device B consents with the device A’s capability/requirement, device B sends NDPA frame to initiate NTB ranging
NDPA
11bd device B
11bd device A
SIFS
SIFS
NDP1
NDP2
LMR1
(t2, t3)
SIFS
LMR2
(t1, t4)
SIFS
Ranging
Advertisement
      November 2019

## Slide 8: Ranging Error of Moving Vehicle
Length of NGV Preamble is 88us
  L-STF + L-LTF + L-SIG + RL-SIG + NGV-SIG + RNGV-SIG + NGV-STF + 2*NGV-LTF
MAC payload of NDPA and LMR frames are around 25 bytes and 50 bytes, respectively
  Assume 20MHz band and MCS0, the length of NDPA and LMR frames are 120us and 152us
The length of measurement sequence is
  152+88+88+120+120+16*4=632us
Assume the vehicle velocity is 50m/s (180km/h)
  Within the range measurement sequence, the vehicle moves 3cm
      November 2019

## Slide 9: Conclusions
RTT-based ranging protocol is proposed for 11bd
  Enable 11bd devices to implement peer-to-peer ranging
The ranging protocol includes two parts
  Ranging advertisement
  Ranging measurement exchange sequence
  11az ranging measurement exchange sequence is reused for implementation simplicity
      November 2019

## Slide 10: Reference
[1] IEEE 802.11-19/0859 Ranging Performance in 11bd
[2] IEEE 802.11-19/0788 Considerations on Ranging in NGV
      November 2019