## Slide 1: Link Adaptation Improvement
Date: 2020-01-09
Authors:

## Slide 2: Introduction
From IEEE 802.11a to 11ax, we have MCS levels based on code rates 1/2, 2/3, 3/4, and 5/6 where we have well known puncturing pattern for convolutional code
We also have LDPC H matrices based on these code rates
Due to these limited number of code rates, there are some cases where we observed big gap between two MCS levels
In this contribution, we showed how to improve RvR (Rate vs. Range) by adding few more MCS levels for LDPC without adding new H matrix

## Slide 3: Current MCS levels
Due to limited code rates, there are some MCS levels have big gap
  For example, gap between MCS0 and 1 is 3.0dB while gap between MCS5 and 6 is 1.3dB
Less gap results in better spectral efficiency with proper link adaptation
  For example, if SNR of link is 12dB, then link adaptation algorithm will stay at MCS4 and once in a while goes to MCS5 to check whether it can support it. In this case, MCS5 will fail 100%.
If there is an intermediate MCS level between them, then there is chance to have better throughput
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Spectral Efficiency | 0.5 | 1 | 1.5 | 2 | 3 | 4 | 4.5 | 5 | 6 | 6.7 | 7.5 | 8.3
Required SNR* | -1.3 | 1.7 | 4.6 | 7.2 | 11.1 | 15.2 | 16.5 | 17.9 | 21.7 | 23.3 | 26.9 | 28.8
Gap |  | 3.0 | 2.9 | 2.6 | 3.9 | 4.1 | 1.3 | 1.4 | 3.9 | 1.6 | 3.6 | 1.8
* Required SNR is based on 10% PER of 1458B LDPC

## Slide 4: Proposal: more MCS levels
In order to mitigate this problem or improve performance, we propose to have more MCS levels where there is big gap
Note that we try to use existing code rate as much as possible and also try to avoid extremely high code rate as it may cause more errors in frequency selective channel
MCS | Spectral Efficiency | Modulation | R (Coding Rate)
0 | 0.5000 | BPSK | 1/2
MCS0-1 | 0.6667 | BPSK | 2/3
1 | 1.0000 | QPSK | 1/2
MCS1-2 | 1.3333 | QPSK | 2/3
2 | 1.5000 | QPSK | 3/4
MCS2-3 | 1.6667 | QPSK | 5/6
3 | 2.0000 | 16-QAM | 1/2
MCS3-4 | 2.6667 | 16-QAM | 2/3
4 | 3.0000 | 16-QAM | 3/4
MCS4-5 | 3.5000 | 64-QAM | 7/12
5 | 4.0000 | 64-QAM | 2/3
6 | 4.5000 | 64-QAM | 3/4
7 | 5.0000 | 64-QAM | 5/6
MCS7-8 | 5.3333 | 256-QAM | 2/3
8 | 6.0000 | 256-QAM | 3/4
9 | 6.6667 | 256-QAM | 5/6
MCS9-10 | 7.0000 | 1024-QAM | 7/10
10 | 7.5000 | 1024-QAM | 3/4
11 | 8.3333 | 1024-QAM | 5/6

## Slide 5: New Code Rate
In the proposal, we have additional code rate of 7/12 and 7/10
In order not to have more H matrix, we propose to use puncturing to make these code rate
  7/12 code rate is punctured from 1/2 code
  7/10 code rate is punctured from 2/3 code
Overall procedure is same as IEEE 802.11n LDPC mechanism, but we want to modify puncturing pattern
  Current puncturing mechanism is not designed to have new code rate
Update puncturing pattern to improve performance

## Slide 6: Performance Results

## Slide 7: LDPC Extra Symbol Segment for New MCS level
Need to relax LDPC extra symbol segment condition
Below figure is smallest puncturing case vs. largest without LDPC extra symbol segment
Largest puncturing gives only 0.4dB performance degradation with optimized puncturing pattern

## Slide 8: Straw Poll #1
Do you support to have more MCS levels between MCS0 – MCS11 for LDPC in 11be?

## Slide 9: Straw Poll #2
Do you support to have following MCS levels for LDPC in 11be?
  Note: MCS for 4096QAM is TBD
MCS | Spectral Efficiency | Modulation | R (Coding Rate)
0 | 0.5000 | BPSK | 1/2
1 | 0.6667 | BPSK | 2/3
2 | 1.0000 | QPSK | 1/2
3 | 1.3333 | QPSK | 2/3
4 | 1.5000 | QPSK | 3/4
5 | 1.6667 | QPSK | 5/6
6 | 2.0000 | 16-QAM | 1/2
7 | 2.6667 | 16-QAM | 2/3
8 | 3.0000 | 16-QAM | 3/4
9 | 3.5000 | 64-QAM | 7/12
10 | 4.0000 | 64-QAM | 2/3
11 | 4.5000 | 64-QAM | 3/4
12 | 5.0000 | 64-QAM | 5/6
13 | 5.3333 | 256-QAM | 2/3
14 | 6.0000 | 256-QAM | 3/4
15 | 6.6667 | 256-QAM | 5/6
16 | 7.0000 | 1024-QAM | 7/10
17 | 7.5000 | 1024-QAM | 3/4
18 | 8.3333 | 1024-QAM | 5/6

## Slide 10: Straw Poll #3
Do you support the new MCS levels between MCS0 – MCS11 for LDPC in 11be are based on puncturing of MCS0-MCS11?

## Slide 11: Straw Poll #4
Do you support to relax LDPC Extra Symbol Segment conditions for the new MCS levels between MCS0 – MCS11 for LDPC in 11be?

## Slide 12: Appendix- non ideal link adaptation
Non ideal link adaptation case
Assume U[-3,3] SNR error at receiver side

## Slide 13: Appendix- with different new MCS levels
Proposal is in slide 4.
Proposal with 16QAM 5/6 is same as proposal except replacing 64QAM 7/12 with 16QAM 5/6.
Proposal with 16QAM 5/6, without 1024QAM 7/10 is same as proposal except replacing 64QAM 7/12 with 16QAM 5/6 and without 1024QAM 7/10.