## Slide 1: Considerations of FCC NRPM on 11bd
Date: 2020-1-12
Authors:
Onn Haran, Autotalks

## Slide 2: Enabling WiFi in U-NII-4 is FCC’s Prime Target
  FCC plans to allocate lower 45MHz to unlicensed WiFi
  No protection of ITS services
  FCC doesn’t plan to conclude WiFi sharing study
  Dedicated V2X Spectrum will be squeezed to 30MHz
  No room for future V2X services, needed for safety enhancement: Cooperative perception (sensor sharing) / Pedestrian / Platooning bandwidth needs cannot be ignored
Automotive industry consensually asks to maintain 75MHz for V2X

## Slide 3: Proposal: Study V2X Sharing in U-NII-4
  75MHz can be used by V2X only with sharing
  V2X, like any other service, can use the unlicensed band without a need for approval
  Stakeholders have conflicting aspirations
  FCC: Fast approval of exclusive WiFi usage
  Automotive: Protected V2X operation
  802.11bd PAR: 2x throughput requirement using 20MHz
  Other countries (Japan / EU) aren’t impacted
  Proposal: 802.11bd shall develop and validate a sharing scheme
  Serving the industry by solving the bottleneck
167
175

## Slide 4: Proposal: Sharing Should Use 20MHz V2X Channels Without Considering Legacy 10MHz V2X Channels
  10MHz channel is the obstacle for sharing
  The likelihood of 10MHz ch. in U-NII-4 is very low
  Sharing 20MHz channels is simple
  Proposal: Sharing should be based on 20MHz channel
  Proposal: 802.11bd shall redefine 20MHz operation
  Header: plain 11a header (no duplicated 10MHz header)
  Mask: no need for 10MHz channel compliant mask
  Channel access: no need to check for 10MHz activity
167
175

## Slide 5: Proposal: Study V2X Prioritization
  Some sort of V2X prioritization is needed for confidently using V2X in U-NII-4
  Option A: Detect-and-Vacate
  WLAN stops using V2X channels for certain period after detecting 11bd header
  Option B: Raising V2X channel access priority
  For example, shorter DIFS or higher CCA for non-V2X
  Option C: Minimizing non-V2X traffic in V2X preferred channels
  For example, 173 / 177 cannot be primary channels
167
175

## Slide 6: Proposal: Define Wide V2X Channels
  A wider V2X channel is better for WiFi
  V2X would send messages in shorter time
    Unlicensed 160MHz channel degrades to 80MHz regardless if V2X uses 20, 40 or 80MHz
  A wider V2X channel serves better V2X
  Higher positioning accuracy
  Simpler management of V2X services (less channels)
  Simpler V2X hardware (less radios)
  Proposal: Define 40/80MHz V2X channels
171
167
175
163

## Slide 7: Straw Poll #1
Do you agree that 802.11bd shall redefine 20MHz channel operation, without co-existence with legacy 10MHz?
Y:
N:
A:
January 2020
Onn Haran, Autotalks

## Slide 8: Straw Poll #2
Do you agree that 802.11bd shall define and validate WiFi sharing scheme?
Y:
N:
A:
January 2020
Onn Haran, Autotalks

## Slide 9: Straw Poll #3
Do you agree that 802.11bd shall define wider channels (40/80MHz)?
Y:
N:
A:
January 2020
Onn Haran, Autotalks