## Slide 1: Discussion on latency metric
Date: 2020-01-13
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Xin Zuo | Tencent |  |  | xinzuo@tencent.com

## Slide 2: Introduction
We have discussed low latency topic in MAC scope
  We haven't made much progress since we're still in the early stages
  Also we have not reached an agreement on how and how much to improve latency
In PAR document, following sentence mentions low latency scope
  “This amendment defines at least one mode of operation capable of improved worst case latency and jitter” (Sub-clause 5.2 Scope of the Project)
We will focus on latency rather than jitter in this submission

## Slide 3: Previous works
Several submissions have addressed latency performance with various metrics
  [1][2] used average latency and frame drop rate as performance metric
  [3] used 95 percentile latency
  [4] used outage ratio
  They all have showed CDF of latency distribution
However, they didn’t use the worst case latency as performance metric
  Ununified metric makes it difficult to compare candidate features
  The direction of technology development may be determined according to the metric to improve

## Slide 4: Low Latency Target
So we need to discuss on target metric for low latency feature
Followings can be considered as low latency metric
  The worst-case latency
  A representative value about latency distribution (i.e. mean value, 95th percentile value)
  Packet loss (i.e. Outage ratio, frame drop rate)

## Slide 5: Worst case latency
Even though we already have dealt with latency topic, we have never discussed exact meaning or definition of worst case latency
  If we have a common agreement on worst case latency, it would be helpful for us to verify the developing feature more easily
  Also we can clearly identify what we need to focus on in order to develop the low latency feature
The exact definition of the worst case latency is hard to find in other IEEE 802 domain, but it is usually considered the largest value in the latency distribution

## Slide 6: Worst case latency in 802.11
Since 802.11 WLAN operates in ISM band, it can be quite challenging work for us to enhance the worst case latency when we adopt the largest value in the latency distribution
  If we adopt the largest value for worst-case latency, we have to take the extreme case into account
  When we consider the extreme case and develop a feature improving worst case latency, it causes degradation of other performance

## Slide 7: A representative value
Since the worst case latency is difficult to consider, we can consider it on behalf of a representative value from the latency distribution
  Mean value
  Xth percentile value (i.e. 95th percentile, X is TBD)
We prefer Xth percentile value rather than mean value, because low latency traffic is deterministic service so it has latency bound

## Slide 8: Packet loss
Packet loss has a great impact on performance in low latency traffic, so it is better to consider the metric as well
Most low latency traffic requires extreme low values in packet loss [5]
  Under 0.1%: Real-time gaming
  Near-lossless: Cloud gaming, Real time video
  Lossless: Robotics and industrial automation
Notes: R

## Slide 9: Summary
We have discussed on target metric for low latency feature
  There are several options for low latency metric and we don’t have agreement on that
We suggest Xth percentile value rather than other metric
  X is 100 when we consider the worst-case latency
  X is 99 or 95 when we exclude extreme case

## Slide 10: Straw poll 1
Which options do you prefer for low latency metric in TGbe?
  Option 1: The worst-case latency (Maximum value)
  Option 2: A representative value about latency distribution (i.e. mean value, 95th percentile value)
  Option 3: Packet loss (i.e. Outage ratio, frame drop rate)

## Slide 11: Straw poll 2
Which value do you prefer for low latency metric in TGbe?
  Option 1: 99.9th percentile value
  Option 2: 99th percentile value
  Option 3: 95th percentile value

## Slide 12: Reference
[1] 11-19-1523-00-00be-performance-evaluation-of-deterministic-service-for-eht
[2] 11-19-1888-01-00be-performance-evaluation-of-deterministic-service-for-eht-follow-up
[3] 11-19-1081-01-00be-multi-link-aggregation-gain-analysis-latency
[4] 11-19-2071-00-00be-performance-evaluation-of-multi-link-channel-access-schemes
[5] 11-18-2009-06-0rta-rta-report-draft

## Slide 13: Worst case latency in TSN
802.1Q (Bridges and Bridged Networks)
  Annex L.3 Determining worst-case latency contribution and buffering requirements
802.1CM: Time-Sensitive Networking for Fronthaul
  7.1 Latency components: Equation for latency
802.1BA: Audio Video Bridging (AVB) Systems
  In Table 6-2, “Max end-to-end latency”
802.1 TSN uses the term “worst case latency’ without technical definition