## Slide 1: MLA: Support for Constrained Devices
Date: 2020-01-10
Authors:

## Slide 2: Terminology
STR (simultaneous Tx and Rx)
  An MLD that is capable of simultaneous Tx/Rx on multiple links even when the links are near band
Non-STR
  An MLD that is not capable of simultaneous Tx/Rx on multiple links when the links are near band (i.e., it can only do Tx/Tx or Rx/Rx on all links)

## Slide 3: Background (1/2)
A non-STR MLD cannot use Async mode so Sync mode is preferred
However, Sync (Tx/Tx) PPDUs transmission requires tight inter-STA co-ordinations within a Tx MLD
  E.g., Tx on one link needs to trigger Tx on the other link within a very short time (e.g., within SIFS) to avoid blocking the EDCA of the other link

## Slide 4: Background (2/2)
For a link to obtain full benefits of MLA in both directions, both peer MLDs of the link should be able to Tx Sync PPDUs
  However, there are cases where one of the peer MLDs may not support tight inter-STA co-ordinations
Is Sync PPDUs currently possible in BOTH directions?
 | AP (tight co-ord.) | AP (not tight co-ord)
STA (tight co-ord.) | Yes (case 1) | No (case 2)
STA (not tight co-ord.) | No (case 3) | No (case 4)

## Slide 5: Proposal
To enable case 2 and case 3, we propose to use ML-RTS to allow Sync PPDUs for cases where at least one of the MLDs is capable of tight inter-STA co-ordinations
  Use ML-RTS to trigger responses from both receiving STAs of the peer MLD before transmitter the Sync PPDUs

## Slide 6: An Example (Case 2)
TXOP owner AP sends a an ML-RTS
Both STAs responses by a n ML-CTS (if NAV/CCA checks allow)

## Slide 7: An Example - Cont’d
What if STA2 sent ML-CTS but AP2 detects the medium is busy locally?
  AP2 will not transmit the Sync’ PPDU on link 2
  Receivers of the ML-CTS can use the RTS rules (as if it receives an RTS) to set the NAV so the NAV gets reset if no transmission occurs on link 2 after the ML-CTS (so the medium on link 2 could be used by other STAs)
  The legacy STAs NAV will still be blocked by the ML-CTS though
Alternatively, instead of using ML-CTS, AP1 sends an RTS Poll and the STAs send a regular RTS on each link (with the Duration set to protect the Sync’ PPDU + BA)

## Slide 8: Analysis of Constrained Scenarios
STR = Simultaneous Transmission and Reception capable
 | STR AP | Non-STR AP
STR STA | Not covered (assume Async mode is used) | Not covered (not likely in practice)
Non-STR STA | See slide here | See slide here

## Slide 9: STR AP + Non-STR STA
STA/AP gets access to L1 | UL | DL
L2 is IDLE and PIFS access is allowed on L2 | L1+ L2: Sync’ PPDU (assume tight coupling at STA) | L1+L2 : Sync’ PPDU Use ML-RTS/CTS when AP is loose-coupled
L2 is IDLE and PIFS access not allowed | L1: S1 sends PPDU1 to A1 L2: can be used for UL/DL for Sy. No constraints S2 cannot use until PPDU1-end-time UL: blocked due to CCA DL: AP may send ML-RTS, but doesn’t get response from STA | L1: A1 sends PPDU1 to S1 L2: can be used for one of these: UL/DL for Sy. No constraints A2 sends DL for S2, with end-time same as PPDU1. A2 sends ML-RTS to S2 S2 sends ML-CTS with PPDU1end-time S2 will not use L2 for UL
L2 is BUSY@PPDU1 start, but later became IDLE during PPDU1 |  | 
Multiple Primary channels allowed

## Slide 10: Non-STR AP + Non-STR STA
STA/AP gets access to L1 | UL | DL
L2 is IDLE and PIFS access is allowed on L2 | L1+ L2: Sync’ PPDU (assume tight coupling at STA) | L1+L2 : Sync’ PPDU Use ML RTS/CTS when AP is loose-coupling
L2 is IDLE and PIFS access not allowed | L2 not usable | L2 not usable
L2 is BUSY@PPDU1 start, but later became IDLE during PPDU1 |  | 
Only Single Primary channel
  Pre-11be STAs operate only on this channel
  All EDCA access happens only on this channel (including 11be STAs)