## Slide 1: Coordinated Spatial Reuse Operation
Date: 2019-12-31
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 

## Slide 2: Introduction
Coordinated Spatial Reuse (co-SR) has been proposed since the EHT study group [1], and has shown performance gain in different scenarios [2-3].
Co-SR is a natural extension of the spatial reuse (SR) scheme under the multi-AP operation framework, the general idea is joint power control and link adaptation of multiple APs, and can be implemented with relatively low complexity.
In this contribution, we discuss the basic operation of co-SR, including the following aspects:
  Architecture
  Preparation Stage
  Data transmission procedure
  Control information between APs

## Slide 3: Recap
As defined in 802.11ax, the Spatial Reuse scheme is an old way of doing multi-AP operation
The current SR scheme is still a distributed channel access scheme:
  If the SR transmission happens in the preferred spatial reuse area, then the overall performance may be good
  If the SR transmission happens in the non- preferred spatial reuse area, then the ongoing transmission will be impacted greatly
Non-Preferred spatial reuse area
Preferred spatial reuse area
-72dBm
On going Transmission
With co-SR, the APs can make sure that the secondary transmissions will not happen in the non-preferred spatial reuse area, hence the overall performance can be guaranteed.
-82dBm

## Slide 4: Architecture
The basic operation of co-SR is that, one AP can trigger one or more other APs to perform transmission with it together, with appropriate power control.
To simplify terminology, we call the AP that initiates the co-SR transmission as coordinator AP, and call the other APs as coordinated APs.
Regarding the role of coordinator and coordinated APs, there are two possible options:
  Option 1: Static role. The role of each AP is pre-defined, some APs are always coordinator APs, and some APs are always coordinated APs.
  Option 2: Dynamic role. The role of each AP can be dynamic, any AP that wins the channel can be a coordinator AP, and any AP that is willing to be triggered by the coordinator AP can be a coordinated AP.
We prefer option 2 due to the following reason:
  The co-SR transmission is only beneficial to coordinated APs, and will bring some performance loss to the coordinator AP for one transmission, so it is unfair to make one AP to be the coordinator AP all the time. All APs should take turns to sacrifice and benefit, making the performance balanced for each AP.

## Slide 5: Preparation Stage
Before the co-SR transmission, the coordinator AP should be aware of the following information to make the co-SR work efficiently
Cooperation group setup
  The coordinator AP only knows which AP can be triggered after the setup of the cooperation group.
Buffer status of other APs
  Only the APs with buffer to transmit should be selected as coordinated AP
Channel status of other APs
  Only the APs with idle channel can participate in the co-SR transmission
Mutual interference level between different APs
  MCS and Transmit power should be carefully chosen based on the mutual interference between different APs
  STAs can measure their neighboring APs, and report their neighboring AP list together with the RSSI of each AP to assist its own AP to estimate the mutual interference level between different APs.

## Slide 6: Transmission Procedure
After successfully contending the channel, the coordinator AP can initiate the co-SR transmission by sending a co-SR Trigger frame.
The coordinator AP and the coordinated APs use the same channel for data transmission at the same time.
Co-SR Trigger Frame
AP1
(Coordinator AP)
DL Data Frame (or basic TF)
DL Data Frame (or basic TF)
BA (or UL Data Frame)
BA (or UL Data Frame)
AP2
(Coordinated AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
(BA)
(BA)

## Slide 7: Co-SR Trigger Frame
The co-SR Trigger frame shall carry necessary control information for the coordinated APs to decide their transmission parameters.
The control information should include:
  Coordinated AP’s identifier
  The PPDU length of the co-SR data transmission, so that all AP’s transmission can be aligned.
    In the UL case, the length of the basic TF should also be included
  The maximum TX power of the coordinated APs, so that the interference from the coordinated APs can be upper bounded
  The TX power of the coordinator AP, so that the coordinated AP can choose suitable MCS for the scheduled STAs
  Acceptable interference level, so that the mutual interference of UL data or BA frame can be controlled
  UL/DL flag
  etc.

## Slide 8: Co-SR transmission example (1/3)
Step 1: AP1 has DL data to transmit to STA1, so it starts the channel access procedure.
Step 2: AP1 successfully contends the channel, and it finds that there’s another AP, i.e., AP2, which satisfies the following conditions
  AP2 is in AP1’s cooperation group
  AP2 also has DL data to transmit
  The interference from AP2 to STA1 is not strong
Step 1: pending DL data
AP1
STA1
AP2
Step 2: AP1 finds AP2 satisfying the pre-defined conditions

## Slide 9: Co-SR transmission example (2/3)
Step 3: AP1 sends a co-SR Trigger frame to AP2, indicating DL co-SR transmission, carrying the PPDU length, and the max TX power of AP2
AP1
STA1
AP2
Step 3: co-SR Trigger Frame
indicating DL co-SR transmission, carrying the PPDU length, and the max TX power of AP2

## Slide 10: Co-SR transmission example (3/3)
Step 4: after receiving the co-SR Trigger frame, AP2 performs the following
  Check whether the channel is idle
  Determine STA2 (one or more) which has DL data to receive, and does not suffer strong interference from AP1
  Determine the MCS, NSS and other TX parameters of the DL frame based on the max TX power
  Performs A-MPDU aggregation according to the PPDU length of the DL data frame
Step 5: concurrent data transmission of AP1 and AP2
AP1
STA1
AP2
Step 4: Scheduling, choose STA2, determine TX parameters, construct A-MPDU
STA2
Step 5: Data transmission
Step 5: Data transmission

## Slide 11: Conclusion
  We propose the basic operation of coordinated spatial reuse, which allows multiple APs to transmit concurrently using the same channels.
  Co-SR Trigger frame is used to initiate the co-SR transmission, and carries necessary information for the coordinated APs to decide their transmission parameters

## Slide 12: Straw Poll
  Do you support to introduce a coordinated spatial reuse operation in TGbe?
    A coordinator AP that obtains a TXOP may grant one or more coordinated APs to use the same bandwidth under the control of the coordinator AP

## Slide 13: References
  [1] 11-19-0103-01-0eht-ap-coordination-in-eht
  [2] 11-19-0801-00-00be-ap-coordination-in-eht
  [3] 11-19-1534-01-00be-coordinated-spatial-reuse-performance-analysis