## Slide 1: Discussion on Expansion of Multi-Link Aggregation to Multi-AP
Date: 2020-1-8
Authors:
Name | Affiliations | Address | Phone | Email
Yoshihisa Kondo | ATR |  |  | kondo@atr.jp
Hiroyuki Yokoyama | ATR |  |  | 
Michio Miyamoto | ATR |  |  | 
Ayano Onishi | ATR |  |  | 
Toru Osuga | NICT |  |  | 
Taketoshi Nakajima | NICT |  |  | 
Fumiko Ohori | NICT |  |  | 
Satoko Itaya | NICT |  |  | 
Fumihide Kojima | NICT |  |  | 

## Slide 2: Background
Multi-band/Multi-Channel operation (Multi-Link aggregation)
  There are many proposals
    Framework discussions: [1], [2], …
    Transmission schemes: [3], [4], …
Multi-AP operation
  There are many proposals, but most of them are for PHY resource coordination
RTA [5] is also discussed in TGbe
In this presentation, we are going to discuss the following:
  Multi-Link aggregation for real-time applications
  Expansion of Multi-Link to Multi-AP for more stability
  Difference between Single-AP Multi-Link and Multi-AP Multi-Link
  STA driven transmission control for Multi-Link Multi-AP

## Slide 3: Discussion on Multi-Link for real-time applications
“Link capacity” fluctuates largely
  Frequency related factors: interference, noise
  Position related factors: pathloss, shadowing, multipath
Traffic pattern is not uniform but rather “burst” in many cases
  E.g., real-time video streaming
    Generally, video encoding operation is done at constant intervals: 16.7 ms, for an example
    Large number of packets are generated at the same time and arrived at an AP (transmitter) in a short time
    All packets of a group is needed for decoding the video frame
Latency becomes large if the bunch of packets are arrived at an AP (transmitter) when link capacity is low
Link capacity
Time
Traffic arrival rate
Time
Time
Latency
Transmission duration
16.7ms

## Slide 4: Discussion on Multi-Link for real-time applications (Cont.)
For low latency, it is important to maintain enough link capacity over time
Multi-Link is an effective approach for it
  Link capacity becomes “double”
  Frequency related factors and part of position related factors are mitigated
However, it seems that efficient use of Multi-Link total capacity has not been discussed enough
Link capacity
Time
Total link capacity

## Slide 5: Discussion on Multi-AP Expansion
To maintain enough total link capacity, position related factors should be considered
  Pathloss highly depends on a relative position between an AP and a STA
  Spatial diversity gain of the Multi-Link with single-AP system is limited
Multi-AP is an effective approach to mitigate the deterioration derived from positional relation
  When signal level of a link becomes lower, another link with another AP on a different position can cover it
Expansion of Multi-Link to Multi-AP (link level Multi-AP) should be discussed to maintain total link capacity efficiently
  Multi-AP system has been discussed in TGbe, but most of proposals are about PHY resource coordination
AP
STA
AP
AP
STA
Single-AP
Multi-AP

## Slide 6: Difference between Single-AP Multi-Link and Multi-AP Multi-Link
Single-AP Multi-Link
PHY-MAC entities are on the same AP device
MAC entities of each device can be coordinated directly
Multi-AP Multi-Link
PHY-MAC entities are on different AP devices
MAC entities of APs cannot be coordinated directly
  Supports of services in external network are needed
  Only MAC entities of STA can be coordinated directly
PHY
MAC
PHY
MAC
MLM
PHY
MAC
PHY
MAC
MLM
AP device
STA device
PHY
MAC
PHY
MAC
PHY
MAC
PHY
MAC
MLM
AP device
STA device
AP device
(External service)
MLM: Multi-Link Management
Datapath

## Slide 7: STA Driven Transmission Control for Multi-AP Multi-Link
For downlink transmission, STA needs to drive transmission of APs since MAC entities of APs cannot be coordinated directly
For efficient use of multi-link capacity, duplicated transmission between links must be reduced
Downlink transmission
(External coordination service configures multi-link session)
External allocation service allocates traffic to APs
  Large number of packets are arrived in a short time
Each AP transmits frames so that the transmission frames may not be duplicated
  Details to be presented in next contribution
MAC entities of STA share context of received frames
STA sends the context to APs using Ack(BA)
Each MAC of AP controls transmission frames and queue according to the context
  MAC deletes frames which have been received by STA via another link
PHY
PHY
BA:1,2,3,4
1
2
AP1
3
4
BA:1,2,3,4
STA
PHY
PHY
Reorder
MAC
MAC
Rx Context
AP2
MAC
MAC
Allocation
1
2
3
4
1
2
3
4
Coordination

## Slide 8: Summary
Multi-Link aggregation is potentially capable of realizing stable real-time applications
To maintain total link capacity over time and efficient use of the total link capacity are important
Expansion of Multi-Link to Multi-AP is effective to maintain enough total link capacity
In Multi-AP Multi-Link, STA needs to drive transmission of APs since MAC entity of each AP cannot be coordinated directly
For efficient use of the total link capacity, duplicated transmission must be avoided
  Shared feedback from STA enables APs to reduce duplicated transmission
  More details will be proposed in the next contribution

## Slide 9: References
  [1] 802.11-19/760r1 Multi-Band Opinion
  [2] 802.11-19/773r7 Multi-link Operation Framework
  [3] 802.11-19/1101r1 Conditional Packet Duplication in Multiple Link System
  [4] 802.11-19/1144r4 Channel Access for Multi-link Operation
  [5] 802.11-18/2009r6 RTA report draft