## Slide 1: Power saving considering non-AP MLD without STR capability
Date: 2020-01-13
Authors:
Name | Affiliations | Address | Email
Namyeong Kim | LG Electronics | LG Seocho R&D Campus, Korea | namyeong.kim@lge.com
Insun Jang |  |  | insun.jang@lge.com
Jeongki Kim |  |  | jeongki.kim@lge.com
Sungjin Park |  |  | allean.park@lge.com
Taewon Song |  |  | taewon.song@lge.com
Jinsoo Choi |  |  | js.choi@lge.com

## Slide 2: Overview
We agreed that 802.11be shall allow a MLD that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links [1]
In terms of power management, we can consider the above mentioned constraints of operation over a pair of links to save power consumption of non-AP MLD
  Note that we consider only the case where AP MLD has STR capability but other cases will be discussed in the next phase
Therefore, we propose the power saving mechanism considering the constraints of MLD that doesn’t support simultaneous TX/RX (STR) capability on a pair of links in 11be
  In this contribution, we will refer to the proposing power saving mechanism as ‘non-STR PSM(Power saving mechanism)’ to explain simply.

## Slide 3: Motivation (1/2)
Non-STR non-AP MLD should consider the interference issue when it receives or transmits frames to avoid data conflict
  By this constraints, there may be a period where a STA of non-STR non-AP MLD does not receive or transmit frames when another STA of the same non-AP MLD transmits or receives frames

## Slide 4: Motivation (2/2)
Non-STR non-AP MLD should consider the interference issue generated by itself when it transmits frames
  By this constraints, there may be a period where the CS result of a STA of the non-STR non-AP MLD which does not transmit frames is 'busy' when another STA of the same non-STR MLD transmits frames.

## Slide 5: Proposal 1: non-STR PSM for UL data TX
While a STA of non-STR non-AP MLD transmits the UL frames, if another STA of the same non-AP MLD does not transmit UL data, the another STA may enter doze state until end of the UL TX (e.g., UL PPDU duration or UL TXOP)
  The STA that has entered doze state will awake after end of UL TX (e.g., UL PPDU duration or UL TXOP)
  However, the STA can awake before the end of UL TX in some cases
    If the STA has the UL frame, the STA can awake by itself to send the data
    The STA may awake by TXOP early termination such as TXOP truncation (See appendix#1 for example)

## Slide 6: Example: Power saving considering UL TX
When only STA 1 transmits UL frames to AP 1 over Link 1, a STA 2 enters doze state until end of the UL PPDU duration or UL TXOP to save power
  During BAs RXs period, the STA 2 may perform CCA for UL data but the STA 2 should not transmit the UL data during BAs RXs period to avoid data conflict
    Note: the STA 2 can receive DL data during BAs RXs period. However, it may be more efficient in terms of power saving for the STA 2 to maintain doze state until UL TXOP
  If the STA prefers to save more power, the STA can choose the power saving mechanism based on TXOP period instead of PPDU duration.

## Slide 7: Proposal 2: non-STR PSM for DL data RX
While a STA of a non-STR non-AP MLD receives the DL frames, if another STA of the same non-AP MLD does not receive DL frames, the another STA may enter doze state until end of DL RX (e.g., DL PPDU duration or DL TXOP)
  The STA that has entered doze state will awake after end of DL RX (e.g., DL PPDU duration or DL TXOP)
  However, the STA can awake before the end of the DL RX in some cases
    If DL data is generated for the STA that has entered doze state, the AP may awake it by transmitting a signal over other link in awake state
    The STA may awake by TXOP early termination such as TXOP truncation (See appendix#2 for example)

## Slide 8: Example: Power saving considering DL RX (1/2)
When only STA 1 receives DL frame from AP 1 over Link 1, a STA 2 enters doze state until end of the DL PPDU duration or DL TXOP of AP 1 to save power
  During BAs TXs period, the STA 2 may perform CCA but the CS result will be busy by self-interference of STA1. Therefore, it will be more efficient to maintain doze state during DL TXOP of AP 1 for more power saving
  If the STA prefers to save more power, the STA can choose the power saving mechanism based on TXOP period instead of PPDU duration.
CS result will be busy due to BA TXs by STA1

## Slide 9: Example: Power saving considering DL RX (2/2)
When the AP 1 obtains TXOP for STA 1, AP 1 transmits DL frames including indication for no traffic of STA 2.
  On receiving the indication for no traffic, the STA 2 enters doze state until end of TXOP for AP 1
Optionally, if AP 2 has buffered DL data for STA 2 after the STA 2 had entered doze state, the AP MLD can send a signal for awake over Link 1
  The signal may indicate the buffered traffic for STA 2
  On receiving the signal, STA 2 awakes and will transmit QoS null frame to AP 2
    Note: the QoS null frame may be skipped

## Slide 10: Signaling for non-STR PSM capability
A non-AP MLD can announce the capability of whether the STA supports the non-STR PSM.
  During initial multi-link setup, an AP MLD and a non-AP MLD can negotiate with each other to enable the non-STR PSM.
    After multi-link setup completion, the non-STR PSM is activated on the STA.
The example of operation of MLD which enables Non-STR PSM.
  When an AP of AP MLD transmits DL frames to a STA of non-STR non-AP MLD, it carries an indication of buffered data for transmission on another STAs of the same non-AP MLD.
    In SFD [1]: An AP of an AP MLD may transmit on a link a frame that carries an indication of buffered data for transmission on other enabled link(s)
  On receiving the no buffered data indication, the STA may enter doze state.
  Then, the AP does not transmit DL frames to the STA until the STA awakes even if the data for the STA is generated
    Optionally, the AP can awake the STA that has entered doze state using the awake signaling

## Slide 11: Summary
The proposed non-STR PSM (non-STR Power Saving Mechanism) is a power saving mechanism that can be considered by a non-STR non-AP MLD that requires more power saving.
The objective of the non-STR PSM is to save more power of the non-AP MLD by entering the doze state for a period in which data cannot be transmitted or data reception probability is low due to constraints of non-STR capability.

## Slide 12: Q&A
Throughput loss in DL case
  Members were concerned that throughput loss about entering doze state during DL TXOP despite STA being able to receive DL frames.
How to handle in Urgent case
  Members questioned how to handle a urgent data to be transmitted to the STA who entered doze during DL TXOP duration.
Operating based on the implementation of non-AP MLD in UL case
  Members questioned that the non-STR PSM for UL TX could be implemented without defining a separate mechanism.

## Slide 13: Q1: Throughput Loss (1/2)
When a non-STR non-AP MLD receives DL frames from an associated AP MLD over one link, the following 3 cases may occur for another link.
  Case 1: a case in which DL frames are transmitted over the another link for all DL RX durations of the obtained DL TXOP.
  Case 2: a case in which DL frames are transmitted over the another link for some DL RX durations of the obtained DL TXOP.
  Case 3: a case in which DL frames are not transmitted over the another link for any DL RX durations of the obtained DL TXOP.
<Case 1>
<Case 2>
<Case 3>

## Slide 14: Q1: Throughput Loss (2/2)
If STA 2 enters doze during DL TXOP by the non-STR PSM, the benefits of a non-STR non-AP MLD may be different depending on the cases.
Therefore, if a non-AP MLD prefers to save more power than throughput gain (e.g. low battery case), the non-AP MLD can activate the non-STR PSM for power saving.
<Case 1>
<Case 2>
<Case 3>
Since STA 2 is in a doze state,
throughput loss may occur.
Since there is no data to receive,
it is beneficial for the STA 2 to enter the doze.

## Slide 15: Q2: How to handle urgent case?
An AP of AP MLD can send a traffic indication to awake the STA that had entered doze state.
  After receiving the traffic indicator for itself, the STA may wake up and receive a DL frame.
  The use of traffic indicator in the non-STR PSM can handle urgent case.

## Slide 16: Q3: Operating based on the implementation of non-AP MLD?
In UL case, if a STA on non-AP MLD enters the doze state without any this notification, DL data loss may occur on the link.
  For example, because AP2 does not know that STA2 had entered doze state, AP2 can send a frame to STA2 during BA durations.
To avoid this issue, AP should know whether the STA will enter the doze state in this case or not
Therefore, STA MLD should inform AP MLD of whether the STA MLD operates the non-STR PSM before operating the PS mode
  The signaling is TBD (e.g., capability indication, A-Control field)

## Slide 17: Conclusion
11be needs to provide the mechanism that a non-STR non-AP MLD can save its more power rather than high throughput when the MLD is in the lower battery case.
  The non-AP MLD can enter doze state for a period in which data cannot be transmitted or data reception probability is low due to constraints of non-STR capability.
  We can call this as non-STR Power Saving Mechanism (non-STR PSM)
In this case, the non-AP MLD should inform AP MLD of whether the non-AP MLD operates the non-STR PSM before operating the PS mode
  The signaling is TBD (e.g., capability indication, A-Control field)

## Slide 18: Reference
[1] 11-19-1262-06-00be-specification-framework-for-tgbe

## Slide 19: SP #1
Do you support that 802.11be allows the following operation for power saving:
  While a STA of a non-STR non-AP MLD transmits the UL frames, if another STA of the same non-AP MLD does not transmit UL data, the another STA may enter doze state until end of the UL TXOP of the STA transmitting the UL frames.
    The signaling for enabling this operation is TBD.

## Slide 20: SP #2
Do you support that 802.11be allows the following operation for power saving:
  When a STA of non-STR non-AP MLD receives DL frames intended to itself from a peer AP, if another STA of same non-AP MLD does not receive DL frame intended to itself, the another STA may enter doze state until end of DL TXOP of the peer AP transmitting the DL frames.
    The signaling for enabling this operation is TBD.

## Slide 21: SP #3
Do you support that 802.11be allows the following operation for power saving:
  When a STA of a non-STR non-AP MLD receives DL frames, which is intended to itself from a peer AP, including a traffic indicator for another STA of same non-AP MLD and the traffic indicator indicates no buffered data for the another STA, the another STA may enter doze state until end of DL TXOP of the peer AP transmitting the DL frames.
    The signaling for enabling this operation is TBD.
    The details of traffic indicator is TBD.

## Slide 22: Appendix

## Slide 23: Appendix #1
Example: UL data TXOP early termination
  The STA 2 that have entered doze state can awake before end of UL TXOP by transmitting CF-end frame over Link 1
    Note that STA 2 awakes from doze state after end of UL TXOP for AP 1 in general case

## Slide 24: Appendix #2
Example: DL data TXOP early termination
  The STA 2 that have entered doze state can awake before end of DL TXOP by receiving CF-end frame from Link 1
    Note that STA 2 awakes from doze state after end of DL TXOP for AP 1 in general case