## Slide 1: Additional Overhead Reduction in Mixed BF Feedback
Date: 01-01-2020
Authors:

## Slide 2: Introduction
Many contributions have discussed the topic of feedback size reduction and what directions may be used for next generation [1],[2],[3]
Mixed Beamforming (Mixed BF) where the precoder is constructed by two components (wideband and narrowband) was presented in [2] and [3] as a candidate for 802.11be
In [4] we studied the properties of Mixed BF where the difference between the wideband and the narrowband part was analyzed in detail
The main aspect was the limited impact of narrowband component on the equivalent SNR and the performance of Mixed BF
In this contribution we want to continue investigating Mixed BF properties, and show a technique that allows additional feedback size reduction with negligible or zero degradation of the performance

## Slide 3: Re-Cap Narrowband Properties
The main property studied in [4] was the impact of the narrowband component of Mixed BF (shown in the diagram below) on the SNR
We showed that the wideband component of Mixed BF mostly defines the beam directions of the beamformed DL transmission, whereas the narrowband part yields a per-tone fine phase adjustment
We also presented the Zero-Forcing post-processing SNR provided by Mixed BF and showed that the narrowband component contributes very little to it
Following this observation we may consider accuracy relaxation for the narrowband part (i.e. smaller feedback size ) with no DL performance degradation
Wideband Precoder Calculation
Narrowband Equivalent Matrix Calculation
Narrowband Precoder Calculation
- per tone
channel matrix
NxM
NxK
NxK

## Slide 4: Narrowband Precoder Properties
We further study the properties of the narrowband precoder in order to find a technique that may be applied for feedback size reduction
We examined the power of the entries of the matrix (the narrowband component) to understand the contribution of each entry to the total power of each column, i.e. impact on per-stream SNR
The figure on the right shows the histogram of the entries of 2x16 matrices obtained from ~3000 realizations of the TGn-D channel
We can see that more than 20% of the entries have a power below 0.01 (of total unit power)
This means we can ignore very small values of the V-matrix and reduce the feedback size of Mixed BF by an additional ~20% with very small reduction in total power
Power

## Slide 5: Main Concept
The main concept is to select those entries of the narrowband V-matrix that contribute the majority of the total power and null the rest
The selection might be done based on some arbitrary threshold (entries below the threshold will be nulled) or by nulling a constant number of (lowest) entries; at each column of V-matrix different entries may be selected
Selected entries are not included in feedback data which means feedback size will be reduced by the number of nulled entries
The diagram of Mixed BF with nulling entries of narrowband V-matrix is shown below (Ksel corresponds to the number of selected entries per column)
Wideband Precoder Calculation
Narrowband Equivalent Matrix Calculation
Narrowband Precoder Calculation
Entries Nulling
Update Narrowband Precoder
- per tone
channel matrix
NxM
NxK
NxK
Nx(K-Ksel)

## Slide 6: Impact on SNR
In order to justify the idea to ignore (null) small values of the narrowband V-matrix we first look at the impact on the post-processing SNR
We compared the PPSNR of the original narrowband V-matrix (without nulling) and V-matrix where some of the entries are nulled
We nulled on average ~25% of the entries
In the figure on the right we can see that in ~80% of the cases the SNR difference is below 60dB, while in all the cases it is below 30dB, which means no degradation of the performance

## Slide 7: Method Applicability
In order to study the applicability of this concept we checked the number of rows that contribute the least at each channel sounding
Per channel realization, we calculated at each tone the number of rows below the threshold of 0.05 and averaged over the entire 20MHz BW
We can see in the figure on the right that the average number depends on the initial K value and reduces with K (additional observation is given in the Appendix)
Following this observation we understand that the beamformee can choose the required number of rows according to the selected K value and manage the desired feedback size

## Slide 8: Simulation Results
We complete the analysis of the idea by simulating two different scenarios:
  MU-MIMO with 2 STAs, Nss = 2 each, 16Tx Ant – in this case we compared between K=6 (wideband precoder size) and K = 10 with nulling of ~3 entries per column of narrowband V-matrix
  MU-MIMO with 3 STAs, Nss= 2 each, 16 Tx Ant – in this case we compared between regular explicit precoder and mixed BF using K = 16 (no size reduction of wideband part) and nulling of ~5-6 entries per column of narrowband V-matrix
We can see in the figures below that in both cases nulling of the V-matrix entries results in no degradation in the performance while the overhead may be further reduced by 25%-35%
69%
Reduction
63%
Reduction
35%
Reduction
50%
Reduction

## Slide 9: Feedback Size Summary
We showed in [4] that Mixed BF can lead to significant feedback size reduction
Here we present an additional feedback size reduction that can be achieved by applying nulling on the entries of the narrowband precoder matrix
We can see in the table below that in all the cases where nulling is applicable the feedback size is further reduced by up to ~25%
Moreover in case K=N_Tx (e.g. last row) we can achieve 35% of feedback size reduction with no performance degradation
Nc | Nc (Nss) per User | Nusers | K | Na Per-Tone Precoder | Na Mixed BF | Na Mixed BF with Nulling | Feedback Size Reduction % | Performance Loss | Feedback Size Reduction with Nulling %
8 | 2 | 4 | 6 | 26 | 18 | 12 | 31 | 0.2dB | 54
8 | 2 | 2 | 4 | 26 | 10 | 4 | 62 | 0.5dB | 85
16 | 2 | 6 | 12 | 58 | 42 | 42 | 28 | 0.2dB | 28
16 | 2 | 2 | 10 | 58 | 34 | 22 | 42 | 0.2dB | 63
16 | 2 | 3 | 16 | 58 | 58 | 38 | 0 | <0.1dB | 35
Presented
on previous
slide

## Slide 10: Conclusions
Mixed BF properties were analyzed with respect to minimizing feedback size
Relaxed accuracy of narrowband precoder allows additional feedback size reduction with no degradation of the performance
Entries nulling is a simple technique that can implement accuracy reduction with easy adjustment to performance requirements
Moreover nulling may be applied for “backward compatible” use-case where wideband component has no size reduction
Summarizing all the details presented above and in [4] Mixed BF is a promising method to be adopted by 802.11be for feedback size reduction

## Slide 11: References
[1] 11-18/1231r6-0eht-eht-draft-proposed-par.
[2] 11-18-1184-01-0eht-eht-discussions-on-throughput-enhancement
[3] 11-19-0391-00-0eht-feedback-overhead-reduction-in-802-11be
[4] 11-19-1115-00-00be-reduced-beamforming-feedback-for-802-11be

## Slide 12: Appendix
The figures below present a power of six lowest entries of narrowband component and also an accumulated power (corresponds to power reduction in case of nulling)
We can see that in majority of the cases we can null 4-6 entries with less 10% reduction of total power