## Slide 1: PPDU Types and U-SIG Content
Date: 2020-01-13
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Lin Yang |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
In these slides we cover
  U-SIG Content
    Bandwidth information
    PPDU type field
  PPDU format design for EHT
    Also address whether we unify SU and MU PPDU formats or not
    Design of Compressed Modes for the MU PPDU format

## Slide 3: Bandwidth Information in U-SIG
So far, there is consensus on having the following version independent fields in U-SIG
  PHY version identifier: 3 bits
  UL/DL flag: 1 bit
  BSS color, number of bits TBD
  TXOP duration, number of bits TBD
The fields in red tell us about the medium utilization of the current PPDU
  How long ? In what link direction? And which BSS is using it ?
Natural to add bandwidth information to the above group of fields (as a version independent field)
  Tells us about the spectrum occupancy of the current PPDU
  Puncturing info maybe useful to add as well as that makes this information more precise

## Slide 4: Bandwidth Information as Version Independent
Intent of version independent fields is for future generations to have a more sophisticated coexistence
Spectrum utilization information has cross-generational appeal
  Ability to understand this information precisely across PHY amendments is useful
What if future amendments add higher bandwidths than 320MHz ?
  We can make the bandwidth field future proof by leaving un-used states
    Un-used states can have a specific meaning for EHT devices (e.g. >320MHz)
    Example on slide 17 in Appendix
  Can also be handled by expanding the BW field in a backwards compatible way in the future

## Slide 5: PPDU Type in U-SIG
The PHY version identifier field in the version independent section of U-SIG differentiates between WiFi amendments (11be/bf/bg…)
We still need a field to differentiate among different PPDU types of a particular amendment
  No longer using L-SIG length for this
Suggest to add a “PPDU type” field in U-SIG for this purpose
  Subsequent format of preamble can change depending on PPDU type
  2-3 bits should be enough
We would like PPDU type to be a version dependent field in U-SIG
  Every version of WiFi can have its own set of PPDU types

## Slide 6: PPDU Types in EHT
11ax supports 4 PPDU types: TB, SU, ER-SU, MU
EHT will support >=2 PPDU types
  TB is quite different from SU & MU, and should be an independent PPDU type
  SU/MU PPDU types may be unified
    Discussion in subsequent slides shows why unification is a good direction
  ER SU need is up for discussion
    Not covered in this slide deck

## Slide 7: EHT TB PPDU Design
For TB PPDU, a 2-symbol U-SIG, with no EHT-SIG is enough
52 bits in U-SIG are more than enough to accommodate all the version independent fields and version dependent fields
  Details in Appendix
L-STF
L-LTF
L-SIG
RL SIG
U-SIG
TB PPDU Format for EHT
EHT-STF
EHT-LTFs
Data

## Slide 8: Whether to unify SU/MU PPDU format or not? (1)
If SU PPDU is a separate format, a 1 symbol EHT-SIG at MCS0 is still needed
  Around a total of >=47 bits need to carried in the U-SIG and EHT-SIG (Details in Appendix)
The decision to merge SU and MU PPDU formats depends on the extra overhead of using the MU PPDU format while sending to a single user
Based on SIG field content, don’t see a huge additional burden by sending the MU PPPDU to a single user
  Only a few redundant fields compared to using a separately optimized SU PPDU format (Details in appendix)
EHT-SIG
L-STF
L-LTF
L-SIG
RL SIG
U-SIG
SU PPDU
(If separate from MU)
1 symbol
Fixed MCS: rate ½, BPSK
EHT-SIG-common
L-STF
L-LTF
L-SIG
RL SIG
U-SIG
SU PPDU
(If combined with MU)
EHT-SIG-per-user
Not a symbol boundary
Variable MCS/length
as indicated in U-SIG

## Slide 9: Whether to unify SU/MU PPDU format or not? (2)
Even if there is some additional burden, the EHT-SIG in MU case can go at a higher MCS than MCS0 in majority of the cases
  The final additional overhead expected to be minimal for most cases
Moreover, the SU puncturing and RU aggregation cases are likely to use the MU PPDU format
Hence, we recommend unifying SU and MU PPDU formats

## Slide 10: Special Cases of MU PPDU
If we go with the SU/MU PPDU unification paradigm, EHT is expected to support the following cases of the MU PPDU
  Ones in red might have potential for compression of SIG field

## Slide 11: Compressed Modes Design
Proposed compressed modes for MU PPDU(assume unification with SU) are shown below
  Compression mode 1: Used for Full BW SU or Full BW MU-MIMO; RU allocation info in the common field is omitted
  Compression mode 2: Used for Punctured SU or Punctured MU-MIMO; RU allocation info in the common field is replaced by a punctured channel info with granularity of 20MHz
  Notes
    SU or MU-MIMO is indicated through the ‘number of EHT-SIG symbols’ field which is interpreted as number of non-OFDMA users
      Value 0 indicates SU
      Similar to 11ax where the number of MU-MIMO users is indicated in this way
    SU will have only ONE EHT-SIG-per-user field of the non-MU-MIMO allocation format (even for puncturing mode)

## Slide 12: Summary
We proposed the following in these slides
  Bandwidth information as a version independent field
  PPDU type as a version dependent field
  No EHT-SIG for TB PPDU Format
  Unification of SU and MU PPDU Formats
    Two compressed modes to support SU and ‘non-OFDMA MU-MIMO’ cases (with and w/o puncturing)

## Slide 13: Straw-poll 1
Do you agree U-SIG will contain bandwidth information, carried as a version independent field?
  This information may also convey some puncturing information
  Number of bits is TBD

## Slide 14: Straw-poll 2
Do you agree to add “PPDU type” as a version dependent field in U-SIG?
  Number of bits is TBD

## Slide 15: Straw-poll 3
Do you agree that in EHT, SU and MU PPDU formats will be merged into a single PPDU type ?

## Slide 16: Appendix
Some more details about SIG contents

## Slide 17: Example of a future-proof BW Field
We can make the bandwidth information future proof by leaving un-used states (shown in red)
  EHT devices may be required to behave in a certain way when they see the field set to those states
3 bit field value (decimal) | Meaning for EHT (in MHz) | Meaning for EHT+ (in MHz)
0 | 20 | 20
1 | 40 | 40
2 | 80 | 80
3 | 160 | 160
4 | 240 | 240
5 | 320 | 320
6 | >320 | New bandwidth 1
7 | >320 | New bandwidth 2

## Slide 18: TB PPDU U-SIG Content
U-SIG transmits total 52 bits, including
  Version independent fields: >=21 bits
    Version identifier (3 bits), UL/DL (1 bit), TXOP (7 bits), BSS color (6 bits)
    PPDU BW & Punctured channel info: >=4 bits
  Version dependent fields
    PPDU type: 2 bits
    Spatial re-use (SR) field(s): 4 bits (option 1: 1 SR field) or 8 bits (option 2: 2 SR fields)
  CRC: 4 bits
  Tail: 6 bits
  TBD: <=15 bits (option 1) or <=11 bits (option 2)

## Slide 19: U-SIG & EHT-SIG content for separate EHT SU PPDU (1/2)
For SU PPDU, a 2-symbol Pre-SIG, with a 1-symbol EHT-SIG is enough
We propose the following fields in U-SIG and part of the common field in EHT-SIG
  Version independent fields: >=21 bits
    Version identifier (3 bits), UL/DL (1 bit), TXOP (7 bits), BSS color (6 bits)
    PPDU BW & Punctured channel info: >=4 bits
  Version dependent field(s) related to EHT-SIG field structure: 2 bits
    PPDU type: 2 bits
  Version dependent fields similar to MU PPDU: 17 bits
    Spatial reuse (4 bits), GI+LTF size (2 bits), Doppler (1 bit), LDPC extra symbol segment (1 bit), STBC (1 bit), Beam change (1 bit), Pre-FEC padding factor (2 bits), PE disambiguity (1 bit)
    The “Number of EHT-LTF symbols and midamble periodicity” field (4 bits) is replaced by “NSTS and midamble periodicity” field (4 bits)

## Slide 20: U-SIG & EHT-SIG content for separate EHT SU PPDU (2/2)
We propose the following fields in U-SIG and part of the common field in EHT-SIG (Cont’d)
  Version dependent fields that are SU specific: 7 bits
    MCS: 4 bit
    DCM: 1 bit
    Coding: 1 bit
    Beamformed: 1 bit
There are >=47 bits
  Fields of at most 42 bits will be in U-SIG, along with CRC (4 bits) and Tail (6 bits)
  Other fields will be in the 1-symbol EHT-SIG

## Slide 21: More details on unification
26 additional bits need to be sent when an MU PPDU is used for single user purposes (vs a separate SU PPDU)
  EHT-SIG MCS (3 bits), EHT-SIG DCM (1 bit), number of EHT-SIG symbols (or number of non-OFDMA users) (5 bits), EHT-SIG compression (2 bits)
  STA ID field (11 bits) and NSTS field (4 bits) in the user-specific field
Extra 26 bits for a unified SU/MU PPDU means >=73 bits total bits need to be sent for the SU case
  42 can be carried in U-SIG and 31 need to be carried in EHT-SIG
    For EHT-SIG MCS> MCS0, one symbol may still be enough  No extra overhead compared to separate SU PPDU for most cases