## Slide 1: MLD MAC Address and WM Address
Date: 2020-01-10
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Dan Bravo |  |  |  | 
Laurent Cariou |  |  |  | 
Arik Klein |  |  |  | 
Ido Ouzieli |  |  |  | 
Notes: September 2012

## Slide 2: Background
Multi-link framework has been proposed below with the definition of MLD address[1]
  a MLD has a MAC address that identifies the MLD management entity
  For example, the MAC address can be used in multi-link setup between a non-AP MLD and an AP MLD
We provide follow up to MLD MAC address and STA WM medium address
AP1
AP2
AP3
STA1
STA2
STA3
AP MLD
Non-AP MLD
AP1
Non-AP STA1
Request frame for multi-link setup
Response frame for multi-link setup
Link 1
Link 2
Link 3

## Slide 3: MLD MAC Address and STA WM Medium Address
On a high level, we think that
  MLD MAC address is used to identify and differentiate different MLDs
  STA WM MAC address is used for on the air transmission on the corresponding wireless medium
The following clarification in SFD is needed
  A MLD has a MAC address that singly identifies the MLD management entity.
STA 1
2.4 GHz
STA 2
5 GHz
STA 3
6 GHz
MLD
MLD MAC address is used to identify different MLDs
STA 1/2/3 WM MAC address is used for over the air transmission on the corresponding WM

## Slide 4: AP MLD MAC Address and WM Medium Address
For AP MLD to continue to serve legacy non-HT/HT/VHT/HE STA, each affiliated AP of a AP MLD shall use different MAC address
There exists ambiguity if two affiliated APs use the same MAC addresses
  For example, if AP1 and AP2 use the same MAC address, it is hard for legacy STA to know if AP2 is a different AP of AP1 or it is AP 1 doing channel switch
For AP MLD MAC address, we do not see requirement to standardize relation with the MAC address of affiliated APs, but are open for discussion
AP 1
2.4 GHz
AP 2
5 GHz
AP 3
6 GHz
AP MLD

## Slide 5: Non-AP MLD MAC Address and WM Medium Address
For non-AP MLD, if AP MLD uses different MAC addresses for affiliated STAs, it makes sense to have symmetric operation for non-AP MLD as well
  Non-AP MLD may serve as soft AP for peer to peer communication. Symmetric operation simplify implementation consideration
  Transmission from non-AP MLD to AP MLD in different link may have the same Nonce for different message if affiliated non-AP STAs have same MAC address under same PN space/PTK [3], which destroys the security property
For non-AP MLD MAC address, we do not see requirement to standardize relation with the MAC address of affiliated non-APs, but are open for discussion
Non-AP 1
2.4 GHz
Non-AP 2
5 GHz
Non-AP 3
6 GHz
Non-AP MLD

## Slide 6: non-AP MLD Address in Multi-link Setup Procedure
For legacy association, an AP differentiates different associated non-AP STA through MAC address of non-AP STA
For multi-link setup, we envision that differentiation of different non-AP MLD will require a similar identifier, and we think the MAC address of non-AP MLD can serve similar purpose
  An identifier with smaller size may lead to identifier collision and confusion of setup result
  Without identifier, differentiation of different non-AP MLD has to be based on all the configuration details of non-AP MLD, and figuring out difference like resetup with different configuration is difficult
Knowing non-AP MLD MAC address after setup is useful for following negotiations like security [3] and BA [4]
Proposal: non-AP MLD MAC address is indicated during the multi-link setup procedure

## Slide 7: Example
Easily differentiate multi-link setup with different non-AP MLD
Easily understand as same non-AP MLD with configuration change during resetup

## Slide 8: AP MLD Address in Multi-link Setup Procedure
For legacy association, the MAC address of the associated AP is known before association.
For multi-link setup, it is TBD if AP MLD discovery can provide the MAC address of AP MLD
  If AP MLD address is not known before multi-link setup, then having AP MLD address in multi-link setup procedure is useful for following negotiations like security [3] and BA [4]
  If AP MLD address is known before multi-link setup, then having AP MLD address in multi-link setup procedure is useful to confirm the destined MLD for setup and avoid weird corner case
Proposal: AP MLD MAC address is indicated during the multi-link setup procedure

## Slide 9: Example
If AP MLD address is not available before multi-link setup,
Both AP MLD and non-AP MLD knows the MLD address of each other after setup, which is useful for following negotiations like security [3] and BA [4]

## Slide 10: Example
If AP MLD address is available before multi-link setup, using AP MLD address in multi-link setup request rather than AP1 address in RA to identify AP MLD avoids the possible ambiguity when configuration changes
Configuration changes
AP
2
AP MLD
1
AP
3
AP
4
AP MLD
2
AP
5
AP
1
AP
1
AP
4
AP
5
AP MLD 2
Non
-
AP
1
.
1
Non
-
AP MLD
1
Non
-
AP
1
.
2
Non
-
AP
1
.
3
Multi
-
link setup request
with non
-
AP MLD address
and AP MLD 1 address
Multi
-
link setup response
deny the setup due to
different understanding

## Slide 11: Need of MLD address in SA/DA
The definition of SA and DA in the spec is as follows:
  The source address (SA) parameter specifies an individual MAC sublayer address of the sublayer entity from which the MSDU is being transferred.
  The destination address (DA) parameter specifies either an individual or a group MAC sublayer entity address.
Given that in multi-link, a MLD only has one data service interface to the LLC, the address used in the SA/DA shall use the MLD address to identify the source MLD and destination MLD.

## Slide 12: Conclusion
We think that different affiliated APs of a non-MLD shall have different MAC addresses.
We think that if different affiliated APs of a non-MLD shall have different MAC addresses, then different affiliated non-AP STAs of a non-AP MLD shall have different MAC addresses.
We propose to indicate AP MLD MAC address and non-AP MLD MAC address during the multi-link setup procedure
  Clearly identify the MLD for setup and avoids ambiguity, which aligns with the agreed motion text in SFD
  For example, the MAC address can be used in multi-link setup between a non-AP MLD and an AP MLD
  Useful for following negotiations like security [3] and BA [4]
  Useful for filling in SA/DA

## Slide 13: Straw Poll #1
Do you agree to revise the 11be SFD as follows:
  A MLD has a MAC address that singly identifies the MLD management entity.
  Y: 41
  N: 3
  A: 37

## Slide 14: Straw Poll #2
Do you support to indicate AP MLD MAC address and non-AP MLD MAC address during the multi-link setup procedure?

## Slide 15: Straw Poll #3
Do you support that if different affiliated APs of an AP MLD have different MAC addresses, then different affiliated non-AP STAs of a non-AP MLD with more than one affiliated STA have different MAC addresses?

## Slide 16: Reference
[1] 19/0822r9 Extremely efficient multi-band operation
[2] 19/0773r8 Multi-link operation framework
[3] 19/1822r2 Multi-link security consideration
[4] 20/0053r0 Multi-link BA