## Slide 1: Sequence number and BA operation with larger BA buffer size
Date: 2020-01-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Sequence Number in 802.11 Baseline
12-bit sequence number field is used to identify the MPDU being transmitted.
211 rules are used to decide whether a received frame is discarded or not:

## Slide 3: Large BA Buffer Size and Large MPDU Number in A-MPDU
320MHz BW, 16Nss, 2048 QAM mean that the larger (i.e. 4 times) A-MPDU size, larger BA TX buffer, longer scoreboard context bitmap, and larger BA reorder buffer are required:
  Option 1: increment of 4 times
    <=1024 BA buffer size and <=1024 MSDUs within an A-MPDU.
      New BA variant to support <=1024 BA bitmap.
  Option 2: increment of 8 times with the consideration of multiple links
    <2048 BA Buffer size and <=2048 MSDU within an A-MPDU.
      New BA variant to support <=2048 BA bitmap and the changes in the following slides (Scoreboard context operation changes, additional sequence number field).

## Slide 4: Solution 1: Improving Scoreboard Context Updating Rules
After changing the scoreboard context updating rules (in green), the BA bitmap size, BA buffer size can be as large as 2048:
  If the buffer size of the BA negotiation is no more than 210, the current scoreboard control rules apply.
  If the buffer size of the BA negotiation is more than 210, the following scoreboard control rules apply (note the cases where WinStartR<SN/SSN<WinEndR are not shown here since there are no changes to them):
    When a QoS Data frame with sequence number SN is received,
      If WinEndR < SN < WinStartR + 211 + AdditionThreshold
        Set to 0 the bits corresponding to MPDUs with Sequence Number subfield values from WinEndR+1 to SN – 1.
        Set WinStartR = SN – WinSizeR + 1.
        Set WinEndR = SN.
        Set to 1 the bit at position SN in the bitmap.
      If WinStartR + 211 + 210 <= SN < WinStartR, make no changes to the record.
    When a BAR frame with Start Sequence Number SSN is received,
      If WinEndR < SSN < WinStartR + 211 + AdditionThreshold
        Set to 0 the bits corresponding to MPDUs with Sequence Number subfield values from WinEndR+1 to SN – 1.
        Set WinStartR = SSN.
        Set WinEndR = SSN + WinSizeR - 1.
        Set to 0 for all the bits within the window defined by WinStartR and WinEndR .
      If WinStartR + 211 + 210 <= SSN < WinStartR, make no changes to the record.
  Note: AdditionThreshold has value of >=210 and < 211

## Slide 5: Solution 2: Additional Sequence Number Bits in Fragment Number Field
Fragment Number/
Additional Sequence Number
Observation: when the sequence number size is more than 4096, there is no requirement to do frame fragmentation.
Proposal 1: the Fragment Number field or part of Fragment Number field can be used as additional sequence number bits.
  The additional sequence number bits are the MSB of the combined sequence number or the LSB of the combined sequence number.
Proposal 2: a new optional field “Additional Sequence Number” is added in MAC header.
Variable
Length
Additional
Sequence Number
Frame
Body
FCS
Variable
Length
4
1

## Slide 6: Solution 2: Additional Sequence Number Bits in Fragment Number Field
Each STA/AP announces whether it supports >12-bit sequence number through management frame in EHT Capabilities element, Extended Capabilities element or other elements.
  One variant to this could be that all EHT STAs/APs support >12-bit sequence number.
Indication of additional sequence number:
  Method 1: one bit in TID field of QoS Control field indicates whether the Additional Sequence Number is carried in the frame.
    The TXOP holder that supports >12-bit sequence number transmits the frames by using >12-bit Sequence Number if the recipient of the frames supports >12-bit sequence number.
Fragment Number/
Additional Sequence Number
Variable
Length
TID
B0
B2
Long Sequence
Number
B3
EOSP/
Queue Size Indication/
TXOP Duration Indication
B4
TXOP Limit/
Queue Size/
TXOP Duration
B5
B7

## Slide 7: Solution 2: Additional Sequence Number Bits in Fragment Number Field
Indication of Additional sequence number (cont’d):
  Method 2: one bit in MPDU Delimiter, e.g. redefining the reserved B1 as Long Sequence Number field, indicates whether the Additional Sequence Number is carried in the MPDU that follows MUDU Delimiter are the additional sequence number bits
    The TXOP holder that supports >12-bit sequence number transmits the frames by using >12-bit Sequence Number if the recipient of the frames supports >12-bit sequence number.
MPDU Delimiter
Long Sequence
Number
Fragment Number/
Additional Sequence Number
Variable
Length

## Slide 8: Solution 2: Additional Sequence Number Bits in Fragment Number Field
Indication of Additional sequence number (cont’d):
  Method 3: in EHT PPDU, the Additional Sequence Number is carried in the MPDU.
Fragment Number/
Additional Sequence Number
Variable
Length
Legacy
PHY
Header
EHT
PHY
Header
Data
  Method 4: in frames from an EHT AP/STA to another EHT STA/AP, the Additional Sequence Number is carried in the MPDU per SRC MLD, DST MLD, TID.

## Slide 9: Straw Poll 1
Which one do you support:
  <=1024 BA buffer size and MSDUs/A-MSDUs in an A-MPDU, additional BA bitmap of 512, 1024.
  <=2048 BA buffer size and MSDUs/A-MSDUs in an A-MPDU , additional BA bitmap of 512, 1024, 2048.