## Slide 1: BA Consideration
Date: 2020-05-26
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap
11be group agreed that the BA can include 512, 1024 BA bitmap.
There is a requirement to decrease the BA overhead.
Several methods are proposed:
  HE/EHT PPDU to carry the BA frame.
  BAR to indicate whether the WinStartR is adjusted per the received BAR.
  The A-MPDU transmitter to request the BA buffer size through MAC header in QoS Data frames or BAR.

## Slide 3: Methods to Decrease BA Overhead 1
Instead of non-HT duplicated PPDU to carry BA, wider BW HE/EHT PPDU can be used to carry the BA.
  The TXOP holder that transmits the BA in a PPDU other than non-HT duplicated PPDU may transmit CF-End in non-HT duplicated PPDU if there is no other frame exchange in the TXOP.
  This is suitable in BSS with wider operating BW, e.g. in 5/6GHz band.

## Slide 4: Methods to Decrease BA Overhead 2
Each link may maintains separate Scoreboard Context Control with same WinStartB to prepare the retransmission of frames in different links.
Shorter Block Ack Bitmap can be used if the sequence number difference of the acknowledged QoS Data frames are smaller, e.g.
  256-bit Block Ack Bitmap can be used when the negotiated BA buffer size is 1024, and the acknowledged QoS Data frames are 255 frames from Sequence Number 1000 to 1254.
When a BAR whose Starting Sequence Control field has a value (Value1) larger than WinStartB and WinStartR is used to solicit the Block Ack, the future transmitted QoS Data frame with Sequence Number that are smaller than Value1 can’t be correctly acknowledged per scoreboard context and discarded in reorder buffer. The following rules can solve the issue:
    For block ack agreement that is not a protected block agreement:
      Treat BAR same as in protected block ack agreement, or
      Redefine BAR: the initiator of BAR can indicate whether it wants the recipient of BAR to shift the WinStartB and WinStartR or not.

## Slide 5: Methods to Decrease BA Overhead 3
Explicit request by the initiator of A-MPDU indicates shorter BA bitmap size than the negotiated BA bitmap size:
  The initiator transmits starting sequence number and requested BA bitmap size in BAR (compressed BAR, multi-TID BAR, MU BAR).
    The Fragment Control field in BAR indicates the requested BA bitmap size.
  HE Control field should support the case where a multi-TID A-MPDU request the block acks for multiple TIDs.
    24 bits can be used where every 3 bits indicate the request BA bitmap size (a specific value indicates no request).
BA creating updating:
  Instead of creating BA bitmap per WinEndR, the start sequence number of soliciting BAR or A-MPDU is used to preparing the BA bitmap.
BA Starting Sequence Number Control field in BAR

## Slide 6: Straw Poll 1
Do you support to allow HE SU PPDU to carry the solicited BA in 5 GHz bands if the transmit time of HE SU PPDU is less than the PPDU duration of a non-HT PPDU containing the Control frame sent at the primary rate?

## Slide 7: Straw Poll 2
Do you support to allow EHT SU PPDU to carry the solicited BA in 5 ang 6 GHz bands if the transmit time of EHT SU PPDU is less than the PPDU duration of a non-HT PPDU containing the Control frame sent at the primary rate?

## Slide 8: Straw Poll 3
Do you support that for block ack agreement that is not a protected block agreement, the initiator of BAR can indicate whether it wants the recipient of BAR to shift the WinStartB and WinStartR or not?

## Slide 9: Straw Poll 4
Do you support that the Fragment Number field in BA Starting Sequence Number Control field of BAR carry the requested BA bitmap size?