## Slide 1: Non-AP MLD Link Address
Date: 2020-01-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: AP MLD and Non-AP MLD
A STA/AP MLD has multiple STAs/APs.
An AP MLD has different MAC addresses in its different links.
This presentation discusses the link addresses of a non-AP MLD.
AP MLD
MAC with Addr11
MAC with Addr21
Common MAC
Link1
Link2
non-AP MLD
MAC with Addr18
MAC with Addr28
Common MAC
Link1
Link2
A-MPDU1
A-MPDU2

## Slide 3: Recap: Per STA/AP Checking in 11 Baseline
Operation in an AP:
  DL
    Find security key.
    Find power save state.
    Find Tx power, BW, MCS, Nss
  UL:
    Find Security key.
Operation in a STA:
  DL:
    Find security key.
  UL:
    Find security key.
    Find Tx power, BW, MCS, Nss.
The AP’s information check in a STA is not an issue since a STA only associates with one AP.
Note: other per STA checking operations are also possible, e.g. Tx power, whether a STA is 11a/b/g/n/ac/ax/EHT STA.

## Slide 4: Per STA (or non-AP MLD) Checking in AP MLD
AP DL:
  Find security key per non-AP MLD.
  Find the DL link per non-AP MLD’s TID, link mapping when different TID link mappings are allowed for non-AP MLDs.
    Figure out AP link address once the downlink is decided.
    This per STA checking can be removed if the unique TID to link mapping exist in the MBSS.
  Find STA link address when the different link addresses are allowed at a non-AP MLD.
    This can be removed if non-AP MLD has same address in all its links.
  Find power save state per STA.
  Find Tx power, BW, MCS, Nss per STA.
AP UL:
  Find Security key per non-AP MLD.
  Map STA link address to SAP address of non-AP MLD.
    This per STA checking can be removed if non-AP MLD has same address in all its links.

## Slide 5: Link Address Consideration of STA MLD
It is good for unified link address selection rules for both AP MLD and STA MLD, i.e. both STA MLD and AP MLD have different link addresses for STAs affiliated with them:
  No change to encryption/decryption.
  Easy design for STA MLD that supports soft-AP MLD.
The addition of AP’s per STA/MLD checking can be removed by some design, e.g.
  A-MSDU is used to carry MSDUs.
  An AP MLD can disable TID to Link mapping or disabling TID to link mapping per non-AP MLD (the TID to link mapping policy for the whole multi-link BSS is allowed).

## Slide 6: Per STA Checking and A-MSDU
For UL A-MSDU, the following address setting rules are defined:
  SA is set to SAP address of non-AP MLD.
  With this UL A-MSDU, the AP doesn’t need to do STA link address to SAP address of non-AP MLLD mapping, and the AP doesn’t need to do AP link address to SAP address of AP MLLD mapping.
For DL A-MSDU, the following address setting rules are defined:
  DA is set to SAP address of non-AP MLD.
A-MSDU Subframe structure

## Slide 7: Straw Poll 1
Do you support that:
  An STA MLD uses different MAC addresses on each STA affiliated with it.