## Slide 1
Authors:
Unified Multi-Link and Multi-AP Reference Model
Date: 2020-01-11
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | sun.bo1@zte.com.cn
Zhiqiang Han | ZTE |  |  | han.zhiqiang1@zte.com.cn
Nan Li | ZTE |  |  | li.nan25@zte.com.cn
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses the issue in the reference model to support both multi-link and multi-AP features in IEEE802.11be, and suggests to consider the unified reference model to support both ML and MAP features.

## Slide 3: Background
Multi-Link Logic Entity
  In the reference [1], it proposes the ML reference model with MLLE.
  In the reference [2], it proposes the definition of MLLE as:
    A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.

## Slide 4: Background
Virtual BSS of Multi AP
  In the reference [3], it proposes the multi AP to form a virtual BSS for
    Single association and authentication state maintenance within the MAP group
    Dynamic AP selection by STA and V-BSS Coordinator
  In the reference [4], it proposes two options for forming a MAP group with
    pre-configured MAP group for a STA.
    Dynamic MAP group formation for a STA
  In the reference [4], it discusses the backhaul impact in the MAP joint transmission.
Coordinator AP
Coordinated AP1
Coordinated AP2
X

## Slide 5: Concerns on Reference Model
Multi-Link
  Multi-Link operation is one of 802.11be features to support aggregation of packets sent on multiple bands/channels concurrently, or distribution of packets to transmit over multiple bands/channels concurrently. This feature requires to update the current reference model.
Multi-AP
  Multi-AP operation (e.g. coordinated and/or joint transmission) is another enhancement feature listed in the EHT PAR. This feature needs the coordination and/or data synchronization at least in the MAC layer among multiple AP devices. This feature requires to define a new or update the current reference model as well. However no detail proposal has been made yet.
  Issues
  When both features are supported,
    what the combined reference model should be ?
    What is the SAP in the combined reference model to the DS and WM ?
  How to support multi AP in ML AP case ?
  It would be better to define the unified reference model for both multi-link and multi-AP.

## Slide 6: Unified ML and MAP Framework
AP MLD instance
  An AP MLD instance is a logical device that has one or more affiliated STAs, where each STA affiliated with the MLD is an AP. The MLD AP instance has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
  The AP MLD instance forms a MLD Service Set (i.e. MLD-SS) with an identifier of MLD-SSID.
  Note: MLLE is the multi-link logical entity (TBD)
MLD AP
ML Logical Entity (MLLE)
STA (MAC/PHY)
AP Device
STA (MAC/PHY)
Link1
Link2
MLME
MAC-SAP
DS
AP MLD instance

## Slide 7: Unified ML and MAP Framework
Affiliated AP MLD instance and AP MLD Group
  An affiliated AP MLD instance is a logical device of AP with a collaborated link to an AP MLD instance. It has no direct MAC data service interface and primitives to the LLC, and a single address associated with the interface to communicate on the DSM.
  The AP MLD instance and affiliated AP MLD instance(s) can form an AP MLD Group.
  The AP MLD Group creates a MLD Group Service Set (i.e. MLD-GSS) with an identifier of MLD-GSSID.
A MLD AP Group
ML Logical Entity (MLLE)
STA (MAC/PHY)
AP MLD Instance
STA (MAC/PHY)
Link3
Link4
MLME
Affiliated AP MLD Instance
STA (MAC/PHY)
Link1
DS
MAC-SAP
AP MLD Group
STA (MAC/PHY)
Affiliated AP MLD Instance
Link2

## Slide 8: Unified ML and MAP Framework
Multiple MLD AP Groups and MLD GSSs
  Each AP MLD instance and its affiliated AP MLD instance(s) forms a MLD-GSS with a unique MLD-GSSID.
  Each MLD-GSS may support a network slicing to differentiate services from other MLD-GSS.
Multiple MLD AP Group
MAC-SAP
MLME
DS
ML Logical Entity (MLLE)
STA (MAC/PHY)
MLD AP Instance
STA (MAC/PHY)
Link3
Link4
MAC-SAP
MLD AP Group 1
MLD AP Group 2
Affiliated MLD AP Instance
STA (MAC/PHY)
Link1
STA (MAC/PHY)
Affiliated MLD AP Instance
Link2

## Slide 9: Unified ML and MAP Framework
An example of MAC functions in AP MLD instance
 | TX |  | RX | 
MLLE (MAC-U) | A-MSDU Aggregation |  | A-MSDU De-aggregation | 
 | PS Defer Queue |  | (null) | 
 | Sequence Number Assignment |  | (null) | 
 | MSDU Integrity Protection (optional) |  | MSDU Integrity Protection (optional) | 
 | Fragmentation |  | Defragmentation | 
 | Packet Number Assignment |  | Replay Detection (optional) | 
 | (null) |  | Block Ack Buffering and Reordering | 
 | MPDU Encryption and Integrity Protection |  | MPDU Decryption and Integrity Check | 
 | (null) |  | Duplicate Removal | 
 | (null) |  | BA (delayed) | 
MAC-L | TX1 | TX2 | RX1 | RX2
 | (null) | (null) | HARQ-ACK/NACK, ACK, BA | HARQ-ACK/NACK, ACK, BA
 | (null) | (null) | Address Filtering | Address Filtering
 | MPDU Header + CRC Creation | MPDU Header + CRC Creation | MPDU Header + CRC Validation | MPDU Header + CRC Validation
 | MPDU Aggregation | MPDU Aggregation | MPDU De-aggregation | MPDU De-aggregation

## Slide 10: Unified ML and MAP Framework
Special Functions of AP MLD Group
  AP MLD group formation
    Select an AP MLD (i.e. the master or coordinator) with affiliated MLD AP(s) to form the AP MLD group for non-AP MLD(s)
    Establish the multi links between the AP MLD group and a non-AP MLD based on the service category of the traffic, RSSI measurement, etc. and link delay measurement.
    Timing synchronization among the AP MLD and its affiliated AP MLD(s) for the coordinated AP MLD transmissions.
  Multi AP MLD transmissions
    Acquire CSI information from the AP MLD group
    Determine the transmission type of AP MLD group
      joint MLD AP DL transmission, i.e. multi AP MLDs transmit the same PPDU at same time.
      coordinated ML transmission, i.e. coordinated multi AP MLDs beamforming, OFDMA or SR.
    Invoke the multi AP MLD transmission from the AP MLD group to the MLD STA

## Slide 11: Summary
In this contribution, we
  Discussed the issue in the reference model to support both multi-AP and multi-link features.
  Proposed a framework of unified ML and MAP reference model for 802.11be.

## Slide 12: Straw Polls
SP1
  An AP MLD instance is a logical device that has one or more affiliated STAs, where each STA affiliated with the MLD is an AP. The MLD AP instance has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
  An AP MLD forms a MLD Service Set, i.e. MLD-SS, with an identifier of MLD-SSID.
  Note: the name could be determined and changed later.
SP2
  Affiliated AP MLD instance is a logical device of AP with a collaborated link to an AP MLD instance without a direct MAC data service interface and primitives to the LLC, and a single address associated with the interface to communicate on the DSM.
  The AP MLD instance and affiliated AP MLD instance(s) form an AP MLD group.
  An AP MLD group creates a MLD Group Service Set, i.e. MLD-GSS, with an identifier of MLD-GSSID.
  Note: the name could be determined and changed later.

## Slide 13: References
11-19-0823-02-00be-multi-link-aggregation
11-19-0773-05-00be-multi-link-operation-framework
11-19-1451-01-00be-virtual-bss-for-multi-ap-coordination-follow-up
11-19-1616-01-00be-multi-ap-group-formation
11-19-1588-00-00be-multi-ap-backhaul-analysis

## Slide 14
Thank you!