## Slide 1
Authors:
Multi-Link Communication Mode Discussion
Date: 2020-01-11
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | sun.bo1@zte.com.cn
Nan Li | ZTE |  |  | li.nan25@zte.com.cn
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution proposes the definition of multi-link communication mode.

## Slide 3: Introduction
Multi-Link framework requirements
  ML framework requirements are proposed to support
    Dynamic selecting and switching an operating link to address the use cases of reducing access latency for fast connection, balancing loads, etc..
    Concurrent transmit or receive packets over multiple links to address the use cases of improving transmission reliability and increasing peak-throughput.
  In SFD, only one capability of MLD is described as
    A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
      NOTE 1 – The 2 links are on different channels.
      NOTE 2 – Whether to define a capability of announcing the support transmission on one link concurrent with transmission on the other link is TBD.
    But it misses the definition of multi-link communication modes.

## Slide 4: Introduction
  Definitions of communications in industry [1, 2, 3]
  Simplex communication: a communication channel that operates in one direction at a time, but that may be reversible.
  Half Duplex communication: a communication channel can operate in both directions, but only one direction at a time (not simultaneously).
  Full Duplex communication: a duplex communication channel requires two simplex channels operating in opposite directions.
  We suggest to follow the terms used in the communication industries to define multi-link operation modes.

## Slide 5: ML Communication Mode Definition
  ML Simplex Mode
  A MLD can transmit on one or more links, or receive on one or more links, but not transmit and receive concurrently.
ML Duplex Mode
  A MLD can transmit on one or more links concurrently with receiving on other link(s).

## Slide 6: Straw Poll
Do you support to define ML communication mode as follows ?
  ML Simplex Mode: A MLD can transmit on one or more links, or receive on one or more links, but not transmit and receive concurrently.
  ML Duplex Mode: A MLD can transmit on one or more links concurrently with receiving on other link(s).
YES/NO/ABS

## Slide 7: References
The IEEE Authoritative Dictionary of Standard Terms, 7th Ed., 2000, Inst. of Electrical and Electronic Engineers, p.1053
https://en.wikipedia.org/wiki/Simplex_communication
https://en.wikipedia.org/wiki/Duplex_(telecommunications)

## Slide 8
Thank you!