## Slide 1
Authors:
Multi-Link Power Saving Discussion
Date: 2020-01-11
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Nan Li | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution follows up the discussion of EHT multi-link communication to support low latency, high reliability and high throughput applications, and discusses the issue of power consumption in ML operation. It also proposes a possible approach for establishing an anchored link for ML power saving operation.

## Slide 3: Introduction
Multi-Link framework requirements
  In [1], it proposed the ML framework requirements
    Dynamic selecting and switching an operating link to address the use cases of reducing access latency for fast connection, balancing loads, etc..
    Concurrent transmit or receive packets over multiple links to address the use cases of improving transmission reliability and increasing peak-throughput.
    Utilizing multi-link efficiently for power saving especially for stations.
Power consumption issue
  In [2], it summaries power consumption of 802.11ax devices (single link)
    the power consumption in the idle mode is 50mA, 60mA and 75mA for bandwidth 20MHz, 40MHz and 80MHz, respectively.
    the power consumption of receiving mode is 100mA, 140mA and 200mA for bandwidth 20MHz, 40MHz and 80MHz, respectively.
  In ML operation, the power consumption could be multiple times of a single link’s when multiple links are turned on in idle state. Therefore a mechanism is required to address the power consumption issue in ML operation.

## Slide 4: MLD Power Saving Proposal
  Principle
  In MLD active operation mode, at least one link of MLs is enabled and in active state when
    AP MLD and Non-AP MLD has data to transmit, or
    The non-AP MLD receives from the AP MLD a message for establishing ML operation.
  In MLD power saving operation mode
    Select only one link of ML as the anchored link in idle state for non-AP MLD, and turn off other links for power saving.
    Apply the existing power saving mechanisms (like TIM, etc.) defined in 802.11 to the anchored link to further save the power consumption.

## Slide 5: MLD Power Saving Proposal
  MLD Power Saving Operation Setup
  AP MLD assigned anchored link:
    AP MLD may indicate one or more anchored links for the MLD power saving operation in Beacon frame or other management frames.
  Non-AP MLD requested anchored link:
    AP MLD announces ML information in the Beacon frame
    The non-AP MLD selects one link as the anchored link in MLD PS operation
      NOTE: A Non-AP MLD may notify the anchored link selection to the AP MLD.

## Slide 6: MLD Power Saving Proposal
  MLD Operation Modes
  MLD Active Operation (MLD-AO):
    Non-AP MLD enables one or more links based on the need of ML Operation.
  MLD Power Saving Operation (MLD-PSO):
    Non-AP MLD only enables the anchored link and disables other links.
  A MLD can switch its mode between MLD-AO and MLD-PSO
  Switching Anchored Link
  A MLD (either AP or non-AP) may switch the anchored link for MLD power saving operation when some case happens
    such as for load balance or interference avoidance.
  A MLD may include a new anchored link information for the ML power saving operation in ML switching message exchange.

## Slide 7: MLD Power Saving Proposal
  Non-AP MLD Link State
  Non-AP MLD maintains the state of each link of ML.
    Link-Disabled: This link is disabled for any activity.
    Link-Enabled: This link is in either MLD active operation or MLD power saving operation
      Link-Active: This link is in MLD active operation. The non-AP MLD can receive and/or transmit frames over this link at anytime.
      Link-Awake: This link is in MLD power saving operation. The non-AP MLD can listen the transmission on this link, but not transmit.
      Link-Doze: This link is in sleep for power saving. The non-AP MLD does not listen or transmit on the link.
Link-Active
Link-Awake
Link Disabled
Link-Doze
Power Saving
Link Enabled

## Slide 8: MLD Power Saving Proposal
  ML UL transmission
  Non-AP MLD in MLD-PSO mode can activate one or more non-anchored links at anytime for UL transmissions, i.e. transit the anchored link and/or non-anchored links to the active state for UL transmissions.
ML DL transmission
  AP MDL may send Beacon frames with wake-up indication over the anchored link to wake-up a non-AP MLD in MLD-PSO mode.
  The non-AP MLD in MLD-PSO mode will activate the indicated non-anchored link(s) after receiving the Beacon frame, i.e. transit the anchored link and/or non-anchored links to the active state for receiving frames from the AP MLD.

## Slide 9: Summary
In this contribution, we discuss
  Power consumption issues in ML operation
  A possible approach to address the power consumption on ML operation.

## Slide 10: Straw Poll
SP1
  Do you support to define MLD power saving operation ?
  SP2
  Do you support to define an anchored link in MLD power saving operation?
  SP3
  Do you support to define the link state ?

## Slide 11: References
11-19-1095-00-00be-multi-link-requirement-discussion
11-14-0980-16-00ax-simulation-scenarios

## Slide 12
Thank you!