## Slide 1: Synchronous Transmitter Medium State Information
Date: 2020-01-09
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Notes: November 2012

## Slide 2: Abstract
EHT non-AP STA devices will have operating States with restrictions on TX and RX behavior
  E.g. Simultaneous TX/RX might be restricted for certain link channel combinations for non-AP STA aka Non-STR (NSTR)
When an NSTR STA starts a TX on one Link1, medium state of Link2 is lost
  Due to NEXT (Near End Cross Talk)
Need a mechanism to maintain Link2 medium state during Link1 TX operation
Propose that Link1 TX recipient supplies Link2 medium state information

## Slide 3: Synchronous Transmitter EDCA Problem
STA1 non-AP NSTR STA is the first TXOP winner
  STA1 begins TX on Link1 to STAw
STAx attempts transmission to STAw during STA1 Link1 TX
  STA1 Link1 TX NEXT causes RX failure at STA1 Link2
At end of TX on Link1, STA1 identifies Link2 as IDLE
  Unless TX on Link2 > -62 at STA1 location
    Actually, no rule yet on STA1 Link2 CCA sensitivity during Link1 TX!
  STA1 Link2 Backoff quickly resumes and hits 0, STA1 TX on Link2 to STAw causes existing Link2 PPDU failures
E.g. STAw == AP
RA=STAw, TA=STA1
LINK1
RA=STAw, TA=STAx
LINK2
BA
R
C
RED is STA1 TX, other colors are STA1 RX
BA
R
R
R
Potential Loss of MPDUs at STAw
Potential Loss of MPDUs at STAx
R
C
STA1 EDCA DEAF
STA1 EDCA Resumes

## Slide 4: Link2 Medium State Information
MSI = Medium State Information
AP knows that Link1 transmitter STA1 is NSTR STA
  Maybe include bit in PHY header so that AP does not have to look it up
AP is STR
  Could be any STR device, e.g. non-AP
AP provides medium state information for Link2 to STA1 in the response to STA1 TX to AP
  AP provides:
    Duration/End time of concurrent Link2 PPDU
    Duration/End time of concurrent Link2 NAV

## Slide 5: MSI Conveyance
E.g. a new PPDU
  Built to hold this information
E.g. a Null DATA PPDU with A-control field value
E.g. within a PHY Header field
Not restricted to AP providing information to non-AP STA
  Any recipient of a PPDU transmitted by an NSTR STA
  Even if the recipient is also an NSTR STA
    Because that recipient is not performing TX, so it has Link2 MSI

## Slide 6: Synchronous Transmitter EDCA Fixed
L2 EDCA HOLD
STA1 receives MSI with BA on Link1
  STA1 cannot declare Link2 IDLE until it has MSI information
  STA1 Link2 deafness disappears at end of STA1 TX PPDU
  STA1 MSI information is determined at end of STA1 RX PPDU BA+MSI
  STA1 must suspend EDCA until MSI information is available at the end of RX PPDU BA+MSI
    i.e. L2 EDCA HOLD as shown in the diagram
STA1 uses MSI to adjust Link2 Medium State
  E.g. set CRS, set NAV for Link2
  Subsequent operation is per normal EDCA
RA=STAw, TA=STA1
LINK1
RA=STAw, TA=STAx
LINK2
BA+MSI
R
C
RED is STA1 TX, other colors are STA1 RX
BA
R
R
C
RA=STAw, TA=STA1
BA+MSI
C
STA1 EDCA DEAF

## Slide 7: MSI Wait Time
Because MSI information is in the response frame
  It is not available when the Link2 deafness first disappears
  If Link2 is IDLE, then STA1 is performing unnecessary EDCA hold
    I.e. as long as MSI is not yet available
Can include a Link2 IDLE indication in the PHY header
  When, per the information obtained at the BA transmitter location, Link2 is IDLE at the end time of the Link1 PPDU, the Link2 IDLE indication can be asserted in the PHY Header of BA+MSI
  This information is available much earlier in the RX PPDU
  Reduces the wait time for Link2 EDCA resynchronization

## Slide 8: MSI Time in PHY Header
Could transform the Link IDLE information into a full wait time
  I.e. simply put the Link2 BUSY duration in the PHY header of the response frame
  Value of 0 indicates Link2 IDLE
  Non-zero value is equivalent of supplying PPDU Length and/or DUR NAV value
  I.e. equivalent of a PHY header TXOP value for another link
  I.e. equivalent of PHY header MSI, or a subset of that MSI

## Slide 9: MSI Frame as an MPDU (1)
  MSI Control
    Includes a bitmap that indicates the presence and absence of Medium State Information per link
    A “1” in the bitmap indicates that MSI is present for the link with LinkID corresponding to the position of the bit in the bitmap
    A “0” indicates that MSI is not present for the corresponding link
  MSI Block contains N copies of Per Link MSI
    Where N is equal to the number of bits in the MSI Control bitmap that are equal to “1”
    The Per Link MSI fields that are present are arranged in ascending order of LinkID
MSI Block
FC
LINK1
MSI Control
DUR
RA
TA
FCS

## Slide 10: MSI Frame as an MPDU (2)
  Per Link MSI
    May contain three subfields
      MSI_NAV_INTRA
        The predicted value of the Intra NAV of the MSI MPDU transmitter for the corresponding link, at the end of the last symbol of the PPDU that carries the MSI MPDU
      MSI_NAV_BASIC
        The predicted value of the Basic NAV of the MSI MPDU transmitter for the corresponding link, at the end of the last symbol of the PPDU that carries the MSI MPDU
      MSI_LEN
        The predicted value at the transmitter of the MSI MPDU, of a counter that counts down a PHY LENGTH field value following the reception of a valid PHY Header containing PHY LENGTH field information, for the corresponding link
          i.e. remaining PHY LENGTH value at the MSI transmitter for the specified link at the end of the PPDU carrying the MSI

## Slide 11: MSI Frame as an MPDU (3)
  Options:
  The subfields all have an unsigned positive value, with a minimum value of 0
    Values may be expressed in microseconds or some larger unit of time
  The subfields may have positive or negative values, where
    A positive value indicates the time in the future, starting from the end of the PPDU that contains the MSI, when the indicated medium state variable is expected to change from BUSY to IDLE
    A negative value indicates the time at which the indicated medium state was expected to have changed from BUSY to IDLE previous to the end of the PPDU

## Slide 12: MSI In the PHY Header
The PHY Header may contain bits to indicate MSI IDLE, per link
  For example, one bit per Link that indicates MSI IDLE or BUSY
    If this bit indicates BUSY for the link, then the receiving MLD should examine received MPDUs in the same PPDU for more detailed information, e.g. MSI_NAV_BASIC, MSI_NAV_INTRA, MSI_LEN
    E.g. a “1” indicates IDLE
The PHY Header may contain more complete MSI fields, per link
  E.g. MSI_NAV_BASIC, MSI_NAV_INTRA, MSI_LEN as described in the MSI frame
  Note: an IDLE State is indicated by all fields having a value of 0

## Slide 13: MSI Receiver Behavior (1)
An NSTR MLD shall:
  During transmission on a link, suspend EDCA operation on any other link on which the MLD is unable to assess the medium State according to the performance requirements of receiver minimum sensitivity
    Suspend EDCA means to act as though the affected link is experiencing a medium BUSY State

## Slide 14: MSI Receiver Behavior (2)
MSI Receiver MSI_LEN Counter
An NSTR MLD shall
  Support MSI exchange
  Implement an MSI_LEN counter for each operating link
    The MSI_LEN counter for a link shall be set to the value of the received MSI_LEN field for that link and shall count down the appropriate units of time beginning at the end of the last symbol of the received PPDU which contained the MSI_LEN field

## Slide 15: MSI Receiver Behavior (3)
An NSTR STA that receives MSI for a specific link, shall, for that link:
  Replace the Intra NAV counter value with the received MSI_NAV_INTRA value after appropriate scaling, if the scaled received value is greater than the Intra NAV value at the time of the end of the last symbol of the PPDU that contained the MSI MPDU
  Replace the Basic NAV counter value with the received MSI_NAV_BASIC value after appropriate scaling, if the scaled received value is greater than the Basic NAV value at the time of the end of the last symbol of the PPDU that contained the MSI MPDU

## Slide 16: MSI Receiver Behavior (4)
Subsequent to a transmission by an MLD on a link that required EDCA to be suspended on another link, the NSTR MLD may resume EDCA operation on the links on which it was suspended
    1. At the end of a valid PHY signal field of a PPDU received on the link on which it was previously transmitting, when the received PHY signal field contains MSI indication for the suspended link
      Either full MSI information or an indication that the suspended link is IDLE
    2. At the end of the last symbol of a PPDU received on the link on which it was previously transmitting, when the received PPDU contained an MPDU that contained MSI for the suspended link
    3. At any time after the end of the transmission, if it receives any valid PPDU PHY Header on the suspended link

## Slide 17: MSI Receiver Behavior (5)
If an MSI parameter for a link is received with a negative value in a PPDU, then
  The NSTR STA that is the recipient of the MSI may perform an adjustment to its backoff process on the affected link
    E.g. the backoff should be calculated at the end of the receipt of the PPDU containing the MSI, assuming that the magnitude of the negative value of the parameter is effectively that amount of IDLE time that has passed previous to the end of the PPDU
      For example, if all MSI parameters indicate either 0 or a negative value, then at the end of the receipt of the PPDU, the recipient determines the earliest time, backwards from the end of the PPDU, at which all parameters had reached zero, representing a sum IDLE indication for the link, and the amount of time from that point forward in time to the end of the PPDU is an amount of time considered IDLE for that link which can be used to determine the current state of the EDCA for that link,

## Slide 18: MSI Receiver Behavior (6)
      Assuming that the EDCA for that link had resumed operation at the time when the link was determined to be IDLE
      E.g. if the earliest time from the end of the PPDU that was determined to be IDLE according to the values:
        MSI_INTRA_NAV == -70
        MSI_BASIC_NAV == -140
        MSI_LEN == -110
        Then the earliest IDLE backwards in time from the end of the received PPDU containing the MSI information is 70 usec from the end of the PPDU
        The recipient can then adjust the backoff process(es) to account for the fact that 70 usec of IDLE medium has elapsed previous to the end of the PPDU reception
        If the result of the adjustment is that an existing backoff function for the link would have reached 0 before the end of the received PPDU, then the recipient may perform the following steps

## Slide 19: MSI Receiver Behavior (7)
      Examine the current medium condition
        Using ED and Preamble detect
          For a period of one SLOT
        If the medium is IDLE, then the recipient may initiate a transmission
        If the medium is BUSY, then the recipient should restart each expired backoff function by choosing a new backoff number either:
          Randomly
          OR
          By using the number that is equal to the number of backoff slots between the calculated IDLE medium start time and the end of the received PPDU
            This number is potentially different for each backoff function due to potential differences in the value of AIFSN for each backoff function

## Slide 20: MSI Receiver Behavior (8)
Subsequent to a transmission by an NSTR MLD on a link (e.g. Link1) that required EDCA to be suspended on another link (e.g. Link2), the MLD
  Shall perform EIFS on Link2 starting from the zero time point of the time value determined from the MSI_LEN value, if the MSI included MSI_LEN information for Link2
    Note that the MSI_LEN zero point might be in the past
    I.e. MSI_LEN might have a negative value

## Slide 21: Synch Transmitter Indication
An NSTR STA transmitter indication should be included in the PHY header of a PPDU
  So that the recipient of such a PPDU can prepare MSI to be included in the response
  The indication in the PHY Header could be a single bit that indicates that the PPDU transmitter is an NSTR STA

## Slide 22: Straw poll 0
Do you support the inclusion of the following in the SFD:
  802.11be shall include a mechanism for the exchange of Medium State Information and rules for the use of that information by an NSTR STA
  YES
  NO
  ABS

## Slide 23: Straw poll 1
Do you support the creation of a new frame for conveying other link Medium State Information?
  YES
  NO
  ABS

## Slide 24: Straw poll 2
Do you support the creation of a new A-control subfield for conveying other link Medium State Information?
  YES
  NO
  ABS

## Slide 25: Straw poll 3
Do you support the creation of a (set of) link IDLE indication(s) to be added to the PHY header?
  i.e. set == set of links
  YES
  NO
  ABS

## Slide 26: Straw poll 4
Do you support the insertion of a TXOP-like value in a PHY header to indicate TXOP information for another link?
  I.e. a link other than the one on which the PPDU appears
  i.e. possibly PHY LEN information, NAV information
  YES
  NO
  ABS

## Slide 27: Straw Poll 5
Do you support that an NSTR MLD shall support MSI information exchange and the rules for reception of MSI?
  YES
  NO
  ABS

## Slide 28: Straw Poll 6
Do you support that an NSTR MLD shall indicate that it is NSTR in a signaling bit within the PHY header of PPDUs that it transmits?
  YES
  NO
  ABS

## Slide 29: Reference
[1] Draft P802.11REVmd_D3.0
[2] Draft P802.11ax_D5.0