## Slide 1: Multi-Link Power Save - Link Bitmap
Date: 2020-1-9
Authors:

## Slide 2: Abstract
In this presentation, we propose a method to extend legacy power save operations to multi-link operation for 802.11be

## Slide 3: Power management mode transition for a single link
The PM bit in the Frame Control field is used to indicate the power management of a non-AP STA
  PM bit = 0  Active mode (power state of the STA is awake state)
  PM bit = 1  Power save mode (power state of the STA is either awake or doze state)
Link 1
time
: Awake
: Doze
: Data frame
(incl. null-data)
d
d
AP 1
STA 1
a
a
a
: Ack frame
PM=1
STA1
AP1
PM=0
d
Active mode
Active mode
PS mode

## Slide 4: Power management mode transition for multi-link operation
Propose to define a link bitmap in a frame that indicates links to which the PM bit applies
  Link bitmap = (Link 1, Link 2, …, Link n)
Link 1
time
: Awake
: Doze
: Data frame
(incl. null-data)
d
d
AP 1
STA 1
a
a
a
: Ack frame
PM=1
STA1
AP1
PM=0
d
Link 2
time
d
AP 2
STA 2
a
a
PM=1
STA2
AP2
PM=0
d
Active mode
Active mode
PS mode
AP MLD
Non-AP MLD
Active mode
Active mode
PS mode
a
PM=1 Link Bitmap = (1,1)
d
PS mode
PS mode
a
PM=0 Link Bitmap = (1,1)
d
Active mode
Active mode
: Link bitmap included in the frame
STA1 and STA2 enter PS mode
STA1 and STA2 enter Active mode
PM bit applies to Link 1 and Link 2

## Slide 5: U-APSD operation for multi-link operation
Link bitmap in a U-APSD trigger frame indicates links on which STAs are awake
Link bitmap in a data frame from the AP indicates links to which the EOSP bit applies
: Awake
: Doze
: Data frame
(incl. null-data)
d
AP 1
STA 1
a
: Ack frame
AP 2
STA 2
AP MLD
Non-AP MLD
: Link bitmap included in the frame
Link 1
t
d
a
a
EOSP=1 More Data (MD)=0
STA1
AP1
Trigger frame applies to Link 1 – indicates STA1 is awake
EOSP applies to Link 1
time
STA2
AP2
t
d
a
a
EOSP=1 MD=0
Trigger frame applies to Link 2 – indicates STA2 is awake
EOSP only applies to Link 2
t
: U-APSD trigger frame
d
a
a
Link bitmap = (1,1)
EOSP=0 MD=1
EOSP
Trigger frame applies to both Link 1 and Link 2 – indicates STA1 and STA2 are awake
EOSP = 1 applies to both Link 1 and Link 2 – indicates the end of SPs on Link 1 and Link 2
a
EOSP=1 MD=0
d
a
EOSP=0 MD=1
d
t
Link bitmap = (1,1)
Link 2

## Slide 6: Returning to a link that is fully managed by AP
STA 2 sends a frame with the link bitmap = (1 , 0) on Link 2 that doesn’t need to wait for a Trigger frame and quickly return to Link 1 that is fully managed by the AP with Trigger frame for UL
: Awake
: Doze
: Data frame
(incl. null-data)
d
AP 1
STA 1
a
: Ack frame
AP 2
STA 2
AP MLD
Non-AP MLD
: Link bitmap included in the frame
Link 1
T
AP1
time
STA2
AP2
t
d
a
a
EOSP=1 MD=0
- Link bitmap indicates STA1 will be in Active mode and awake on Link 1 after this frame exchange
- This frame doesn’t affect the operation of STA2 on Link 2; STA2 remains in the PS mode
t
: U-APSD trigger frame
Link bitmap = (1,0)
PM=0
Link 2
STA1
T
T
d
a
Active mode
Trigger frame
d
a
T
Trigger frame

## Slide 7: TWT operation for multi-link operation
Link bitmap in a U-APSD trigger frame indicates links on which STAs are awake
Link bitmap in a data frame from the AP indicates links to which the EOSP bit applies
: Awake
: Doze
: Data frame
(incl. null-data)
d
a
: Ack frame
: Link bitmap included in the frame
Link 1
STA1
AP1
time
STA2
AP2
t
: U-APSD trigger frame
d
a
a
Link bitmap = (1,1)
EOSP=1 MD=0
Trigger frame applies to both Link 1 and Link 2 – indicates STA1 and STA2 are awake
d
a
EOSP=1 MD=0
t
Link 2
TWT SP
AP 1
STA 1
AP 2
STA 2
AP MLD
Non-AP MLD
Link 1
STA1
AP1
time
STA2
AP2
d
a
a
EOSP=1 MD=0
d
a
EOSP=1 MD=0
t
Link 2
TWT1 SP
a
t
Trigger frame applies to Link 1 – indicates STA1 is awake
Trigger frame applies to Link 2 – indicates STA2 is awake
TWT2 SP
AP 1
AP 2
AP MLD
STA 1
STA 2
Non-AP MLD
Each STA has its own TWT schedule
Both STA1 and STA2 have a same TWT schedule
T
T
Trigger frame

## Slide 8: Proposed Multi-link Power Save Control subfield in the A-Control subfield
Define a new Control subfield in the A-Control field
  Multi-link Power Save (MLPS) Control subfield
MLPS Control field contains
  Link Bitmap Size subfield: TBD (e.g. 2-bit)
    E.g.: 2, 4, 8, 16 bits to indicate 2-16 links
  Link Bitmap: each bit is mapped to each link
    Link bitmap = (Link1, Link2, …, Link M)
    n-th bit of the Link Bitmap represents Link n
    When n-th bit is set to 1, the PM bit, U-APSD trigger frame (non-AP STA to AP), and the EOSP bit (AP to the non-AP STA) apply to Link n and to the STA associated to Link n; otherwise set to 0.
Link Bitmap
Link Bitmap Size
TBD (2-16)
TBD (8-22 bits)
TBD (2)
MLPS Control subfield
Control ID
(MLPS)
4
reserved
Bit:

## Slide 9: Straw Poll
Do you agree with the following?
Between a non-AP MLD and an AP MLD, a STA may transmit a frame to an AP to indicate the transition to awake state of other STA(s) of the non-AP MLD - Optional for both AP and non-AP