## Slide 1: Opportunistic Implicit Channel Sounding
Date: 2020-1-11
Authors:

## Slide 2: Introduction
Explicit BF Feedback:
  BF Feedback Overhead esp in case of higher number of antennas/higher number of STAs, and Multi-AP
  Quantization/Compression impact
  Channel aging/Feedback delay
Implicit channel sounding may result:
  Lower network overhead/ Less Latency as there is no BF feedback transmission.
  No quantization/compression impact as BF weights are calculated directly from channel.
  Efficient DL Multiuser (MU) BF, MU scheduling, power control

## Slide 3: Introduction
In [1, 2, 3], feasibility of AP calibration to enable implicit sounding are discussed.
In [4, 5], Precoding performance and network overhead analysis for implicit feedback are
presented.
In [4] a Trigger-based scheme was presented for enabling Implicit Channel Sounding in 802.11be.
  AP transmits a trigger frame, to trigger one or multiple STAs, to send NDP in uplink.
  The STAs are directed to be multiplexed in spatial/ frequency/ time domain.
  Upon receiving NDP from the STA(s), AP will directly calculate BF weights and transmit data.
In this contribution, opportunistic implicit sounding is discussed for high traffic STAs.
Uplink data traffic can be leveraged to extract channel information.

## Slide 4: Opportunistic Uplink Channel Sounding
  Option A - UL TB Block ACK transmission
    Trigger frame type-2 is adopted in 802.11ax to trigger multi-user Block ACK responses from multiple STAs within an HE UL MU frame.
    AP should configure relevant parameters such as LTF type, number of HE-LTF symbols as well as MU-MIMO LTF mode in Common Info subfield of the Trigger frame.
    For full channel sounding on each STA, AP will set the number of HE-LTF symbols in Common Info field to the maximum number of antennas supported by all of the solicited STAs to enable full MIMO channel sounding.

## Slide 5: Opportunistic Uplink Channel Sounding
  Option B - Trigger-based (TB) UL MU PPDU:
    For the purpose of UL channel sounding, the AP indicates the number of HE-LTF symbols to be transmitted from each STA, in the “Number Of HE-LTF Symbols And Mid-amble Periodicity (B23-25)” subfield of the Common Info field of a Trigger frame (type 0, Basic).
    HE-LTFs which are overlapping from multiple STAs in the same RU are multiplexed by Matrix-P. The spatial index for each STA is also defined in User Info field of the Trigger frame.
    Even if the STA is transmitting single data stream, AP will set the number of HE-LTF symbols to the maximum number of STA’s transmit antennas for UL MIMO channel sounding.
    No spatial expansion (SE) at STA even if transmitting one spatial stream

## Slide 6: Opportunistic Uplink Channel Sounding
  Option C - High-Efficiency (HE) UL single-user (SU) PPDU:
    The AP which requires MIMO UL channel sounding, may indicate the number of required HE-LTF symbols in HE UL SU PPDU transmissions in Operating Mode (OM) Control field indication (OMI).
    This can be done by defining a new subfield (e.g., “NHE-LTF for Implicit Sounding”) in OM Control field.
    The STA which receives the above OMI indicating implicit sounding with the required number of HE-LTF symbols, will set the number of HE-LTF symbols to the minimum of the number indicated in the “NHE-LTF for Implicit Sounding” subfield of the OM Control field, and number of STA’s transmit antennas.
    In HE SU PPDU, a 2-bits subfield is defined in HE-SIG-A to indicate NHE-LTF transmitted by the STA in the UL. For example, even if STA is transmitting single stream, if the “NHE-LTF for Implicit Sounding” subfield is set to 4 (in OMI), 4 HE-LTF symbols may be transmitted in HE SU.

## Slide 7: Conclusion
Options for enabling opportunistic implicit channel sounding are discussed.
For STAs with high traffic, uplink block ACK or UL MU PPDU /UL SU PPDU may be leveraged for opportunistic channel sounding in uplink.
If the dimensionality of MIMO channel is larger than the number of HE-LTFs, AP should configure number of HE-LTF symbols for full MIMO channel sounding even if the STA is transmitting single stream.
No SE at STA even if transmitting one spatial stream

## Slide 8: References
[1]: IEEE802.11-19/0767r1, Implicit Channel Sounding in IEEE 802.11 (Feasibility Study)
[2]: IEEE802.11-19/1939r0, Calibration of Implicit Sounding
[3]: IEEE 802.11-20/0080, Calibration for Implicit Feedback
[4]: IEEE 802.11-19/0768r0, Implicit Channel Sounding in IEEE 802.11
[5]: IEEE802.11-19/1934r0, Precoding perf. using implicit channel estimation