## Slide 1: Multi-AP Implicit Channel Sounding
Date: 2020-1-11

## Slide 2: Introduction
Multi-AP Transmission
Multi-AP Channel sounding is required to provide channel information from OBSS STAs.
  In Joint BF, the channel information from each STA to all APs is required to calculate BF vectors for data transmission
  In Collaborative BF (CBF), each AP requires channel information from OBSS STAs for the sake of interference cancellation and scheduling.
Both Implicit and Explicit Sounding are considered.
In Explicit Sounding, network overhead and channel aging can be a serious concern.
In Multi-AP, more frequent sounding may be required (to be evaluated)
In [1, 2], we presented arguments to define implicit feedback in 802.11be.
Implicit sounding should be defined for all new modes in .11be.
In this contribution, some details of Multi-AP sounding is presented.
Interference channel

## Slide 3: Implicit Sounding
In Multi-AP scenario, master and/or slave AP may need to trigger/schedule OBSS STAs (beside in-BSS STAs) for uplink NDP transmission.
The sequence for trigger-based implicit sounding has two key design parts:
  Trigger frame transmission from multiple AP
  NDP Transmission from OBSS STAs
Two modes can be considered:
  Centralized, controlled by initiator (Master) AP
  Sequential where APs in coordinated set sequentially trigger the STAs for NDP transmission
Both modes can be utilized for both CBF and JBF.

## Slide 4: Multi-AP Implicit Sounding
Mode 1: Centralized
  The initiator (Coordinate) AP sends a trigger frame which includes all APs IDs in coordinated set, and user info for its own STAs and all other STAs in OBSS
  The STAs will be directed to be multiplexed in time/frequency/ space for NDP transmission
    User Info in Trigger Frame: AID, RU on which NDP will be transmitted, Multiplexing type for MU NDP, HE LTF type for NDP, Number of STA’s antennas to transmit sounding
  The STAs will send NDP as directed in Trigger frame, SIFS time after receiving Trigger frame.
  If STA is triggered to participate in implicit feedback, no precoding is applied over multiple transmit antennas.
  UL TB NDP PPDU: The format is the same as UL TB PPDU, but without data payload.

## Slide 5: Multi-AP Implicit Sounding
Upon NDP transmission from each STA in UL, all APs in coordinated set will be able to measure the channel for that STA.
Multiplexed in
Time/ Frequency/ Space
AP-1
AP-2
SIFS
UL NDP
SIFS
UL Sounding Trigger
UL NDP
M-AP
Trigger
Data
Data

## Slide 6: Multi-AP Implicit Sounding
A solution is required for the case all STAs may not necessarily hear master AP.
  In this case, the same trigger frame may be sent from all APs
  The initiator AP is required to trigger this process by sending a M-AP trigger frame to initiate and synchronize APs and identify AP/ STAs IDs
Multiplexed in
Time/ Frequency/ Space
AP-1
AP-2
SIFS
UL NDP
SIFS
SIFS
UL Sounding Trigger
UL Sounding Trigger
UL NDP
M-AP
Trigger
Data
Data

## Slide 7: Multi-AP Implicit Sounding
Mode 2: Sequential
  APs in coordinated set will sequentially trigger the transmission of UL NDPs
  The first Trigger frame transmitted by Initiator AP may identify IDs for APs (in coordinated set), sequential ordering for performing the uplink sounding, user info for its own STAs and all OBSS STAs and the detailed allocation of time/code/tone for each STA.
    This is to inform other APs in coordinated set on the RU each user may send NDP.
  Trigger frames transmitted from slave APs may only carry user info for its own STAs.
AP-1
Trigger Frame
SIFS
AP- k
M-AP
Trigger
Data
Data
Trigger
Frame
SIFS
UL NDP
STAs-k
Multiplexed in Time/ Frequency/Space

## Slide 8: Multi-AP Implicit Sounding
If all APs can hear each other, the first trigger frame/master AP may only carry AP IDs and user info for its own STAs.
The sequential mode can be also used for the purpose of JBF.
When each STA transmits NDP in uplink, each AP in coordinated set is able to measure the channel.
  In JBF, the channels measured by all APs should be sent to the master AP/ central processor for JBF vector calculation
  In CBF, each AP individually will process the channel data and calculates the BF vectors.
  This is true for both modes of central and sequential modes.

## Slide 9: Network overhead: Explicit vs Implicit Feedback
Network Overhead: In implicit sounding, the NDP transmission (STA) contribute to overhead but there is no feedback mechanism while in explicit beside NDP transmission, BF feedback reports add to the overhead.
An example of Explicit sounding is given in Appendix:
  Overhead=Trigger+NDPA+NDP+BF Reports
An approximated overhead calculation is provided for implicit and explicit sounding for CBF as well as single AP.
Overhead 4-antennas AP MCS=1 /2/ 4 | Single AP/ Two STA Explicit | CBF: 2 AP/ 4 STA Explicit | CBF: 2 AP/ 4 STA Implicit | CBF: 3 AP/ 4 STA Explicit | CBF: 3 AP/ 4 STA Implicit
Sounding Duration (msec) | .75/ .53/ .4 | 1.7/ 1.3/ .9 | .24 | 2.5/ 1.9/ 1.3 | .29
Overhead 8-antennas AP MCS=1/ 2/ 4 | Single AP/ 4 STA (2 ss) Explicit | CBF: 2 AP/ 8 STA (1 ss) Explicit | CBF: 2 AP/ 8 STA Implicit | CBF: 3 AP/ 8 STA (1 ss) Explicit | CBF: 3 AP/ 8 STA Implicit
Sounding Duration (msec) | 2.7/ 1.8/ 1.1 | 6.2/ 4.2/ 2.6 | .33 | 9.2/ 6.3/ 3.8 | .38
Explicit/Implicit BF Feedback Overhead for 4/8-antennas AP, BW=80 MHz, MCS=1/2/4, Ng=4

## Slide 10: Network overhead: JBF
Approximate network overhead calculation for Explicit vs Implicit Feedback
Overhead 4-antennas AP MCS=1/ 2/ 4 | JBF: 2 AP/ 3 STA (2 ss) Explicit | JBF: 2 AP/ 8 STA (2 ss) Explicit | JBF: 4 AP/ 6 STA (2 ss) Explicit | JBF: 4 AP/ 10 STA (2 ss) Explicit | JBF: 4 AP/ 10 STA (2 ss) Implicit
Sounding Duration (msec) | 2.1/ 1.5/ .9 | 5.3/ 3.5/ 2 | 8.6/ 6/ 3 | 14/ 9/ 5 | .5
Explicit/Implicit BF Feedback Overhead for 4/8-antennas AP, BW=80 MHz, Ng=4

## Slide 11: Conclusion:
Multi-AP Implicit Sounding is discussed.
Network overhead is evaluated considering both implicit and explicit sounding.
Implicit sounding significantly reduces the network overhead compared to explicit feedback.

## Slide 12
Appendix

## Slide 13: References
[1]: IEEE 802.11-19/0768 Implicit Channel Sounding in IEEE 802.11be
[2]: IEEE 802.11-20/0086 Opportunistic Implicit Channel Sounding

## Slide 14
Appendix

## Slide 15: Explicit Channel Sounding
Example used for calculation of network overhead:
AP-1
NDPA
SIFS
SIFS
SIFS
AP- k
Compressed BF Reports
M-AP
Trigger
Data
Data
AP- 2
Multi-AP NDP
Multi-AP NDP
Multi-AP NDP
Data
SIFS
BFRP Trigger-1
BFRP Trigger-k
Compressed BF Reports
Multiplexed in Time/ Frequency/Space

## Slide 16: NDP Spatial Multiplexing in Uplink
The impact of CFO error when there is a power imbalance across multiplexed STAs
Transmit power accuracy/ RSSI Measurement accuracy:
  Class A: ±3/ ±3
  Class B: ±9/ ±5
2x LTF is used and STAs may have maximum of 350 Hz residual CFO
%5

## Slide 17: Network Overhead Evaluation: Implicit vs Explicit
Explicit Feedback: Network overhead is increased with number of antennas at AP and number of STAs.
Use Cases: Examples: BW=80 MHz, MCS 2/4, =4 | Sounding Duration (msec) |  | 
 | Explicit (MCS=2) | Explicit (MCS=4) | Implicit
4-antennas AP : 2 STA / 3 STA/ 20 STAs | .5/ .7/ 3.6 | .4/.5/2 | .24/ .25/ .6
8-antennas AP : 3 STA / 6 STA/ 20 STAs | 1.4/ 2.6/8.3 | .9/1.5/5 | .25/ .3/ .6
16-antennas AP: 6 STA / 10 STA/ 20 STAs | 5.5/ 9/ 17.5 | 3/5/9 | .3/ .37/ .6
 | Sounding Duration (msec) |  | 
 | Explicit (MCS=2) | Explicit (MCS=4) | Implicit
4-antennas AP : 2 STA / 3 STA/ 20 STAs | .5/ .7/ 3.6 | .4/.5/2 | .24/ .25/ .6
8-antennas AP : 3 STA / 6 STA/ 20 STAs | 1.4/ 2.6/8.3 | .9/1.5/5 | .25/ .3/ .6
16-antennas AP: 6 STA / 10 STA/ 20 STAs | 5.5/ 9/ 17.5 | 3/5/9 | .3/ .37/ .6