## Slide 1: Multi-Link for Low Latency
Date: 2020-01-10
Authors:

## Slide 2: Abstract
Multi-link and low-latency operation are targeted features of 802.11be
In this contribution, we propose a multi-link-based mode of operation to specifically reduce latency in 802.11be

## Slide 3: Recap on earlier contributions
[19/0402r1] - Reducing Channel Access Delay
  Channel access delay may be decreased by simultaneously contending for channel access on several channels
[19/1405r7] - Multi-link Operation Channel Access Discussion
  In-device power leakage may prevent simultaneous TX and RX on two different links

## Slide 4: 802.11be multi-link definitions
40MHz - 2.4 GHz
80MHz - 5 GHz
A multi-link device (MLD) may simultaneously TX and RX frames in multiple links
A link, in such multi-link operation, may include a primary channel, and optionally, secondary one(s)
  A link may only include a primary channel
The multiple links, in such multi-link operation, may be on a single or multiple frequency bands
PHY
PHY
L-MAC
L-MAC
U-MAC / BSS
P
S
P
S
P
S
PHY
L-MAC

## Slide 5: Motivation for multi-link
Increased system efficiency
  by making a more dynamic usage of the spectrum
Increased peak throughput
  by simultaneously TX/RX via 2 or more links
Decreased channel access delay
  by simultaneously contending for channel access on several channels and getting channel access through the first available one

## Slide 6: Decreased channel access delay with multi-link
For real-time applications like cloud gaming, voice/video calls, etc. reliable low channel access delay may be the most important reason to use multi-link
  The more links  the smaller the channel access delay [19/0402r1]
For example, if devices can support 8 active links, and each link can support 1ms latency with 90% probability, then such multi-link devices can support in theory 1ms latency with 99,999999% probability
However, operating simultaneously 8 links may be impractical if each of them is assumed to have its own PHY
  The cost and the power consumption of such a device may be too high as they may increase linearly with the number of links
  Links are expected to set constraints to each other when they operate in channels relatively close to each other [19/1405r7]
How about considering multiple links in adjacent channels with one PHY?

## Slide 7: Decreasing channel access delay with a new multi-link mode of operation
40MHz - 5 GHz
We propose,
  a new optional mode of operation, referred to as Reliable Low Latency Multi Link (RLLML), for 802.11be multi-link devices
This new mode of operation is intended to
  efficiently operate links on adjacent physical channels within a band with one PHY,
  in devices where the number of PHY layers/RF chains is smaller than the number of links,
  by reusing/sharing the available PHY layers/RF chains among such links
In the following, we address the RLLML
  Rules of operation, which resemble existing ones, and
  Fairness between the multi-link and legacy devices
  with focus on links sharing a single PHY layer/RF chain
L-MAC
U-MAC / BSS
L-MAC
CCA (20 MHz)
CCA (20 MHz)
RLLML
one PHY layer to handle multiple links

## Slide 8: RLLML rules of operation (I)
An AP willing to provide low latency access may, as an example, have 8x20MHz links on a continuous 160MHz frequency band
  Let’s call these 8 links a RLLML set
If implementing RLLML, such an AP shall indicate to its associated STAs that it will
1) run separate carrier sense and access mechanisms per link, and
2) receive or transmit data only on one link at a time
  The associated STAs also inform their serving AP of these capabilities
Non-AP multi-link device
AP multi-link device
Link 1 @channel 1
Link 8 @channel 8
Link 1 @channel 1
Link 8 @channel 8
Backoff
Backoff
Backoff
Backoff

## Slide 9: RLLML rules of operation (II)
An RLL MLD must
  run separate carrier sense and access mechanisms per link
  receive or transmit data only on one link at a time
  consider all the other links/channels busy when transmitting or receiving on one of the links
  use a probe delay mechanism (e.g. NAVSyncDelay or ProbeDelay) on other links/channels after TX/ RX is done on one link
    as the device may not keep NAV up-to-date while TX/RX on one link
A non-AP RLL MLD must
  keep up-to-data state information on whether the serving AP is busy operating on any of the links of the RLLML set
    as the device should not transmit towards its serving AP

## Slide 10: Mix of RLLML and regular ML
40MHz - 6 GHz
The new mode could be used also with normal links
For example one could have 1) a normal link in the 5GHz band, and 2) RLL links on the 6GHz band
L-MAC
U-MAC / BSS
L-MAC
CCA (20 MHz)
CCA (20 MHz)
one PHY layer to handle multiple links
80MHz - 5 GHz
L-MAC
PHY

## Slide 11: RLLML fairness
In general, an asynchronous 802.11be multi-link device wins the channel contention more often than a legacy single-link device
  Multi-link devices with n links may get up to n times more airtime
  This is an intended feature and considered fair in general
A MLD implementing RLLML may also potentially access the channel more often, but due to the limitation on simultaneous TX/RX, its airtime is in most cases less than n times larger
  The competitive edge in contention is the exact reason why channel access latency is reduced

## Slide 12: Conclusions
We propose a Reliable Low Latency Multi-Link (RLLML) mode of operation where a MLD
  runs links on adjacent channels,
  runs carrier sense and channel access mechanisms per link basis, and
  transmits or receives only on one link at a time
Such operation requires:
  signaling to indicate RLLML capabilities/limitations

## Slide 13: Straw poll
Should 802.11be allow a Reliable Low Latency Multi-Link (RLLML) mode of operation, in which a MLD
runs links on adjacent channels,
runs carrier sense and channel access mechanisms per link, and
transmit or receive only on one link at a time?
Yes
No
Abstain
Should be further discussed

## Slide 14: Additional slides

## Slide 15: Implementation constraints considered by the RLLML mode of operation
As per 802.11be SFD: “802.11be shall allow a MLD that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links. Signaling of these constraints is TBD.”
  In-device interference and other in-device coexistence issues may limit simultaneous TX/RX on two or more links
    Especially when the links are close-by in the frequency domain
Additional important implementation constraints are
Cost of the implementation, and
Power consumption
    As a solution to both, some layers/functionalities may be shared among links
    For example, a STA may only have one PHY layer/RF chain for links that operate on the same band
      Such a STA would not be able to transmit on two or more links at the same time