## Slide 1: 11be HARQ Discussions
Date: 2020-01-09
Authors:

## Slide 2
Introduction
Many contributions have discussed using different HARQ units for retransmission and acknowledgement. Two HARQ units were mentioned:
  MPDU
  Codeword (CW)
In this contribution, we discuss a potential problem when HARQ unit is adopted in 802.11be.

## Slide 3: Recap: A-MPDU Format
A-MPDU format is given below
A-MPDU subframe 1
A-MPDU subframe n
…
EOF padding*
MPDU delimiter
MPDU
padding
MPDU length
CRC
Delimiter signature
Reserved
Mac header
MSDU
FCS
*: EOF padding is introduced from 802.11ac

## Slide 4: Recap: Problems for MPDU HARQ Unit
In [1], retransmitted A-MPDU may not be the same as the first transmitted A-MPDU because of :
  Arbitrary numbers of delimiters (DL) among the MPDUs
  Each MPDU Header’s flipped retry bit
  Different Cipher Text
  Different CRC bits
In this contribution we add another potential problem regarding the duration field when HARQ (re)transmissions are within one TXOP.

## Slide 5: HARQ Transmissions in a TXOP
HARQ transmissions within one TXOP have following benefits:
  Within a TXOP, the transmissions are protected so that collision probability is controlled. With this assumption, HARQ combining will be beneficial.
    This is also the reason that TXOP signaling in PHY layer is important.
  Within a TXOP, scheduled transmissions are possible so that the devices may know the transmitter and receiver of the packet without decoding the MAC header.
  HARQ transmissions are completed in an efficient way so that the implementation (e.g. HARQ buffers) may be easier.

## Slide 6: Duration Field
When HARQ transmissions are within one TXOP, the duration field for retransmission may not be the same as that in the preceding transmissions.
  Duration field is in MAC header. Therefore, the MAC frame for retransmission is different from MAC frame for the first transmission and HARQ combining is not possible.
  This is a direct problem when MPDU HARQ unit is adopted. It is also a problem when CW HARQ unit is used. NAV setting is largely based on duration field in MAC header. HARQ transmissions need to provide a mechanism for STAs to set NAV.
If HARQ retransmission and acknowledgement is adopted, necessary changes should be considered to address the problem.
First transmission
Retransmission
…
TXOP
Duration field in MAC header

## Slide 7: Conclusion
Based on the current standard, there is no guarantee that the duration value in the Duration field in MAC header remains the same in retransmissions.
If HARQ retransmission and acknowledgement is adopted, necessary changes should be considered to address the issue.

## Slide 8: Reference
IEEE 802.11-19/0873r1, Quantenna, “HARQ Framing”