## Slide 1: Link Latency Statistics of Multi-band Operations in EHT
Date: 2020-01-08
Authors:

## Slide 2: Introduction
In EHT, latency improvement is the key task
Multilink operation(MLO) targets to increase the overall throughput and to improve connection stability.
For EHT MLO, in the view of load balance
  In addition to legacy BSS load statistics, latency serves as another important indicator helping STA to understand if a link is qualified for time critical applications
  AP can further provide latency statistics of each link to help STA using a suitable link
This contribution explores latency statistics in current specs. and proposes to add more latency statistics in EHT for MLO

## Slide 3: Re-cap of Latency Related Elements [1]
BSS Average Access Delay element
  contains the AP Average Access Delay, which is a measure of load in the BSS and is available in both QoS APs and non-QoS APs.
BSS AC Access Delay element
  contains an Access Category Access Delay. Use same delay definition as the BSS Average Access Delay but separate measures of each access category
Measurement Report element
  In Transmit Stream/Category Measurement report, average queue delay and average transmit delay are reported for a TS or TC to a specific peer STA

## Slide 4: Delay Types
Queue delay
Channel(Medium) access delay
Transmit delay

## Slide 5: Queue Delay
MSDU base
Queue delay is measured from the time the MSDU is passed to the MAC until the point at which the first or only corresponding MPDU begins transmission. (TS/TC Measurement report)
Each access category has its own queue. Average queue delay of access categories is different
EDCA in 802.11, four ACs are defined
  VO, VI, BK, and BE
Enter the queue
In the EDCA control to WM

## Slide 6: Channel Access Delay
MPDU base
Channel(Medium) access delay is measured from the time the DCF or EDCAF MPDU is ready for transmission (i.e., begins CSMA/CA access) until the actual frame transmission start time. (BSS Average Access Delay element)
  No considerations of collision or failed transmission

## Slide 7: Transmit Delay (1/2)
MSDU base
Transmit delay is measured from the time the MSDU is passed to the MAC until the point at which the entire MSDU has been successfully transmitted, including receipt of the final Ack frame from the peer STA if the QoS Ack service class is being used. (TS/TC Measurement report)

## Slide 8: Transmit Delay (2/2)
Collision or retransmission may happen
Transmit delay counts until the MSDU is successfully Acked by the peer STA
  If an MSDU is divided into fragments, delay counts until all fragments are Acked
  If an MSDU is discarded due to timeout or other reasons, the MSDU is not taken account into transmit delay measurement
Transmit delay is not equal to queue delay + channel access delay

## Slide 9: Current Latency Statistics Insufficiency
BSS Average/BSS AC Access Delay elements cover only channel access delay. Channel access delay is not accurate enough information without considering transmission failure
Transmit delay and queue delay are by request and only cover delay statistics between two peer STAs
Transmit delay conveys key information how long it takes for an MSDU being successfully delivered to the destination but there is no such information measured in BSS or in link base
Average based statistics are not enough for latency critical applications [2]

## Slide 10: Latency Statistics in EHT MLO
In the view of load balance, especially for latency critical applications, average and percentile statistics of transmit delay on each link are necessary
EHT STAs running time critical applications may set transmit delay statistics as a higher priority reference for traffic distribution
Transmit delay can be separately generated depending on MSDU sizes, such as small, medium, and large MSDUs for specific traffic types

## Slide 11: Usage Examples
Load balance: AP can steer delay sensitive STAs to a link with shorter latency
Single link devices may pick up a low latency link during association.
TID mapping assistance: For a TID mapping to multiple links, sending MSDUs to a link already suffering from long latency may further increase traffic congestion

## Slide 12: Latency Statistics Proposal for EHT MLO
EHT MLO AP should provide latency statistics of each link, including
  Average transmit delay over all ACs
  95% percentile transmit delay over all ACs
  Average transmit delay of the highest priority AC
  95% percentile transmit delay of the highest priority AC
  Average MSDU loss rate
  In optional subelements,
    Detailed transmit delay statistics depending on MSDU sizes
    Detailed delay statistics such as queue delay and channel access delay
    Detailed delay statistics of each AC
Enhancement in measurement report element to cover UL transmit delay of STA, such percentile statistics

## Slide 13: Straw Poll 1
Do you support that EHT MLO AP should provide transmit delay statistics of each link carried in an information element?

## Slide 14: Straw Poll 2
Do you support the delay statistics proposed in slide 10 for EHT AP?

## Slide 15: References
IEEE 802.11md D3.0
11-18-1160 Controlling latency in 802.11