## Slide 1: Link Latency Statistics of Multi-band Operations in EHT
Date: 2020-01-08
Authors:

## Slide 2: Introduction
In EHT, latency improvement is the key task
Multilink operation(MLO) targets to increase the overall throughput and to improve connection stability.
For EHT MLO, in the view of load balance
  In addition to legacy BSS load statistics, latency serves as another important indicator helping STA to understand if a BSS is qualified for time critical applications
  In addition to BSS latency statistics, AP can further provide latency statistics of each link to help STA using a suitable link
This contribution explores latency statistics in current specs. and proposes to add more latency statistics in EHT for MLO

## Slide 3: Re-cap of Latency Related Elements [1]
BSS Average Access Delay element
  contains the AP Average Access Delay, which is a measure of load in the BSS and is available in both QoS APs and non-QoS APs.
BSS AC Access Delay element
  contains an Access Category Access Delay. Use same delay definition as the Average Access Delay but separate measures of each access category
Measurement Report element
  In Transmit Stream/Category Measurement report, average queue delay and average transmit delay are reported for a TS/TC to a specific peer STA

## Slide 4: Delay Types Defined in Baseline
Queue delay
(Access category) access delay
Transmit delay

## Slide 5: Queue Delay
MSDU base
Queue delay is measured from the time the MSDU is passed to the MAC until the point at which the first or only corresponding MPDU begins transmission. (defined in TS/TC Measurement report)
Each access category has its own queue. Average queue delay of each access category is different
No separate AC queue delay measures in current specs.
MAC Arrival
Corresponding MPDU starts transmission

## Slide 6: Channel Access Delay
MPDU base
Channel(Medium) access delay is measured from the time the DCF or EDCAF MPDU is ready for transmission (i.e., begins CSMA/CA access) until the actual frame transmission start time. (defined in BSS Average Access Delay element)
  No considerations of collision or failed transmission

## Slide 7: Transmit Delay (1/2)
MSDU base
Transmit delay is measured from the time the MSDU is passed to the MAC until the point at which the entire MSDU has been successfully transmitted, including receipt of the final Ack frame from the peer STA if the QoS Ack service class is being used. (defined in TS/TC Measurement report)

## Slide 8: Transmit Delay (2/2)
Transmit delay counts until the MSDU is successfully Acked by the peer STA
  If an MSDU is divided into fragments, delay counts until all fragments are Acked
  If an MSDU is discarded due to timeout or other reasons, the MSDU is not taken account into transmit delay measurement
Transmit delay is not equal to queue delay + channel access delay
  Collision or retransmission may happen and the period of waiting for ack is not considered as well

## Slide 9: Current Latency Statistics Insufficiency
BSS Average/BSS AC Access Delay elements cover only channel access delay. Channel access delay is not accurate enough information without considering transmission failure
Transmit delay conveys key information how long it takes for an MSDU being successfully delivered to the destination but there is no such information measured in BSS base or in link base
  Current transmit delay is by request and only cover delay statistics between two peer STAs
Average based statistics are not enough for latency critical applications [2]

## Slide 10: Latency Statistics in EHT MLO
In the view of load balance, especially for latency critical applications, average and percentile statistics of transmit delay on each link are necessary
EHT STAs running time critical applications may set transmit delay statistics as a higher priority reference for traffic distribution
Transmit delay can be separately generated depending on MSDU sizes, such as small, medium, and large MSDUs for specific traffic types

## Slide 11: Usage Examples
Load balance: AP can negotiate with STA to recommend STA’s delay sensitive traffic moving to a link with shorter latency
TID mapping assistance: For a TID mapping to multiple links, sending MSDUs to a link already suffering from long latency may further increase traffic congestion
Single link devices may pick up a low latency link during association with an MLO AP
ISP and other service providers need such statistics to analyze network latency, and now they provide WiFi routers to customers but they can’t extract latency information from those routers

## Slide 12: Latency Statistics Ideas for EHT MLO
EHT AP should provide BSS latency statistics, including
  Average and 95th percentile transmit delay over all ACs
  Average and 95th percentile transmit delay of the highest priority AC
  Average MSDU loss rate
  In optional subelements,
    Detailed transmit delay statistics depending on MSDU sizes
    Detailed delay statistics of each AC
    TBD detailed information
EHT MLO AP should further provide latency statistics of each link and contents are similar to the BSS latency statistic
Enhancement in measurement report element to cover UL transmit delay of STA, such as adding percentile statistics
Information can be carried in a new element or extension of current elements

## Slide 13: Straw Poll 1
Do you support that EHT AP should provide BSS transmit delay statistics carried in an information element?
  Transmit delay statistics details are TBD

## Slide 14: Straw Poll 2
Do you support that EHT AP MLD should provide transmit delay statistics of each link carried in an information element?
  Transmit delay statistics details are TBD

## Slide 15: References
IEEE 802.11md D3.0
11-18-1160 Controlling latency in 802.11