## Slide 1: Target STA Announcement in AP TXOP of MLO Operation
Date: 2020-03-08
Authors:

## Slide 2: MLO Operations and STR
Multi-link operation (MLO)
  A multi-link device can perform channel access (e.g., EDCA) on multiple wireless links independently
Simultaneous Transmit Receive (STR)
  A multi-link device is capable of independent transmission and receive on each link
  Devices may not be able to perform STR due to hardware constraints or frequency band assignment
In this contribution, we assume that AP is capable of STR and explore issues when STAs are non-STR during an AP TXOP only on one link

## Slide 3: Problem Statement (1/2)
When AP grabs a TXOP only on a link (say, Link 1), and starts DL/UL frame exchange with some STAs on Link 1
During the TXOP
  Different frame exchange may happen on Link 2
  For STR STAs, since Link 2 is independent from Link 1, they can freely use Link 2
  When non-STR STAs monitor frame exchange on Link 1, their Link 2 connection is almost useless if eventually no frame exchange happens with AP on Link 1. These non-STR STAs downgrade to single link operation and are stuck on Link 1 during the TXOP
Frame exchange with non-STR STAs?

## Slide 4: Problem Statement (2/2)
Link 2 constraints of non-STR STAs
Examples:
  STA can not transmit on Link 2 when its Link 2 EDCA counter goes to zero and STA is decoding a Link 1 DL frame (it happens before STA knows the DL frames’ target STAs)
  STA may lose a DL frame for it on Link 1 because before its UL frame on Link 2 ends, a DL frame on Link 1 arrives
      AP may schedule a DL frame for the STA before it decodes a UL frame from that STA on Link 2
Example 1
Example 2

## Slide 5: Ideas
Knowledge of which STAs to have frame exchange during the Link 1 AP’s TXOP helps improving non-STR STA efficiency if they can doze (suspend, or shutdown) Link 1 during the TXOP and use Link 2 regardless what happens on Link 1
  Non-STR STAs capable of more links benefit more

## Slide 6: Re-Cap of VHT TXOP power save
Motivations
  A station can save power when it knows that there are no frames for it during a downlink MU-TXOP
A non-AP VHT STA that is in TXOP power save mode may enter the doze state until the end of that TXOP when one of the following conditions is met:
  On receipt of a VHT MU PPDU, the STA determines that it is not a member of the group indicated by the RXVECTOR parameter GROUP_ID.
  On receipt of an SU PPDU, the STA determines that the RXVECTOR parameter PARTIAL_AID is not equal to 0 nor does it match the STA’s partial AID
  and, …etc
Drawbacks for those STA allowed to enter doze state
  VHT MU PPDU from AP: any STAs do not belong to the MU group may go to doze mode
  VHT SU PPDU from AP: any STAs do not match their partial_AID may go to doze mode
  A single MU/SU PPDU may cause many STAs to go to doze mode
VHT TXOP power save is not a good solution to the problem in MLO

## Slide 7: Scenario 1
MLO AP grabs a TXOP of a link and based on its buffers, it plans to load only DL frames to several target STAs
  An announcement frame of which STAs to have frame exchange during the TXOP is sent before DL data frames
  DL frames can be MU or SU
STAs are not listed in the announcement frame make the link enter power save mode
  In the end of the TXOP, those STAs resume the link to regular operation

## Slide 8: Scenario 2
MLO AP grabs a TXOP of a link and it plans to load both DL and UL frames
  In addition to AP’s own buffer, AP sends BSRP/BSR frames to inquiry STAs’ buffer status
  AP determines which STAs to have frame exchange (UL or DL) during the TXOP and send an announcement frame before data frames
STAs are not listed in the announcement frame make the link enter power save mode
  In the end of the TXOP, those STAs resume the link to regular operation

## Slide 9: Benefits
DL TXOP power save for STAs not listed in the announcement frame
Non-STR MLO STA to have no frame exchange during the DL TXOP owns a free link to use
AP may do different level of estimation of STAs to be listed in the announcement frame

## Slide 10: Announcement Frame (Element) Content Ideas
Broadcast on specific link(s)
Announcement may contain different contents to save frame size
  Use similar indication as TIM
  Use AID
    AIDs of all STAs expected (not) to have frame exchange during the link’s TXOP
    AIDs of non-STR STAs only expected (not) to have frame exchange during the link’s TXOP (Save announcement size)
    Group ID if necessary
    1 bit indicates “not”
Instead of using a specific announcement frame, defining an element carried in a broadcast PPDU/frame is another implementation method
More details are TBD

## Slide 11: Straw Poll 1
Do you support that during a DL TXOP of MLD AP, AP may send a broadcast announcement frame(element) carrying information about which STAs to have frame exchange with AP during the TXOP?

## Slide 12: backup

## Slide 13: Supplemental Data
DL TXOP occupied most of transmission time >80%
Using EDCA to access channel, the traffic of the access category is allocated in advance