## Slide 1: ITU AHG Introduction Presentation
Author:
Date: 2020-01-13

## Slide 2: Background
IEEE 802.11 announced the formation of ITU Liaison Ad Hoc Group (ITU AHG) on December 17, 2019: With this email, I announce establishment of the 802.11 ITU Liaison Ad-hoc Group (ITU AHG), and appoint Hassan Yaghoobi (hassan.yaghoobi@intel.com ) as Chair of the group.
At least the following ITU-R document sections (might be more) are out of date as far as their description of 802.11 standard radio characteristics:
ITU-R M.1450-5 Table 2, Annex I, Annex2, Table 3 (see summary in https://mentor.ieee.org/802.18/dcn/19/18-19-0157-00-0000-an-update-on-the-recommendation-itu-r-m-1450-5.pptx ), see https://www.itu.int/rec/R-REC-M.1450-5-201404-I/en
ITU-R M.1801-2 Table 5, see https://www.itu.int/dms_pubrec/itu-r/rec/m/R-REC-M.1801-2-201302-I!!PDF-E.pdf pages 34-35

## Slide 3: Background (cont’d)
The ITU AHG charter is: To develop IEEE 802.11 contribution(s) with proposed updates to relevant ITU-R documents, including but not limited to M.1450-5 and ITU-R M.1801-2
Meetings: To meet during the January and March 2020 sessions, potentially with additional scheduled teleconferences
Timeframe: initial ITU submission(s) for the 2020-04-27 to 2020-05-08 ITU-R WP 5A meeting, see
  https://www.itu.int/en/events/pages/Event-Details.aspx?eventid=17353
Once 802.11 approved contribution(s) are available, the contribution(s) will be taken to 802.18 for information and endorsement, notified to the 802 EC (5 day objection period). and submitted to ITU-R as IEEE contribution(s).

## Slide 4: WP 5A & 5D Responsibilities
ITU-R Working Party 5A – Land mobile service excluding IMT; amateur and amateur-satellite service: is responsible for studies related to the land mobile service, excluding IMT and including wireless access in the fixed service, and is also responsible for studies related to the amateur and amateur-satellite services.
  WP 5A responsible for revising recommendations M.1801 & M.1450
  WP 5A Technology WG responsible for drafting and development of the working documents for recommendations
Working Party 5D (WP 5D) - IMT Systems: is responsible for the overall radio system aspects of International Mobile Telecommunications (IMT) systems, comprising the IMT-2000, IMT-Advanced and IMT for 2020 and beyond.
  WP 5D is responsible for sharing studies and co-existence mechanisms using WP 5A parameters

## Slide 5: Updates to the Recommendation Needed
Recommendation ITU-R M.1450-5: Characteristics of broadband radio local area networks (02/2014)
Recommendation ITU-R M.1801-2: Radio interface standards for broadband wireless access systems, including mobile and nomadic applications, in the mobile service operating below 6 GHz (02/2013)

## Slide 6: WRC-19 Results Triggering Studies (60 GHz)
WRC’s resolution COM4/7 [1, pp. 389-390]:
that administrations wishing to implement IMT make available the frequency band 66-71 GHz identified in No. 5.J113 for use by the terrestrial component of IMT;
that administrations wishing to implement IMT in the frequency band 66-71 GHz, identified for IMT under the provisions in No. 5.J113, which are also wishing to implement other applications of the mobile service, including other wireless access systems in the same frequency band, consider coexistence between IMT and these applications
to develop harmonized frequency arrangements for the implementation of the terrestrial component of IMT in the frequency band 66-71 GHz;
to develop ITU-R Recommendations and/or Reports, as appropriate, to assist administrations in ensuring the efficient use of the frequency band through coexistence mechanisms between IMT and other applications of the mobile service, including other wireless access systems, as well as between the mobile service and other services;
to regularly review, as appropriate, the impact of evolving technical and operational characteristics of IMT systems (including base-station density) and those of systems of space services on sharing and compatibility, and to take into account the results of these reviews in the development and/or revision of ITU-R Recommendations/Reports addressing, inter alia, if necessary, applicable measures to mitigate the risk of interference into space receivers.

## Slide 7: WRC-19 Results Triggering Studies (6 GHz)
WRC’s resolution COM6/1 on Agenda for WRC-23 [1, pp. 470-474]:
1.2: to consider identification of the frequency bands 3300-3400 MHz, 3600-3800 MHz, 6425-7025 MHz, 7025-7125 MHz and 10.0-10.5 GHz for International Mobile Telecommunications (IMT), including possible additional allocations to the mobile service on a primary basis, in accordance with Resolution COM6/2 (WRC-19);
WRC’s resolution COM6/2 [1, pp. 475-476] : To conduct and complete in time for WRC-23 the sharing and compatibility studies, with a view to ensuring the protection of services to which the frequency band is allocated on a primary basis, without imposing additional regulatory or technical constraints on those services, and also, as appropriate, on services in adjacent bands, for the frequency bands:
  3600-3800 MHz and 3300-3400 MHz (Region 2);
  3300-3400 MHz (amend footnote in Region 1);
  7025-7125 MHz (globally);
  6425-7025 MHz (Region 1);
  10 000-10 500 MHz (Region 2),

## Slide 8: ITU Process: WP 5A
The process for updating the Recommendations in WP 5A is independent of sharing studies in WP 5D
  IEEE 802.11 submission to WP 5A, in form of revision mark on ITU-R M.1450-5 & ITU-R M.1801-2
  If no objection, working documents for new revisions of the two Recommendations are generated
  And an LS is initiated to all relevant organizations stating the IEEE 802.11 proposal and requesting if they have other inputs to the working documents
  The Recommendations is approved as soon as all inputs received and processed; Meeting Schedule
    2020-04-27 to 2020-05-08, ITU-R WP 5A (Deadline 1 week 04-19)
    2020-11-09 to 2020-11-20, ITU-R WP 5A (Deadline 1 week 11-01)
    May 2021 TBD, ITU-R WP 5A

## Slide 9: ITU Process: WP 5D
WP 5D is tasked to conduct co-existence mechanism for 60 GHz and sharing studies for 6 GHz
  WP 5D to start the sharing studies in Nov 2021
  WP 5A to provide the sharing parameters for RLAN and IMT sharing studies (approved Recommendations or stable drafts) to WP 5D by June 2021
  WP 5A may approve Recommendations before or after sharing studies started

## Slide 10: IEEE 802.11 Coverage in the Recommendations
IEEE 802.11 Standards to be Considered
  IEEE Std P802.11ac-2013, 2013-12-09
  IEEE Std P802.11ax , Nov 2020
  IEEE Std P802.11ay, Dec 2020
  IEEE Std P802.11ba, Sep 2020 (?)
  IEEE Std P802.11az, Mar 2021 (?)
  Others?
IEEE 802.11 technologies should have STD status by the time of approval in SG5 for Publication (that is two months after WP 5A submission of Recommendations to SG5)
WP5A members may request delayed submission to SG5 for publication of STDs

## Slide 11: ITU AHG Work Plan and Timeline
Jan-Mar 2020: Develop proposed revisions to Rec ITU-R M.1450-5 & ITU-R M.1801-2 based on the latest drafts of the 802.11 specifications
  Jan 2020 Interim: ITU AHG Formation and Introduction Presentation; Call for contribution
  Feb – Mar 2020: Four conference calls (dates TBD)
  Mar 2020 Plenary: Recommendation to 802.11 for approval and Notification to 802.18
Apr 2020 and after: Maintenance as needed