## Slide 1: Multi-link Triggered Uplink Access
Date: 2020-03-26
Authors:

## Slide 2: Recap: Synchronous Multi-link Transmission
When a STA simultaneously transmits and receives frames on multi-link, it may have some in-device coexistence (IDC) interference.
  When simultaneous Tx and Rx is happened between 2.4 GHz band and 5 GHz band, the IDC interference is probably negligible.
  But, the IDC interference caused by simultaneous Tx and Rx between 5 GHz band and 6 GHz band may be significantly problematic worse depending on some implementation capability like the RF filter performance.

## Slide 3: Multi-link Triggered Uplink Access (TUA)
An AP performs an independent EDCA channel access on each link with its own EDCA parameters (CWmin, CWmax, AIFS, CW, and Retry Counter).
After obtaining a TXOP, the AP sends the Trigger frame and the STAs responds with the EHT TB PPDU.
  On each link, the PPDUs carrying the Trigger frame and the EHT TB PPDU can be independently encoded into one of frequency segments.
Trigger
5GHz
6GHz
EHT TB PPDU
Trigger
EHT TB PPDU
Block ACK
Block ACK
AP
STA
AP
STA
Back-off
5
4
3
2
1
0
Back-off
9
8
7
6
5
4
3
2
1
0
Trigger
EHT TB PPDU
Trigger
EHT TB PPDU
…
…

## Slide 4: Constrained Multi-link TUA
But, when the STA has the IDC interference issue, the AP shall not schedule to the STA the PPDU carrying the trigger frame while the STA is responding with an EHT TB PPDU.
Trigger
5GHz
6GHz
EHT TB PPDU
Trigger
No Response
Block ACK
Block ACK
AP
STA
AP
STA
Back-off
5
4
3
2
1
0
Back-off
8
7
6
5
4
3
2
1
0
Trigger
EHT TB PPDU
Trigger
EHT TB PPDU
…
…
Error by IDC interference

## Slide 5: Constrained Multi-link TUA
Synchronization requirement [1]
  A difference between the ending times of PPDU transmissions shall be less than SIFS - (10%×aSlotTime).
    Because a minimum inter-frame space is not less than SIFS, Tx and Rx are not overlapped.
      A margin of 10%×aSlotTime considers the SIFS accuracy of the IEEE 802.11-2016 spec.
5GHz
6GHz
Trigger (CS Required = 0)
MAC Padding
AP
STA
AP
STA
PHY Padding
PE
Trigger (CS Required = 0)
MAC Padding
PHY Padding
PE
EHT TB PPDU
Difference between the ending times of the transmissions is less than SIFS - (10%×aSlotTime).
SIFS
SIFS
EHT TB PPDU

## Slide 6: Constrained Multi-link TUA
Additionally, a STA’s IDC interference can change the carrier sense (CS) of another link to a busy state (e.g., greater than ED threshold) while the STA is transmitting an EHT TB PPDU. In such case, the STA may not respond to the Trigger frame with the CS Required field set to 1.
5GHz
6GHz
Trigger (CS Required = 1)
MAC Padding
AP
STA
AP
STA
PHY Padding
PE
Trigger (CS Required = 1)
MAC Padding
PHY Padding
PE
EHT TB PPDU
Interference leakage cause the CS status to a busy state.
Difference between the ending times of the transmissions is less than SIFS - (10%×aSlotTime).
SIFS

## Slide 7: Constrained Multi-link TUA
So, when the AP sends to the STA a PPDU containing the Trigger frame with the CS Required field set to 1, the AP should meet the following additional requirement.
  The time difference between the ending time of the soliciting DL PPDU that is lastly sent and the starting time of the solicited TB PPDU that is firstly sent is greater than or equal to aCCATime (TBD).
    aCCATime (e.g., 4μs, 8μs) can be predetermined in the spec.
    Or, each STA can signal its aCCATime requirement to the AP.
5GHz
6GHz
Trigger (CS Required = 1)
MAC Padding
AP
STA
AP
STA
PHY Padding
PE
Trigger
(CS Required = 1)
MAC Padding
PHY Padding
PE
SIFS
EHT TB PPDU
EHT TB PPDU
SIFS
The time difference between the last DL PPDU and the first TB PPDU is greater than or equal to aCCATime.

## Slide 8: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1305-00-00be-synchronous-multi-link-operation.pptx

## Slide 9: Straw Poll 1
Do you support the following PPDU transmission restriction in the MLO?
  The AP MLD may solicit simultaneously TB PPDUs requiring the carrier sense from the non-STR STA MLD when the time difference between the ending time of the soliciting DL PPDU that is lastly sent and the starting time of the solicited TB PPDU that is firstly sent is greater than or equal to aCCATime.
    Where aCCATime is TBD.