## Slide 1: 3GPP RAN1 status on NR-Unlicensed
Date: 2020-01-16
Authors:
Name | Affiliations | Address | Phone | email
Shubhodeep Adhikari | Broadcom |  |  | shubhodeep.adhikari@broadcom.com
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com

## Slide 2: Outline
This presentation provides a short update from the 3GPP RAN1 meeting (RAN1#99 led between 18/Nov – 22/Nov) on the standardization of NR-Unlicensed. The focus of this presentation is on features that impact fair coexistence between NR-U and 802.11. From RAN1 perspective, NR-U standardization in 3GPP Release 16 completed in meeting.
The presentation discusses the following topics:
Multi-channel LBT
Within a TXOP, the maximum duration of transmission without LBT.
Contention Window adaptation procedure in NR-U
  For channels with explicit feedback
  For channels without explicit feedback
LBT procedure in 16us gap
Next steps

## Slide 3: Multi-channel LBT
LAA DL multi-channel LBT i.e. the version where exponential back-off is performed on one channel and PIFS back-off on other channels is known to be unfair to Wi-Fi. It also does not adhere to EN 301 893.
As LAA is the baseline for NR-U, there was an expectation in RAN1 that NR-U may follow the same multi-channel scheme, even if its unfair to Wi-Fi.
However, RAN1 agreed not to follow the LAA baseline in this case and instead follow the multi-channel access procedure similar to Wi-Fi and what is specified in EN 301 893. This will also make it fair to Wi-Fi.
This is a positive development.

## Slide 4: Within a TXOP, the maximum duration of transmissions without LBT
Similar to 802.11ax, NR-U transmissions inside a TXOP can happen without LBT if they follow a preceding transmission within a gap of 16us.
However, it is known that transmissions without LBT, even when they happen within a TXOP are inherently unsafe. This is because they can collide with transmissions from hidden nodes.
So, it is necessary that such transmissions are allowed only in a very restricted manner, say for transmission of ACK/NACKs within 16us.
It had been earlier agreed in Nov/2018 that NR-U will allow such transmissions without LBT and within a TXOP without any further restriction. This had made coexistence between Wi-Fi and NR-U problematic.
However, in the last meeting, RAN1 agreed to allow such transmissions only if their duration is <= 584us. This is also the same restriction that is applied by 802.11ax.
This is a positive development.

## Slide 5: Contention Window adaptation procedure in NR-U
The CW adaptation mechanism agreed for NR-U is ballpark similar to that used by Wi-Fi and what is also specified by EN 301.893.
However, there are the following aspects where RAN1 agreed to specify better procedures for NR-U than in Wi-Fi or EN 301.893.
  In EN 301.893, if (H)ARQ feedback if not available the CW is kept unchanged. This procedure can lead to unfair/poor performance. For example, if the receiver delays sending (H)ARQ feedback in order to bundle multiple feedbacks together before transmission to reduce control message overhead. This would lead to usage of stale CW.
    In this case, RAN1 agreed to put a restriction and set a maximum time (which in the presence of Wi-Fi is max(5ms, duration of the previous transmission burst + 1ms)) by which such feedback can be delayed and retransmissions allowed without updating the CW. Retransmissions beyond this window and without corresponding feedback will use a doubled CW.
  In EN 301.893 and also in Wi-Fi, transmissions without explicit feedback reset the CW to CWmin. This is also a poor procedure.
    In this case too, RAN1 agreed to not follow the current EN 301.893 and Wi-Fi procedure and keep the CW unchanged for such transmissions without feedback.
    We think Wi-Fi too should be updated to follow the same procedure as has been agreed for NR-U.
This too is a positive development.

## Slide 6: LBT procedure in 16us gap
As noted earlier, RAN1 decided to restrict the duration of transmissions without LBT inside a TXOP and within 16us of a preceding transmission.
So, it became necessary to define an LBT procedure for all the other longer transmissions that can occur within 16us of a preceding transmission.
For such LBT, it was decided to do energy measurement for at least 5us within the 16us gap, of which at least 4us of energy measurement is made in the 9us slot immediately before the intended transmission.
This too is a positive development.

## Slide 7: Next Steps
NR-U standardization in < 7GHz is now complete in RAN1.
However, it is expected that there would be a large number of CRs submitted to the next RAN1 meeting in Athens Greece (24-28/Feb/2020).
So, it is necessary that Wi-Fi representatives continue to attend the next few RAN1 meetings in order to enable fair coexistence between NR-U and Wi-Fi.
  This is also important since certain aspects/features that we not resolved at the close of the work item may get introduced as CRs
RAN1 will also have a new work item on unlicensed operations in 60 GHz. So, companies with interest in 802.11ad/802.11ay should attend RAN1 to follow this work item.