## Slide 1: MLO a-synchronize and synchronize operation discussions
Date: 2020-01-20
Authors:
Name | Affiliations | Address | Phone | Email
Zhou Lan | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | zhou.lan@broadcom.com
Albert Bredewoud |  |  |  | 
George Kondylis |  |  |  | 
Matthew Fischer |  |  |  | 
Notes: September 2012

## Slide 2: Summary
Terminologies
  Non-Constrained MLO mode: A STA/AP MLD is under the Non-Constrained MLO mode if the MLD operation links support concurrent TX/RX operations across the links
  Constrained MLO mode: A STA/AP MLD is under the Non-Constrained MLO mode if the MLD operation links DON’T support concurrent TX/RX operations across the links
  Four practical MLO scenarios:
    Async. TX, Async RX scenario: A STA/AP MLD under Non-Constrained mode transmits data and solicits response from a STA/AP MLD under Non-Constrained mode
    Async. TX, Sync RX scenario: A STA/AP MLD under Non-Constrained mode transmits data and solicits response from a STA/AP MLD under Constrained mode
    Sync. TX, Async RX scenario: A STA/AP MLD under Constrained mode transmits data and solicits response from a STA/AP MLD under Non-Constrained mode
    Sync. TX, Sync RX scenario: A STA/AP MLD under Constrained mode transmits data and solicits response from a STA/AP MLD under Constrained mode
This contribution proposes the frame sequences for the these MLO scenarios

## Slide 3: Scenario 1-Async. TX, Async. RX
  Each link operates independently, which is similar to today’s Dual/Tri-band AP operations

## Slide 4: Scenario 2-Async.TX, Sync. RX
  Typical usage case: AP MLD is not under Constrained mode, STA MLD is under Constrained mode
  APs of AP MLD run independent EDCA on each link
  APs of AP MDL align the PPDU ending time
    RTS/CTS case is further discussed in the later slides
  BA/MBAs are triggered to make the alignment of the BA/MBA ending time

## Slide 5: Scenario 3-Sync. TX, Async. RX
  Typical usage case: AP MLD is not under Constrained mode, STA MLD is under Constrained mode
  Option 1:
    STA1 on link1 sends a RTT(Request to Trigger) frame to obtain TXOP on link 1, AP1 responds with ACK on link1
    AP2 run EDCA for Trigger TX on link 2. Once AP2 obtains TXOP on link2, Both AP2 and AP1 send Trigger frame on link 2 and link 1
        Trigger frame on link 1 is for keeping the channel busy on link 1
    The following transmissions on link 1 and link 2 are aligned

## Slide 6: Scenario 3-Sync. TX, Async. RX (cont.)
  If no trigger frame is received within RTT Timeout duration. STA MLD falls back to single link operation (still option 1)

## Slide 7: Scenario 3-Sync. TX, Async. RX (cont.)
  Typical usage case: AP MLD is not under Constrained mode, STA MLD is under Constrained mode
  Option 2a:
    STA1 on link1 sends a RTT(Request to Trigger) frame to obtain TXOP on link 1, AP 1 responds with a trigger frame after SIFS to trigger STA1 to transmit UL data
    AP MLD is not constrained, while STA 1 is transmitting on link 1, AP2 can still perform full EDCA
    Once backoff reaches 0 on link 2, AP2 sends a CTS-to-self to keep the channel, the CTS will not affect STA1’s transmission on link 1 because AP MDL is not constrained
      The CTS-to-self may use legacy mode only setting NAV for other STAs
      Or, the CTS-to-self can be in a A-MPDU and padded to end at the same time of TX on link1
    The following transmissions on link 1 and link 2 are aligned.

## Slide 8: Scenario 3-Sync. TX, Async. RX (cont.)
  Typical usage case: AP MLD is not under Constrained mode, STA MLD is under Constrained mode
  Option 2b:
    STA1 on link1 sends a RTS to obtain TXOP on link 1, AP 1 responds with a CTS after SIFS, STA1 starts to transmit UL data SIFS after CTS reception (i.e. STA1 on link1 doesn’t have to triggered)
    AP MLD is not constrained, while STA 1 is transmitting on link 1, AP2 can still perform full EDCA
    Once backoff reaches 0 on link 2, AP2 sends a CTS-to-self to keep the channel same as option 2a
    The following transmissions on link 1 and link 2 are aligned.

## Slide 9: Scenario 4-Sync. TX, Sync. RX
  Propose not to allow this mode of operation?

## Slide 10: Straw poll 1
  Do you agree 802.11be defines that a STA/AP MLD is under the Non-Constrained MLO mode if the operation links support concurrent TX/RX operations across the links and a STA/AP MLD is under the Constrained MLO mode if the operation links don’t support concurrent TX/RX operations across the links.
    YES
    NO
    ABS

## Slide 11: Straw poll 2
  Do you agree 802.11be shall disallow a mode of MLO operation that supports NON STR STA MLD to transmit frames to a NON STR AP MLD concurrently (PPDUs on multiple links overlapping in time domain) on multiple available links and solicit response.
    YES
    NO
    ABS

## Slide 12: Straw poll 3
  Do you agree 802.11be supports the frame sequence as shown in slide xxx when a STA MLD that is under constrained mode to concurrently transmit frames to another AP MLD that is under non constrained mode on the operation links and solicit response.
    YES
    NO
    ABS

## Slide 13: Straw poll 4
  Do you agree 802.11be supports the frame sequence as shown in slide xxx when an AP MLD that is under non constrained mode to concurrently transmit frames to another STA MLD that is under constrained mode on the operation links and solicit response.
    YES
    NO
    ABS

## Slide 14: Scenario 2-Async.TX, Sync. RX
  RTS/CTS case 1

## Slide 15: Scenario 2-Async.TX, Sync. RX
  RTS/CTS case 2

## Slide 16: Scenario 2-Async.TX, Sync. RX
  RTS/CTS case 3

## Slide 17: Scenario 2-Async.TX, Sync. RX
  RTS/CTS case 4: not sure if the regulation permits?

## Slide 18: Scenario 3-Sync. TX, Async. RX
  TX alignment : not sure if the regulation permits?