## Slide 1: MLO Typical Usage Cases and Sub-Feature Prioritization
Date: 2020-01-20
Authors:
Name | Affiliations | Address | Phone | Email
Zhou Lan | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | zhou.lan@broadcom.com
Albert Bredewoud |  |  |  | 
George Kondylis |  |  |  | 
Matthew Fischer |  |  |  | 
Notes: September 2012

## Slide 2: Summary
This contribution discusses the MLO typical operation scenarios and proposes MLO sub-feature prioritization

## Slide 3: Today
  Today, AP with 4x4 antenna, STA with 2x2 antenna become mainstream devices on the market
  Most of APs support bandwidth 160 MHz, a few STAs support bandwidth 160 MHz
  Dual/Tri-band APs are available
    E.g. 2.4GHz+5GHz(low)+5GHz(high)
    Each band establishes its own BSS and operates independently
      i.e. each band supports “aysnc.” mode without coordination (no sync. mode)
      Two 5 GHz radios can be configured to operate on the same channel sharing the same bandwidth
    Peak system throughput (SU or MU) on one 5GHz reaches 2.4Gbps (160MHz, 2SS, 1024QAM)
    Throughput can not be aggregated across BSSs (i.e. across links)
      Some proprietary implementation may support link aggregation, but there is no standard specified to guarantee the interoperability

## Slide 4: One baby step towards real MLO
  802.11be decides to supports 240/320 MHz bandwidth and 4K QAM
  Per the current timeline (D1.0 ready @May 2021), it is realistic to assume STA may only support 2 or less antennas
  Peak throughput on each link: 4.3 Gbps@5GHz (2SS, 240 MHz, 4K QAM) and 5.7 Gbps@6GHz (2SS, 320 MHz, 4K QAM)
  By defining a mechanism to support multiple links operating in a single BSS boosts the system throughput to 10 Gbps (4.3+5.7)
    Call this mode of MLO operation as flow level aggregation in this presentation
      No intention to propose such terminology in 11BE spec
    10 Gbps throughput is shared by multiple applications (i.e. multiple ACs, multiple TIDs), which should be sufficient to cover all the current and near future usage cases (e.g. AR/VR, HD Video Streaming)
    Example operation
      MLO association
      Each TID maps to a single link
      BA agreement on MLD level
      No simultaneous outstanding MPDUs (i.e. MPDUs that are not ACKed) on multiple links

## Slide 5: Single TID split across links
  802.11be decides to support a MLO mode that can split single TID QoS data to multiple available links
    There can be outstanding MPDUs on multiple available links at the same time
    Call this mode of MLO operation as packet level aggregation in this presentation
    Packet level aggregation offers single TID throughput gain but no further system throughput gain
    Packet level aggregation may offer latency gain depending on implementation architecture
      It is hard to justify high MAC split can provide latency gain due to long delay of re-queue operation of the retransmits
      Low MAC split is not easy to implement per the current timeline
        Low MAC split requires significant amount of information exchanges across links
        Low MAC split requires actuate time sync across links
        Etc.

## Slide 6: Straw poll 1
  Do you agree the reception of QoS Data frames of a single TID across multiple available links is optional for R1
    The transmitting STA splits QoS Data frames of a single TID to multiple available links for AMPDU aggregation, the outstanding MPDUs (i.e. the MPDUs not ACKed) may be transmitted on multiple links at the same time)
    The receiving STA indicates if it is capable of receiving such AMPDUs from multiple available links
    Note- A link is available when the link is enabled and the associated STA is in awake state
    Yes
    No
    Abs
      *The results of straw poll 1 decides straw poll 2. If the group decides to push packet level aggregation to R2, then MU operation on MLO is same as MU operation on single link.

## Slide 7: Pursuing peak system throughput
  The main role of MLO should be boosting system throughput to reach the maximum PHY capability, which is difficult to be achieved with SU operation
  DL MU MIMO + MLO boosts the system throughput to 20 Gbps
    8.6 Gbps @ 5GHz (4SS, 240 MHz, 4K QAM)
    11.4 Gbps @ 6GHz (4SS, 320 MHz, 4K QAM)
  Packet level aggregation is complimentary to the MU operation for latency improvement, however has implementation implication of complicated queue management etc.

## Slide 8: Flexibility
  DL OFDMA + MLO doesn’t provide further throughput enhancement
    Peak throughput on each link: 4.3 Gbps@5GHz (2SS, 240 MHz, 4K QAM) and 5.7 Gbps@6GHz (2SS, 320 MHz, 4K QAM)
  Mixed PPDU + MLO however provides flexibility of operation
    STA 1 requires more than 240 MHz capacity but less than 240+320 MHz
    AP MLD may MLO 240 MHz@link1 + 80 MHz (996 RU) to STA MLD 1
    AP2 may utilize the left of bandwidth to transmit legacy OFDMA 160 MHz (2x996 RU) to STA3
  Packet level aggregation is complimentary to the MU operation for latency improvement, however has implementation implication of complicated queue management etc.

## Slide 9: Straw poll 3
  When transmitting STA splits QoS Data of single TID to multiple available links, what is the maximum number of links do you support for 11be R1?
    2
    3
    Others

## Slide 10: Async. and Sync. operation
Terminologies
  Non-Constrained MLO mode: A STA/AP MLD is under the Non-Constrained MLO mode if the MLD operation links support concurrent TX/RX operations across the links
  Constrained MLO mode: A STA/AP MLD is under the Non-Constrained MLO mode if the MLD operation links DON’T support concurrent TX/RX operations across the links
Four practical MLO scenarios:
  Async. TX, Async RX scenario: An AP MLD under Non-Constrained mode transmits data and solicits response from a STA MLD under Non-Constrained mode
  Async. TX, Sync RX scenario: An AP MLD under Non-Constrained mode transmits data and solicits response from a STA MLD under Constrained mode
  Sync. TX, Async RX scenario: A STA MLD under Constrained mode transmits data and solicits response from an AP MLD under Non-Constrained mode
  Sync. TX, Sync RX scenario: A STA MLD under Constrained mode transmits data and solicits response from an AP MLD under Constrained mode
Aysnc. operation
Sync. operation

## Slide 11: Straw poll 4
  Do you agree the following 3 mode of MLO operation are in 11be R1 sub-features?
  Async. TX, Async RX scenario: An AP MLD under Non-Constrained mode transmits data and solicits response from a STA MLD under Non-Constrained mode
  Async. TX, Sync RX scenario: An AP MLD under Non-Constrained mode transmits data and solicits response from a STA MLD under Constrained mode
  Sync. TX, Async RX scenario: A STA MLD under Constrained mode transmits data and solicits response from an AP MLD under Non-Constrained mode
  Note-Terminology may be unified with other contributions
    Yes
    No
    Abstain

## Slide 12: Cross link power save
  There are already many sub features of MLO
  Cross link signaling for power save is a nice to have optimization and should be positioned as R2

## Slide 13: Straw poll 5
  Do you agree all the cross link power save sub features (TIM, PM, TWT, etc.) of MLO are in 11be R2
    Yes
    No
    Abs