## Slide 1: EHT Block ACK Optimization
Date: 2020-04-20
Authors:
Name | Affiliations | Address | Phone | Email
Zhou Lan | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | zhou.lan@broadcom.com
George Kondylis |  |  |  | 
Albert Bredewoud |  |  |  | 
Matthew Fischer |  |  |  | 
Notes: September 2012

## Slide 2: Summary
There is a general consensus to add 512 and 1024 BA bitmap options to EHT
For EHT MLO operation, under certain scenario it is required to align BA to support the operation of the non-STR STA
In addition, size optimization of big BA (e.g. BA with 512 or 1024 Bitmap) is preferred
This contribution proposes BA optimization

## Slide 3: Support of Arbitrary BA Bitmap
  Current BA bitmap size selection procedure
  ADDBA procedure to negotiated buffer size that decides the bitmap size options (e.g. 64, 256, 512 and 1024 etc.)
  It is up to the receiver to decide which bitmap size to use within the options that are negotiated during the ADDBA procedure
  Transmit may inform the receiver which BA bitmap to use
  Some drawbacks
  Overhead of the BA is not optimized. There can be BAs with many “zero” in it
  Not easy to make BA alignment across BAs with different bitmap size (e.g. 256 BA on one link 1024 BA on another link)
  This contribution proposes
  Transmit may inform the receiver to use an arbitrary BA bitmap that is under the constrain of the negotiated buffer size. E.g. if the options of the BA bitmap size are 64, 256 and 512. Then transmitter may inform the receiver to use BA bitmap size of 320 (i.e. under the contain of 512)
    Together with the SSN, bitmap size information is conveyed in both BAR or MPDU (e.g. define a new A-Control type)
    Limit the bitmap size to be byte of multiple byte boundary

## Slide 4: Aggregated BA Rules
  Passed decision
    “The receive status of QoS Data frames of a TID received on a link shall be signaled on the same link and may be signaled on other link(s) where the TID is mapped?”
    “…may be signaled on other link(s) where the TID is mapped? ” assumes the receiver who generates BA has the cross link information sharing capability so that the receive status sent on other links may help the transmitter to consume MPDUs on other links
    However, the transmitter still needs to receive BA on multiple links in order to obtain the full receive status, which compromise the motivation of the original proposal
  This contribution proposes
    If the received status of QoS Data frame of a TID received on a link is signaled on other links, then the receive status are duplicated on all the links that are used for the proceeding QoS Data frames soliciting the receive status

## Slide 5: Straw poll 1
  Do you agree that 802.11 BE define a mechanism to support arbitrary BA bitmap size as discussed in slide 3
  YES
  NO
  ABS

## Slide 6: Straw poll 2
  Do you agree that if the received status of QoS Data frame of a TID received on a link is signaled on other links, then the receive status are duplicated on all the links that are used for the proceeding QoS Data frames soliciting the receive status
  YES
  NO
  ABS