## Slide 1: Container for advertising ML Information
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Motivation
A non-AP MLD should be able to gathers complete MLO information about an AP MLD with minimal mgmt. frame overhead
  Saves power by not requiring the non-AP MLD to enable multiple radios (i.e., scan other bands/channels of the AP MLD)
  Reduces discovery to ML setup time
  Reduced air-time occupancy of mgmt. frames

## Slide 3: Advertisement of MLO information
Beacon frames are sent periodically and at lower MCS
  At any given instance, we don’t expect to have several unassociated non-AP MLDs waiting for a beacon
  MLO information that doesn’t get consumed can be considered as an overhead
A scanning STA’s broadcast probe request solicits responses from several APs in the neighborhood
  Unwise to pack too much information in a regular probe response
Therefore, a beacon or a regular probe response should carry minimal information to prevent mgmt. frame overhead
Proposal: Beacon/(regular) probe carries basic MLO information
  A directed ML probing mechanism to exchange complete MLO information
  In addition, complete information exchanged during ML setup

## Slide 4: High-level sequence leading to ML setup
Beacon/(regular) probe response from an AP of an MLD carries basic information of the AP MLD and it’s affiliated APs
  Based on this info, a non-AP MLD can select candidate AP(s) for further probing or to perform ML setup
Non-AP MLD queries (directed request) an AP MLD to gather full information
  During this phase, both MLDs exchange complete information
  Reuse existing probe req/resp frames [2, 5]
Non-AP MLD performs ML setup with suitable AP
  A non-AP MLD may directly perform ML setup after discovery (#1) if it has necessary info. of the AP MLD based on recent scan or by other means
  ML setup uses existing Association Req/Resp frames [2]

## Slide 5: RNR for MLO
11ax 6 GHz discovery mechanism requires an AP to advertise information of a co-located 6 GHz AP via RNR IE.
  RNR carried in Beacon and Probe Response frames. Optionally in FD frames
The RNR already provides a lot of information need for MLO:
  Operating Class, Channel, BSSID information
  TSF offset and short SSID for reported AP
  Identify if a reported AP is co-located and whether it is part of an MBSSID set
In addition, RNR can be extended to carry a little more info:
  Such as identify if a reported AP is part of the same MLD as the reporting AP

## Slide 6: RNR for MLO
However, the RNR structure by itself is not sufficient to provide complete MLO information
  Per-STA capabilities and operational parameters
  carrying the MLD level information (e.g., MLD address or common info)
Further, with multiple BSSID set on a link, the BSSIDs can belong to different MLDs [1]
  This can get quiet involved and RNR is not design to carry a lot of info
  Note: 11ax prohibits carrying RNR in a nonTxBSSID profile
Therefore extending RNR to provide MLD information is not recommended

## Slide 7: Container for carrying MLO information
We looked at existing elements to see if they have the format and properties to carry MLO capabilities information
Elements that came close to matching the requirements were Neighbor Report, Multi-Band element and Multiple BSSID
  However, these elements either didn’t have structure to make them extensible or were not carried in the appropriate frames
    See appendix for analysis on Neighbor Report, Multi-Band, and Multiple BSSID

## Slide 8: Container for carrying MLO information
We propose to define a new element: Multi-Link Attribute (MLA) element
  Exact name TBD
  Element includes fields that carry information that is common to all the links
    A Control field can signal the presence/absence of certain fields
  Element optionally includes sub-elements to provide per-STA information (profiles)
Beacon and (regular) Probe Response can provide MLD-level common information via this element
ML Probe Req/Resp and Association Req/Resp can provide complete MLO information via this element
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | MLD SSID | Authentication Algorithm | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | x | 0 or 6 | 0 or 32 | 0 or 2 | … | variable
MLD-level / Common
Set of elements organized as a profile for every other STA of the MLD
Example structure of Multi-Link Attribute element
MLD Addr Present
MLD SSID Present
Auth Algo Present

## Slide 9: Discovery and setup
Reporting AP is a single BSSID AP
Beacon or (regular) Probe Resp frame
RNR
MLA
AP entries
ML Probe Resp frame
RNR
AP entries
MLD/Common
MLA
Per-AP Info
MLD/Common
…
…
(legacy) IEs for Tx-ing AP
(legacy) IEs for Tx-ing AP
Association Resp frame
MLA
Per-AP Info
MLD/Common
…
(legacy) IEs for Tx-ing AP
EHT Cap/Op
EHT Cap/Op
EHT Cap/Op

## Slide 10: Discovery and setup
Requesting non-AP MLD
Regular Probe Req frame
MLA
ML Probe Req frame
MLD/Common
MLA
Per-STA Info
MLD/Common
…
…
(legacy) IEs for Tx-ing STA
(legacy) IEs for Tx-ing STA
Association Req frame
MLA
Per-STA Info
MLD/Common
…
(legacy) IEs for Tx-ing STA
EHT Cap
EHT Cap
EHT Cap

## Slide 11: Multiple BSSID with MLO
An AP of an AP MLD may correspond to a nonTxBSSID in a multiple BSSID set on a link [1]
In such case, an AP reported in an RNR can belong to an MLD that the nonTxBSSID is affiliated with.
The nonTxBSSID profile in the Multiple BSSID element would carry MLA IE to provide its MLO information
Maintain legacy frame exchange rules – i.e., Beacon/Probe Response from TxBSSID
  Assoc frame exchange with the desired AP (which may correspond to a nonTxBSSID).

## Slide 12: Discovery and setup
Reporting AP belongs to a Multiple BSSID set
Beacon or (regular) Probe Resp frame
RNR
MLA
AP entries
ML Probe Resp frame
RNR
AP entries
MLD/Common
MLA
Per-AP Info
MLD/Common
…
…
(legacy) IEs for Tx-ing AP
(legacy) IEs for Tx-ing AP
Association Resp frame
MLA
Per-AP Info
MLD/Common
…
(legacy) IEs for Tx-ing AP
EHT Cap/Op
EHT Cap/Op
EHT Cap/Op
MBSSID
nonTxBSSID profiles
MBSSID
nonTxBSSID profiles

## Slide 13: Inheritance Model
An MLA IE may be carried in the core frame or within a nonTxBSSID profile of a multiple BSSID element.
To avoid frame bloating, the AP should follow inheritance model to reduce duplication of information
  Similar to 11ax inheritance
The inheritance model would employ the following rules:
  Core frame to a Profile in MBSSID or MLA
    If an element is not carried in the per-STA profile, the value is the same as the element carried in the core frame (this is same as current MBSSID inheritance rule)
  NonTxBSSID Profile to per-AP Profile
    If MLA IE is carried within a nonTxBSSID profile and the per-AP profile doesn’t include an element carried in the nonTxBSSID profile (or inherited by the nonTxBSSID profile), the value is the same as that of the nonTxBSSID profile
Core Frame
RNR
MLA
MBSSID
AP entries
Per-AP profile
nonTxBSSID profile
MLA
Per-link profile

## Slide 14: In conclusion

## Slide 15: Summary
This contribution provides a mechanism to prevent mgmt. frame overhead while enabling a scheme to provide complete information to a non-AP MLD
  Describes a (new) Multi-Link Attribute element which provides a flexible structure to carry variable amount of MLO information
  Utilize RNR IE and MLA IE to provide MLO information
  Element included in an ML AP’s Beacon, Probe Response and ML setup frames
  Element included in a non-AP STA’s Probe Request or ML setup frames

## Slide 16: SP #1
Do you agree to define a new Multi-Link Attribute element to carry:
  Information of the transmitting MLD
  Information common to all the links of the transmitting MLD
  Information of all links of the MLD other than the transmitting link
    Note : Exact name for the element TBD
  Y:
  N:
  A:

## Slide 17: SP #2
Do you agree that the Multi-Link Attribute element will have a structure as described :
  A common portion containing MLD-level information
  Optionally carry per-link profile for each STA of the MLD
    Each profile consisting of a set of element
  Note : Exact name for the element TBD
  Y:
  N:
  A:

## Slide 18: SP #3
Do you agree to amend SP #97 as following:
Do you agree to define a mechanism for a STA of a non-AP MLD to send a probe request frame to an AP belonging to an AP MLD, that enables to request a probe response from the AP that includes the complete set of capabilities, parameters and operation elements of other APs affiliated to the same MLD as the AP
  The complete information is defined as all elements that would be provided if the reported AP was transmitting that same frame (exceptions TBD)
  It’s TBD if the AP is mandated or not to respond with the requested information
  Note: Such a directed probe request requesting complete MLO information for one or more APs of the MLD is referred to as an ML probe request.
  Note: A probe response sent in response to an ML probe request containing complete MLO Information for the requested AP(s) is referred to as an ML probe response
  Y: 48
  N: 1
  A: 30
TGbe editor: Please replace SP #97 with the above SP text for motion

## Slide 19: SP #4
Do you agree that the Multi-Link element when included in a Beacon or non-ML Probe Response frame should carry only MLD-level/common information?
  NOTE : Exact name for the element TBD
  NOTE: Whether the Multi-Link element is always present in the Beacon and non-ML Probe Response frames or is optionally present is TBD.
  NOTE: MLD-Level/Common information includes at least MLD Address, and other information (TBD)
  Y:
  N:
  A:
Approved with unanimous consent

## Slide 20: SP #5
Do you agree that Multi-Link element if included in a non-ML Probe Request frame shall carry only the MLD-level/common information of the non-AP MLD?
  NOTE: Whether the Multi-Link element is always present in the non-ML Probe Request frames or is optionally present is TBD.
  Y:
  N:
  A:

## Slide 21: SP #6
Do you agree to define a mechanism to that enables a non-AP MLD to gather complete MLO information of one or more APs of an AP MLD?
  Y:
  N:
  A:

## Slide 22: SP #7
Do you agree to include a Control field in Multi-Link element to indicate the presence of certain fields?
  Y:
  N:
  A:
Approved with unanimous consent

## Slide 23: Appendix

## Slide 24: References
11-20/0358: Multi-BSSID Operation with MLO (Abhishek Patil, Qualcomm)
11-20/0028 Indication of Multi-link Information (Insun Jang, LGE)
11-20/0030 Multi-link Association Follow up (Guogang Huang, Huawei)
11-20/0356: MLO: Discovery and Beacon bloating (Abhishek Patil, Qualcomm)
11-20/0389 Multi-link Discovery part 1 (Laurent Cariou, Intel)
11-20/0390 Multi-link Discovery part 2 (Laurent Cariou, Intel)

## Slide 25: Neighbor Report element (NRE)
NRE provides the necessary framework to carry information about each link:
  NRE carries Operating Class, Channel, BSSID  useful for identifying the link
  Optional Subelements field can carry Capabilities and Operation elements
    Ability to carry several other elements of interest (such as provide TSF offset info.)
  11ax additions such as SSID element, BSS Load etc can be useful for MLO
NRE doesn’t have the format to carry MLD/Common information
  Such information would need to be duplicated for each AP entry that belongs to that MLD
NRE format allows inclusion of several elements (as sub-elements) which can lead to bloating
  Possibility the reason why NRE is not allowed in Beacon/Probe Response frames in baseline spec
11be spec would need to allow NRE in a non-AP’s Probe Request frame
  This can cause inter-op issues with legacy (pre-11be) APs
Back

## Slide 26: Multi-Band element (MBE)
MBE has fields that can identify a link
  Operating Class, Channel, BSSID
  Carries Beacon Interval and TSF offset
MBE doesn’t have the format to carry MLD/Common information
All other fields are not useful from MLO advertisement point of view
Further, MBE doesn’t have the ability to carry Subelement which would be needed to carry link specific IEs such as Capabilities & Operational parameters
Back

## Slide 27: Multiple BSSID element (MBSSID)
MBSSID has the format to carry profile for each link
  Other properties such as profile straddling and non-inheritance are already defined
MBSSID doesn’t have the format to carry MLD/Common information
Using MBSSID IE for advertising multi-link information will cause legacy compliance issue
  Legacy STAs determine that an AP is MBSSID capable if they see this IE in the Beacon frame.
  Becomes an issue if a single BSSID AP advertises this IE for carrying multi-link information.
Back

## Slide 28: Reduced Neighbor Report (RNR)
RNR has fields that can identify a link
  Provides Operating Class, Channel, BSSID information
  Carries TSF offset and short SSID for reported AP
  Identifies if a reported AP is co-located and whether it is part of an MBSSID set
However, RNR doesn’t have the format to carry MLD-level/Common information
  Such information would need to be duplicated for each AP entry that belongs to that MLD
In addition, it doesn’t have the ability to carry Subelement which would be needed to carry link specific (per-AP) information such as Capabilities & Operational parameters
Further, Probe Request or Association Req/Resp frames do not carry RNR
Back

## Slide 29: Recap: Framework for MLO advertisement [4]
Contribution [4] proposes a framework for advertising MLO capabilities
MLO attributes information are classified into three categories:
  Advertising link’s Information
  MLD (common) Information
  Per-link information
Follow inheritance model that exists in 11ax (Multiple BSSID set)
Advertising Link’s Information (STA 1)
Common/MLD
STA 2
STA 3
STA 4
Information of other STAs of the MLD (link profiles)
Capabilities and parameters different from the advertising link
Non-inheritance

## Slide 30: Recap: M-BSSID feature with MLO [1]