## Slide 1: Proposals for the BA Mechanism
Date: 2020-08-11
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom |  |  | Sindhu.vema@Broadcom.com
Shubhodeep Adhikari |  |  |  | Shubhodeep.adhikari@Broadcom.com
Matthew Fischer |  | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@Broadcom.com
Vinko Erceg |  |  |  | Vinko.erceg@Broadcom.com
Notes: November 2012

## Slide 2: Abstract
This contribution discusses possible changes and enhancements to the existing AMPDU-BA mechanism to achieve improvements in efficiency related to the 802.11be multi-link feature

## Slide 3: Limitations at AMPDU Recipient
An AMPDU recipient is required to respond with BA at SIFS after the eliciting AMPDU’s PPDU
  A recipient might sometimes be incapable of transmitting the BA at SIFS due to
    RX-TX switching delay
    In device coexistence constraints
  A recipient might sometimes be incapable of receiving later MPDUs within an AMPDU due to:
    Internal processing limitations (e.g. processing delay beyond SIFS, based on MCS, byte count, MPDU count, etc)
    In-device coexistence constraints
Delayed BA might have worked here, but it was deprecated and then removed from 802.11

## Slide 4: Limitations At AMPDU Originator
Implementation constraints of MLO may require some time margin for AMPDU construction
  E.g. depending on which link gains access to the channel first and with how much bandwidth
To accommodate this time margin, a short AMPDU could precede a longer AMPDU
  Inserting SIFS+BA+SIFS between the two AMPDUs would be excessive and might cause a problem with synchronous MLD receivers
  Transmitting without rebuilding may cause unnecessary retransmission of MPDUs or transmission of MPDUs with unnecessary gaps in sequence numbers

## Slide 5: Limitations of AMPDU BA Exchange, Other (1)
The LENGTH and contents of an AMPDU cannot be adjusted once the transmission of an AMPDU starts
  LENGTH is contained in the L-SIG.
  Adjustment of LENGTH and contents is useful in case of asynchronous operation on multi-link
    I.e. events on a linkA might impact decisions regarding transmissions on a linkB (e.g. might receive BA correctly on linkA but not on linkB, and in an asynchronous manner)
  Insertion of latency sensitive traffic in an ongoing transmission would help latency
    If the arrival of a low-latency packet is anticipated, an AMPDU can start with a shorter LENGTH which will be followed by an AMPDU with low latency traffic if available, otherwise another AMPDU of longer LENGTH of the original priority

## Slide 6: Limitations of AMPDU BA Exchange, Other (2)
For long AMPDUs, if the initial PHY header is missed, decoding fails for the receiving device and preamble detection fails for any device performing CCA
  The problem can be alleviated if instead of a long AMPDU, a sequence of shorter back-to-back AMPDUs without gaps can be transmitted followed by a single composite BA.
Multiple MCSs/NSSs cannot be tried together and each combination must be tried one at a time followed by a corresponding feedback
  Convergence of the rate control algorithm can be expedited if a composite feedback can be obtained for a back-to-back AMPDU sequence with multiple MCSs/NSSs.

## Slide 7: Solutions for Recipient Capability Restriction (1)
Recipient scenario:
  Recipient cannot transmit BA after AMPDU because:
    Extended RX-TX delay due to high MCS, MPDU count, etc
    In-device coexistence
Recipient solution:
  Recipient indicates RX limitations to AMPDU originator
    Maximum MPDU count, maximum byte count to meet SIFS
    Minimum delay, maximum delay for BA transmission
    In device coexistence is possible
  Originator allows for delayed recipient response
    Determines response parameters dynamically

## Slide 8: Solutions for Recipient Capability Restriction Originator Rules
If the AMPDU originator follows the recipient’s limitations
  E.g. transmits AMPDUs which fall below the RX-TX delay limits, and recipient has not signaled that coexistence interference is present
  Originator interprets lack of BA within SIFS + slot as failure
  Otherwise, originator interprets lack of BA as delayed BA
In the case of delayed BA determination
  I.e. interpreted lack of BA as delayed BA
    Optionally continue with TXOP (i.e. after PIFS)
    Next PPDU to same recipient or other recipient(s)
  Originator assumes that the missing BA will be either:
    Transmitted using contention by the recipient
    Triggered after negotiated minimum delay x and before a maximum delay y. The expiry of maximum delay will lead to the assumption at the originator that the AMPDU is in error
    Whichever comes first

## Slide 9: Solutions for Recipient Capability Restriction Recipient Rules
Recipient exercising delayed BA
  Optionally transmits a BA with an indication of the last processed SEQ, or otherwise indicates that delayed BA is occurring
    E.g. by not responding at all within SIFS
  Eventually transmitted BA should be cumulative in terms of ACK information
    E.g. if additional AMPDUs arrive before BA is transmitted

## Slide 10: Scenario for Originator Flexibility
Originator scenario:
  AMPDU originator does not want BA after SIFS
    E.g. regardless of recipient ability to respond after SIFS
    E.g. to avoid destructive UL TX from recipient
      E.g. destructive to recipient’s ongoing RX on other link
      E.g. while testing various MCS, NSS combinations
    Serial SU DL followed by MU-triggered BA responses
    Slow link-to-link communication regarding PPDU alignment information requiring short PPDU TX while awaiting alignment information

## Slide 11: Solution for Originator Flexibility
Originator solution:
  The originator indicates delayed BA desire
    E.g. indication in PHY header or MAC header
      I.e. only to a recipient that indicates capability
    After signaling, the originator is free to transmit again after SIFS
  The originator will elicit a BA later
    E.g. using a similar signaling bit
      Maybe Ack Policy field
    E.g. using BAR

## Slide 12: Straw Poll 1
Do you support the inclusion of the following in the SFD:
  Recipient indication of constraints
    Maximum MPDU count, maximum byte count to meet SIFS
    Minimum delay, maximum delay for BA transmission
    In device coexistence is possible
  Originator indication within a PPDU that a BA transmission SIFS after the PPDU is not permitted
  Y/N/A

## Slide 13: Reference
[1] Draft P802.11REVmd_D3.4
[2] Draft P802.11ax_D6.1