## Slide 1: Proposals On Unused Bandwidth Utilizations
Date: 2020-08-11
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom | S1, Wipro Electronic City Special Economic Zone,Doddathogur, Begur Hobli, Electronic City, Bangalore, Karnataka, IND,560100 |  | Sindhu.verma@Broadcom.com
Shubhodeep Adhikari |  |  |  | Shubhodeep.adhikari@Broadcom.com
Vinko Erceg |  |  |  | Vinko.erceg@Broadcom.com
Matthew Fischer |  | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Notes: November 2012

## Slide 2: Abstract
A proposal to allow the utilization of some portion of the operating channel when another portion of the operating channel has been detected as BUSY

## Slide 3: Problem Statement
If the primary 20 MHz channel is busy, a device does not transmit on any of the portion of the operating channel, even when those portions are IDLE
Inefficient channel utilization in 802.11 is increasingly problematic with increasing operating bandwidth
  A busy 20MHz primary channel prevents a device from accessing 300 MHz of remaining BW, even when it is IDLE
Competing unlicensed technologies operating in the same bands, such as LAA and NR-U, do not have such limitations
  They are able to utilize any combination of idle subchannels

## Slide 4: Solution
The problem of inefficient channel usage can be alleviated by allowing a device to transmit on any subset of subchannels that are a part of its operating bandwidth if they are idle
  And other qualifying conditions are met

## Slide 5: TXOP Initiation
While competing for access, an AP or non-AP STA finds the primary 20 MHz channel is BUSY
  MyBSS or OBSS transmission
Proposal:
While the primary is BUSY, the STA performs CCA on other subchannels and transmits on the subchannels where CCA completes successfully

## Slide 6: Triggered Case
An AP triggers UL transmissions but identifies a subset of the triggered allocations which have not been utilized by the targeted non-AP STAs
  E.g. due to failed Trigger reception or local BUSY condition, etc which cause the targeted STA to not respond to the Trigger
Proposal:
The AP performs CCA on the unused RUs and

## Slide 7: Considerations For Access Method
The access method which allows the use of unutilized portions of the operating channel needs to:
Ensure fairness to other devices attempting to use the subchannels
  E.g. randomized access process
Adhere to regulatory rules

## Slide 8: Proposed Access Method for non-Primary Subchannels (1)
Regardless of the reason for the BUSY primary channel:
  MyBSS, OBSS or unkown, e.g. ED
CCA shall be performed on the other subchannels
Option 1:
  A device starts full CCA1 on other subchannels after it determines the primary is busy
    E.g. suitable for devices which cannot perform full CCA in parallel on multiple subchannels
    Such sequential CCA can delay gaining access on the idle non-primary subchannels

## Slide 9: Proposed Access Method for non-Primary Subchannels (2)
Option 2: A device always performs full CCA on multiple subchannels including the primary. If the primary is BUSY, CCA continues on other subchannels
  This is suitable for devices that can perform full CCA in parallel on multiple channels and reduces the delay in gaining access to non-primary channels
Definition of “Full CCA”
  ED or ED+PD
    With EDCA-style truncated exponential backoff
    +NAV?

## Slide 10: Proposed Access Method for non-Primary Subchannels (3)
For either option, when a device completes full CCA on any non-primary subchannel while the primary channel is BUSY:
  If the subset of subchannels for which full CCA has completed is part of an 802.11 bonded channel set, perform PIFS CCA on the remaining channels and transmit on those that are found to be IDLE
  If the subset of subchannels for which full CCA has completed is not part of an 802.11 bonded channel set, transmit only on those that complete full CCA together or at about the same time (e.g. using self-defer to align transmissions on the subchannels)

## Slide 11: Precedence of The Access Method
The previous behavior is specified by the ETSI harmonized standard for 5 GHz (EN 301 893)
The behavior is predicted to be copied into the ETSI rules for 6GHz
Both options are supported by LAA and NR-U.

## Slide 12: Non-primary Transmission Alignment
Transmissions on any non-primary subchannels should end at the same time as the BUSY of the primary subchannel, because:
  Supports NSTR STA access
  Allows fair access to devices that only operate EDCA using the primary 20 MHz subchannel
  “Normal” access expectations regarding the primary 20 MHz subchannel
  Allows potential transmitters and recipients to operate using single RX and TX resources
  Allows minimal resources to maintain channel state information
This is possible when PPDU length and/or NAV information is known for the BUSY primary subchannel

## Slide 13: Non-primary Transmission non-Alignment
When primary subchannel BUSY duration information is not available
  E.g. ED based BUSY, e.g. non-802.11 technology, no NAV, no PHY LENGTH
Participating STA may:
  Utilize non-Primary subchannels anyway
    Potentially be required to re-align, per other rules, if it experiences deafness on the primary subchannel
  Transmit short bursts on the non-primary channels while periodically polling the primary channel
    E.g. a compromise deafness solution

## Slide 14: NAV Loss Mitigation
If the proposal allows non-primary transmissions when a device has limited MAC resources
  E.g. the device is capable of Full CCA on only one subchannel at a time
  Then NAV and preamble information may be reduced
    When compared to NAV and preamble information that is known when always monitoring a single subchannel
Use a lower ED threshold for CCA on the non-primary channels
Use RTS/CTS for all TXOPs where the channel monitoring has been interrupted
Limit retries for a period of time

## Slide 15: Straw Poll 1
Do you support the inclusion of the following in the SFD:
  Non-primary transmission: If an AP finds that the primary channel is BUSY, it can employ techniques to access and transmit on the IDLE non-primary subchannels under TBD conditions for R2.
  Y/N/A

## Slide 16: Straw Poll 2
Do you support the inclusion of the following in the SFD:
  To handle missed NAV information on non-primary channels before selecting them for transmission when performing non-primary transmission, that the following mechanisms should be used:
    EDCA uses a lower (TBD) ED threshold
    TXOPs are initiated on the non-primary subchannels with an RTS/CTS exchange
Y/N/A

## Slide 17: Straw Poll 3
Do you support the inclusion of the following in the SFD:
    On returning to the primary subchannel after transmitting using non-primary transmission, a device shall start a MediumSyncDelay timer for the primary subchannel, unless it had a non-zero PPDU length or non-zero NAV on the primary channel and ended the TXOP on the non-primary channel(s) within that non-zero time
    The MediumSyncDelay timer expires after a TBD duration or if the STA receives a PPDU with a valid MPDU or receives a PPDU with a valid TxOP_duration, whichever happens first
    While the MediumSyncDelay timer is running the device is allowed to attempt to initiate up to TBD (>=1) TxOPs using RTS and a TBD ED threshold
Y/N/A

## Slide 18: Straw Poll 4
Do you support the inclusion of the following in the SFD:
  An AP can recover unused but allocated RUs which correspond to a previously transmitted Trigger, under TBD conditions and if the AP determines such RUs to be IDLE using TBD conditions
  Y/N/A

## Slide 19: Reference
[1] Draft P802.11REVmd_D3.4
[2] Draft P802.11ax_D6.1

## Slide 20: Annex

## Slide 21: Unused RU Recovery
If an AP transmits a Triger and some allocated RUs are not used
An AP that is capable of simultaneously transmitting and receiving data on the combination of used and unused RUs
  May perform RU recovery
  See next slide

## Slide 22: Unused RU Recovery Option 1
Treat the unused channels as a continuation of the same Triggered TXOP
The AP is allowed to recover within a short gap
Both IEEE 802.11 and the ETSI harmonized standard for 5 GHz (EN 301 893) permits a maximum gap of 25us
  CCA can be based on Energy Detection for the last 9us in the 25us gap
Collision unlikely because of previous TXOP activity

## Slide 23: Unused RU Recovery Option 2
Start a new TXOP within the unused RUs
  Using a new CCA process
This option does not have a timing requirement
  Therefore, the access time will be increased

## Slide 24: Unused RU Recovery Alignment
It is beneficial for the AP to align the end times of any recovery transmissions with the ongoing triggered transmissions on the other RUs
  Easy for the AP, which is aware of the duration of the ongoing triggered transmissions
No further restrictions are needed for this procedure
  E.g. no ED, RTS/CTS, limited retries
  AP already owns the TXOP