## Slide 1: U-SIG Structure and Preamble Processing
Date: 2020-03-15
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
EHT has adopted
  A 2 symbol U-SIG after RL-SIG
    The U-SIG will contain version independent fields
    The intent of the version independent content is to achieve better coexistence
  EHT-SIG
    Variable MCS and variable length, immediately after the U-SIG
The structure of U-SIG and encoding structure of EHT-SIG across frequency has not been decided yet
In these slides we propose the following
  U-SIG content variation across 80MHz channels
  Preamble processing requirements

## Slide 3: Review: BW and Punctured Channel Info in 11ax
In 11ax, the HE-SIG-A carries the BW field which tells about the puncturing pattern (at content channel level) in the primary 80MHz
  Sufficient information to tell the intended recipients about how to decode the two SIG-B content channels within the [1 2 1 2] encoding structure in primary 80MHz
However, HE-SIG-A gets duplicated in every 80MHz and does not convey anything about the puncturing pattern of non-primary 80MHz
Implication of above is that an 80MHz-operating-mode device cannot park on a non-primary 80MHz channel
  Not enough information to decode the SIG-B field in a non-primary 80MHz
    Which channels are active in the [1 2 1 2] structure of a non-primary 80MHz is unknown
Improve this going forward, especially with the advent of 320MHz in 11be
  80MHz devices parked on non-primary should be able to get enough information to decode EHT-SIG from the U-SIG of that 80MHz

## Slide 4: PPDU BW & Punctured Channel Info in U-SIG
Main idea: Allow the punctured channel information carried in U-SIG to vary across different 80MHz channels, i.e. puncturing information in an 80MHz is specific to only that 80MHz
This enables devices of lower BW capability (e.g., 80MHz-operating-mode device) to park on different 80MHz
  The device can get all the SIG content channels by looking at the 80MHz it is parked on
    Assuming SIG field encoding structure will still have 80MHz duplication like 11ax
  Note: This implies that U-SIG content can vary from one 80MHz to the next

## Slide 5: Illustration of an 80MHz-operating-mode device benefitting from the proposed design
Punctured 20MHz channel
Punctured 20MHz channel
Example shown below is for a 160MHz PPDU to aid simpler illustration
  The concept is very much applicable to 320MHz as well
U-SIG1 and U-SIG2 below are the U-SIG fields carried in the primary 80MHz and secondary 80MHz respectively
  They have different contents as the puncturing patterns in the two 80MHz are different
U-SIG2
U-SIG2
U-SIG2
U-SIG1
U-SIG1
U-SIG1
Primary
80MHz
Secondary
80MHz
An 80MHz-operating-mode STA parked here can decode the
EHT-SIG content channels from this 80MHz
as U-SIG2 indicates that the third 20MHz is punctured
EHT-SIG

## Slide 6: Preamble Processing: EHT SIG Encoding Structure
We would like an EHT device to be required to process ONLY one 80MHz channel as far as the pre-EHT section of the preamble is concerned
  No 80MHz segment change should be needed while receiving the pre-EHT section
  Want to limit complexity of preamble processing
Implications on encoding structure of EHT-SIG
  EHT-SIG in one 80MHz segment should convey to each device monitoring that 80MHz channel its complete assignment information
    Even if the assignment is outside that 80MHz segment

## Slide 7: Summary
We proposed the following
  Allow the U-SIG content to vary from one 80MHz to the other
    Carry each 80MHz’s puncturing channel information in that 80MHz
      This can enable 80MHz-operating-mode devices to park on any 80MHz
  EHT devices should be required to monitor only one 80MHz preamble segment

## Slide 8: SP 1
Do you agree with allowing information in U-SIG to vary from one 80MHz to the next in an EHT PPDU of bandwidth >80MHz?
  Notes
    Each STA still needs to decode only one 80MHz segment in U-SIG
    Within each 80MHz, U-SIG is still duplicated in every non-punctured 20MHz

## Slide 9: SP 2
Do you agree that there will be puncturing information in U-SIG which is allowed to vary from one 80MHz to the other?
  U-SIG in each 80MHz signals the puncturing information of that specific 80MHz

## Slide 10: SP 3
Do you agree that a STA only needs to process up to one 80MHz segment of the pre-EHT preamble (up-to and including EHT-SIG) to get all the assignment information for itself?
  No 80MHz segment change is needed while processing L-SIG , U-SIG and EHT-SIG