## Slide 1: Power save state after multi-link setup
Date: 2020-03-15
Authors:

## Slide 2: Objective
Multi-link setup procedure was agreed to setup multiple links between an AP MLD and an non-AP MLD.
During that procedure, depending on the negotiated TID-to-link mapping, multiple links will be enabled
  We agreed that the default mapping is that all TIDs are mapped to all setup links and all links are enabled
Once this is settled (after multi-link setup), STA is able to change its power save states on each link independently.
What is currently not defined is: what is the initial power save state of the STAs on each link, right after the multi-link setup exchange.
  That’s what we propose to define in this contribution

## Slide 3: Example to better understand
Typical example:
  AP MLD operating on 3 links (2.4/5/6GHz)
  Non-AP MLD with 3 links (2.4/5/6GHz), but with single radio functionality (only one STA of the non-AP MLD can be awake at a time)
  3 links are setup with default mapping:
    TIDs mapped to all 3 links, all 3 links enabled

## Slide 4: Baseline rules and proposal
Baseline spec defined association on a single link, and mandates that the power save mode of the STA, right after the end of the association process, is the active mode (power save state therefore in awake state).
  Following this, STA can obviously change its power state/mode as it wants.
On the link on which multi-link setup frames are exchanged, we propose to follow the same approach:
  STA is in active mode
On the other links that become enabled, we propose that the initial state is doze state (in power save mode).
  Only possible option for our single radio non-AP MLD in the example in previous slide
  Most logical solution also for multi-radio non-AP MLDs to save power
  Obviously, right after this, STA can change its power mode/state through specific signaling

## Slide 5: Straw polls
Do you agree to add to the 11be SFD:
  When a link becomes enabled for a STA that is part of a non-AP MLD through multi-link setup sent on that link, the initial power management mode of the STA, immediately after the signaling exchange, is active mode
  When a link is enabled for a STA that is part of a non-AP MLD through signaling (multi-link setup or TID to link mapping update) send on another link, the initial power management mode of the STA, immediately after the exchange, is power save mode, and its power state is doze