## Slide 1: Beacon, Capability, Operating Parameters
Date: 2020-03-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Multi-band Operation
An STA MLD associates with an AP MLD through one association.
  Common capabilities (capability applying to all bands), per band capabilities.
  Common operation parameters, per band operation parameters.
  Operation Negotiation (BA, security, channel switch, BW update etc.)
    Common operation negotiation (single negotiation applying to all bands), per band operation negotiation.
  UP layer interface:
    No change to MAC data service specification,
    MLME SAP primitives may be changed for per band MLME SAP primitives.

## Slide 3: Capability and Operation Parameters of MLD
An AP/STA MLD may have different capability in different links.
An AP MLD may announce different operating parameters for different links.
The elements without link indication are the elements announced for the link where the frame is transmitted.
Elements for other link has link identifier to indicate the link, e.g. STA Profile.
The following is the possible element format (ML element with STA Profile being encapsulated):
  ML element is used for discovery/association, cross-link management.
  The Common Info and STA Profile may not be required, e.g. in management other than discovery and association.
Element ID = 255
Length
Element ID Extension
Link ID
subelements
STA Profile n
……
Link ID
subelements
STA Profile 1
Common Info
May not be needed for the purpose other than the discovery, association.

## Slide 4: Inherited and Non-inherited Element
An indication about whether the inheritance is applied in ML element.
When the inheritance is applied, the following operations are applied
  the capabilities, operating parameters of the reported STA that are not carried in the management frame in reported STA’s Profile are inherited from the capabilities and operating parameters of the reporting STA.
  A reported STA may not want to inherit an element from the reporting STA.
    To address this, a Non-Inherited element can be used to explicitly indicate the uninherited elements from the reporting STA.
      If an Element ID and Element ID Extension, if exists, are included in Non-Inherited element of a reported STA’s STA Profile, the element identified by the Element ID and Element ID Extension, if exists, is not inherited by the reported STA.

## Slide 5: Beacons of Multi-link AP/STA Entity
Given that a multi-link AP entity transmits Beacons in each its enabled link, the following information announcement rules are applied to avoid the Beacon bloating (with example of MLD of two links):
  In Beacon frames of link2, the information for frame exchange of link1, e.g. the Capabilities, Operating Parameters, e.g. EDCA, MU EDCA, OFDMA random access parameters, Spatial Reuse parameters, BSS Operating Parameters etc. of link1 are not announced.
  In Beacon frames of link2, the information for receiving Beacons of link1, helping the association decision, further information acquirement, e.g. the Primary channel, BW, TSF Difference between Two Link, link1 AP and link2 AP being affiliated with same AP MLD, Check Beacon, Link ID etc.
    The updated the current element, i.e. RNR, can be defined for such announcement.
  Similar rules are applied to broadcast Probe Response frames.

## Slide 6: Capabilities, Operating Parameters in Scanning, Association
The individually addressed Probe Request transmitted in one link can request the full capabilities and BSS operating parameters of other links.
  Probe Request indicates the requirement of other link’s full capabilities, operating parameters.
  The individually addressed Probe Response frame in one link carry the full capabilities and BSS operating parameters of other links.
The Association Request and Association Response in one link need to carry the full capabilities and BSS operating parameters of other links.

## Slide 7: Further Consideration of Decreasing Management Overhead
Multiple STA MLD may request full AP MLD information of all affiliated APs before the AP MLD sends individually addressed Probe Response frame.
  Instead of multiple individually addressed Probe Response frames, a broadcast Probe Response frame with full AP MLD information of all affiliated APs of the requested AP MLD can be transmitted.
  If the transmission of such broadcast Probe Response frame is near TBTT, a Beacon with full AP MLD information of all affiliated APs of the requested AP MLD can be transmitted.
  In such frames, the full MLD information of only one AP MLD that is requested is carried.
    The partial information of other AP MLDs is carried.

## Slide 8: Straw Poll 1
Do you support that an reporting AP of the AP MLD transmits the Beacons and broadcast Probe Response frames carries the partial information of all other APs affiliated with the same MLD as the reporting AP through enhanced RNR element?

## Slide 9: Straw Poll 2
Do you support that a STA of a STA MLD can send a Probe Request frame to an AP of an AP MLD to request the full capabilities, operating parameters of all APs of the AP MLD?

## Slide 10: Straw Poll 3
Do you support to use the inheriting mechanism similar to 11ax such that
  By default, if the capabilities, operating parameters of the reported STA are not carried by the STA Profile of the reported STA, those capabilities, operating parameters of reported STA are inherited from the capabilities, operating parameters of the reporting STA
  Inf the Element ID or Element ID and Element ID Extension is included in the Non-Inherited element of the STA Profile of the reported STA, the related element is not inherited from the reporting STA.

## Slide 11: Straw Poll 4
Do you support to define a mode where no-inheritance is applied to the reported AP?