## Slide 1: EHT BSS with Wider BW
Date: 2020-03-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Multiple BSSID
A single-radio AP device can own multiple virtual APs:
  Only one AP that has transmitted BSSID transmits management frame frames. The BSSIDs of the other APs are non-transmitted BSSID.
  The Multiple BSSID element defines the non-transmitted BSSID profiles for APs that have non-transmitted BSSIDs.
  The non-transmitted BSSID can be figured out through the Multiple BSSID element.
  Multiple BSSID Configuration element defines the actually number of non transmitted BSSID APs.
  The non-transmitted profile of a non-transmitted BSSID in the management frame doesn’t need to carry an element of the AP’s capabilities or operating parameters that is same as the related element of the transmitted BSSID.
    One example is that if the EDCA Parameter Set element is not in the non-transmitted BSSID profile of an AP with non-transmitted BSSID ( e.g. AP2), the EDCA Parameter Set element in the management frame will be used by the STAs associated with AP2.
  An AP with non-transmitted BSSID may announce the non-inheritance of element from the AP with transmitted BSSID.
    One example is that in non-Transmitted BSSID Profile of non-transmitted BSSID1, if the Element ID of EDCA Parameter Set is in List Of Element IDs field, the EDCA Parameter Set element in the management frame will not be used by the STAs associated with AP of BSSID1.
BSSID1,
BSSID2
BSSID3,
BSSID4
Multiple BSSID AP
Transmitted BSSID
Multiple BSSID element
Multiple BSSID Configuration element
Non-inherit element

## Slide 3: Recap: AP MLD
An AP multi-link device (MLD) includes multiple APs:
  Each AP works in different link.
  All the APs share the same security policy, BA agreement, SSID, same MAC SAP.
  The APs have different medium access procedures.
  Each AP may transmit its own management frames with different TSF time, BI, TBTT etc.
  When an AP of an AP MLD transmits a management frame in link1, the management frame doesn’t need to carry a element of another AP’s capabilities or operating parameters in link2 if the element is same as the related element in link1.
  In a management frame of link1, the information of an AP in link2 may not include an element of the specific capabilities or operating parameters, and the AP in link2 doesn’t want to inherit the related element in link1
    The non-inherit Information (identified by the Element ID, Element ID Extension) can be announced to let the STAs associated with the AP in link2 know the element that are not inherited from the AP that transmitted the management frame in link1.
  The AP MLD transmits buffered frame indication of one link in another link.
    The buffer indication of the other link takes effect right away or after the following TBTT of another link.
      No indication about whether this applied to unicast or group-addressed frames. This may not be applicable to group addressed frames.
Multi-link AP device
MAC with Addr1
MAC with Addr1
Common MAC
Link1
Link2
SAP of BSSID1 (addr1)
BSSID1’s management frame
capabilities, operation parameters of AP with BSSID1
Link ID, SAP Addr, capability, operation parameters of AP with BSSID2

## Slide 4: Number of AP MLD with Multiple BSSID in Multiple Links
It is not required that when one link implements multiple BSSID, another link also needs to implement multiple BSSID.
  5GHz legacy STAs, 6GHz HE STAs, and 5GHz + 6GHz STA MLDs
When two links implement multiple BSSID, the following are the relationship of them:
  Option 1:
    If an AP in a link that is affiliated with an AP MLD has transmitted BSSID, the AP in another link that is affiliated with the same AP MLD is the transmitted BSSID.
      Option 1.1: The Multiple BSSID elements in different links define the same number of non-transmitted BSSIDs.
      Option 1.2: The Multiple BSSID elements in different links define the different number of non-transmitted BSSIDs.
  Option 2:
    If an AP in a link that is affiliated with an AP MLD has transmitted BSSID, the AP in another link that is affiliated with the same AP MLD can be a non-transmitted BSSID.
      Option 2.1: The Multiple BSSID elements in different links define the same number of non-transmitted BSSIDs.
      Option 2.2: The Multiple BSSID elements in different links define the different number of non-transmitted BSSIDs.
We prefer option 2.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.

## Slide 5: BSS Parameter Transmission Method1 of AP MLD with Multiple BSSID
The transmitted BSSID AP (APxa) in link_x transmits management frames with the following information:
  APxa’s capabilities and operating parameters
  APxa’s non-transmitted BSSID profiles of the non-transmitted BSSIDs in link_x
  the AP capabilities and BSS operating parameters of transmitted BSSID AP (APya) in link_y,
  APya’s Non-transmitted BSSID Profile with AP capabilities and BSS operating parameters of the non-transmitted BSSIDs in link_y.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.
AP11’s management frame
Elements related to AP11
Non-transmit BSSID Profiles subelement for AP12, AP13, AP14
Elements for AP11’s capabilities, operating parameters
(Sub)Elements for AP21’s capabilities, operating parameters
Non-transmit BSSID Profiles subelement for AP22, AP23, AP24
AP21’s management frame
Elements related to AP21
Non-transmit BSSID Profiles subelement for AP22, AP23, AP24
Elements related to AP11 (may be one element to carry multiple subelement or multiple element with Link ID)
Elements for AP21’s capabilities, operating parameters
(Sub)Elements for AP11’s capabilities, operating parameters
Non-transmit BSSID Profiles for AP12, AP13, AP14
Elements related to AP21 (may be one element to carry multiple subelement or multiple element with Link ID)

## Slide 6: BSS Parameter Transmission Method 2 of AP MLD with Multiple BSSID
This method assume that the transmitted BSSIDs of multiple links can be affiliated with different AP MLDs.
The method 2 to transmit BSS parameters:
  APxa’s capabilities and operating parameters
  APxa’s non-transmitted BSSID profiles of the non-transmitted BSSIDs in link_x
    each non-transmitted BSSID profile of link_x’s APxb includes the capabilities, operating parameters of link_y’s APyb where APxb and APyb are owned by same AP MLD
  the AP capabilities and BSS operating parameters of transmitted BSSID AP (APyb) in link_y.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.
AP11’s Beacon
Elements related to AP11
Non-transmit BSSID Profiles subelement for AP12, AP13, AP14. The capabilities, operating parameters of AP22, AP23, AP24 are in AP12, AP13, AP14’s non-transmit BSSID Profiles respectively
Elements for AP11’s capabilities, operating parameters
Elements related to AP21 ((Sub)Elements for AP21’s capabilities, operating parameters)
AP21’s Beacon
Elements related to AP21
Non-transmit BSSID Profiles subelement for AP22, AP23, AP24. The capabilities, operating parameters of AP12, AP13, AP14 are in AP22, AP23, AP24’s non-transmit BSSID Profiles respectively
Elements for AP21’s capabilities, operating parameters
Elements related to AP11 ((Sub)Elements for AP11’s capabilities, operating parameters)

## Slide 7: Methods to Decrease Management Overhead with Multiple BSSID
When APx1 in link_x and APy1 in link_y are affiliated with one AP MLD, APy1 that is non-transmitted BSSID may inherit the capabilities or operating parameters from the following AP in management frame of Link_x:
  Level 1 inherit variant 1: the capabilities or operating parameters of APx1 where APx1 in link_x and APy1 are affiliated with the same AP MLD.
    Here is an example:
      APy2 is the transmitted BSSID in link_y,
      the operating parameters of APy1 in management frame of link_x don’t include EDCA parameter set,
      APx1 in link_x and APy1 are affiliated with a AP MLD,
      the operating parameters of APy2 in management frame of link_x include EDCA parameter set 1.
      the operating parameters of APx1 in management frame of link_x include EDCA parameter set 2.
      the STAs in link_y that are associated with APy1 have EDCA parameter set 2.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.

## Slide 8: Methods to Decrease Management frame Overhead with Multiple BSSID
When APx1 in link_x and APy1 in link_y are affiliated with one AP MLD, APy1 that is non-transmitted BSSID may inherit the capabilities or operating parameters from the following AP in management frame of Link_x:
  Level 1 inherit variant 2: the capabilities or operating parameters of APy2.
    Here is an example:
      APy2 is the transmitted BSSID in link_y,
      the operating parameters of APy1 in management frame of link_x don’t include EDCA parameter set,
      APx1 in link_x and APy1 are affiliated with a AP MLD,
      the operating parameters of APy2 in management frame of link_x include EDCA parameter set 1.
      the operating parameters of APx1 in management frame of link_x include EDCA parameter set 2.
      the STAs in link_y that are associated with APy1 have EDCA parameter set 1.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.

## Slide 9: Methods to Decrease Management Frame Overhead with Multiple BSSID
When APx1 in link_x and APy1 in link_y are affiliated with one AP MLD, APy1 that is non-transmitted BSSID may inherit the capabilities or operating parameters from the following AP in management frame of Link_x:
  Level 2 inherit: The capabilities or operating parameters of APx2 that APx2 is the transmitted BSSID.
    Here is an example:
      APy2 is the transmitted BSSID in link_y,
      the operating parameters of APy1 in management frame of link_x don’t include EDCA parameter set,
      APx1 in link_x and APy1 are affiliated with a AP MLD,
      the operating parameters of APy2 in management frame of link_x doesn’t include EDCA parameter set.
      the operating parameters of APx1 in management frame of link_x doesn’t include EDCA parameter set.
      the STAs in link_y that are associated with APy1 have EDCA parameter set of APx2.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.

## Slide 10: Methods to Decrease Management Frame Overhead with Multiple BSSID
Predefined priority:
  Priorities to select the inherited element:
    Level 1 inherit > Level 2 inherit.
  Which one is used of two Level 1 inherit variants
      Level 1 inherit option 1: One of them is always selected. If the predefined level 1 is not there, level 2 is used.
      Level 1 inherit option 2: One of them has high priority than another one. And the one with low priority has higher priority than Level 2
Explicit Priority:
  In link_x management frame, the elements being inherited by link_y’s AP from one of link_x’s AP with transmitted BSSID, link_x’s AP with non-transmitted BSSID, link_y’s AP with transmitted BSSID are explicitly announced.

## Slide 11: Straw Poll 1
Do you support that it is not required that when one link implements multiple BSSID, another link also needs to implement multiple BSSID?

## Slide 12: Straw Poll 2
Do you support that if an AP in a link that is affiliated with an AP MLD has transmitted BSSID, the AP in another link that is affiliated with the same AP MLD is not required to be the transmitted BSSID?