## Slide 1: EHT BSS with Wider BW
Date: 2020-03-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Assumption of BSS with Wider BW and Channel Puncture
A BSS can have punctured operating channel or unpunctured operating channel.
An AP announces its primary 20MHz channel and the BSS operating channel.
The BSS operating channel can be dynamically punctured.
A STA whose BW is narrower than an AP’s BW can associate with the AP.
  The STA can park in a subchannel that doesn’t cover AP’s 20MHz primary channel secondary subchannel.
    Subchannel is a group of continuous 20MHz channels of BSS operating channel, e.g. in a 320MHz BSS the primary 80MHz channel (primary subchannel), the secondary 80MHz channel (secondary subchannel), 3rd 80MHz channel (secondary subchannel), 4th 80MHz channel (secondary subchannel).
A STA/AP with BW wider than 20MHz detects a >=20MHz PPDU through the primary 20MHz channel.
  Some rules should be defined for the puncture operation of a STA parks in a subchannel without covering primary 20MHz channel.
A STA has smaller maximal Tx power than AP.
160MHz BSS1 with one 20MHz
channels being punctured
160MHz BSS2 without
Punctured 20MHz channels.
TXOP BW in BSS1
TXOP BW in BSS2
BSS operating channel
Primary 20MHz channel
BSS operating channel
Primary 20MHz channel

## Slide 3: Recap: BSS Operating Parameter Announcement
EHT Operation element includes: 1-bit Channel BW (320/160+160 or not), EHT CCFS.
  If Channel BW is no more than 160/80+80MHz, HE/VHT/HT Operation element is used to announce the BW.
  If Channel BW is 320/160+160MHz, EHT CCFS and CCFS1/2 are used to decide whether the BSS has 320 MHz BW or 160+160 MHz BW.
  Problem with such design:
    When some 20MHz channel within primary 80MHz channel, primary 160MHz channel are punctured, it is not clear how to avoid 11ac/ax STAs to use punctured 20MHz channels.
320MHz BSS with two 20MHz
channels being punctured
Primary 20MHz channel

## Slide 4: Solution 1: Operating Mode Notification + HT/VHT/HE/EHT Operation Element
When some 20MHz channels in the BW announced by VHT/HE Operation element are punctured, the Operating Mode Notification combined with VHT/EHT Operation element is used to announce the BW for HE/VHT unpunctured TW.
Additional rules for such combination:
  When both Operating Mode Notification and EHT Operation element are carried, the EHT Operation element is used for EHT operation;
  When Operating Mode Notification is always combined with VHT/HE/EHT Operation element, the carrying of Operating Mode Notification whose content is not updated is not critical event.

## Slide 5: Solution 2: Unpunctured BW Announced in HT/VHT/HE/EHT Operation Element
An EHT AP/STA uses HT/VHT/EHT Operation element to announce the BW that is not more than 160/80+80MHz and doesn’t include punctured 20MHz channels
BW in EHT Operation element:
  Option 1: Beside 320/160+160MHz BW, an EHT AP/STA announces the BW that is less than 160/80+80MHz in EHT Operation element when the BW includes punctured 20MHz channels:
    0……the BW is less than 80MHz;
      One alternative to this is that when EHT Operation element show no channel puncture, 0 means the BW is no more than 160/80+80MHz.
    1……the BW is 80MHz;
    2……the BW is 160/80+80MHz;
    3……the BW is 320/160+160MHz.
  Option 2: an EHT AP/STA announces the BW that is more than 40MHz:
    0……the BW is less than 80MHz;
    1……the BW is 80MHz;
    2……the BW is 160/80+80MHz;
    3……the BW is 320/160+160MHz.

## Slide 6: MCS, Nss, Channel Puncture
For a BW <=160MHz/80MHz+80MHz, the EHT MCS, NSS are no less than the HE MCS, NSS respectively.
240MHz BW announcement:
  Option 1: 240MHz BSS is a 320MHz BSS with 80MHz channel being punctured (preferred option).
  Option 2: 240MHz is announced by the BW field.
Allowed EHT BSS Channel Puncture
  Option 1 (preferred option):
    The puncture patterns of EHT SU/MU PPDU being addressed to a single STA/AP are the only allowed BSS operating channel punctures.
  Option 2:
    The allowed BSS operating channel punctures are more than the puncture patterns of EHT SU/MU PPDU being addressed to a single STA/AP.
    Per 20MHz channel bitmap can be used to describe the BSS operating channel puncture.
EHT BSS Channel Puncture Coding:
  Option 1:
      Joint coding (compressed coding) can be used to describe the BSS operating channel puncture.
  Option 2 (preferred option):
      Per 20MHz channel bitmap can be used to describe the BSS operating channel puncture.

## Slide 7: Narrower BW of Responding Frame
When an AP transmits a PPDU to a STA with wider BW, e.g. 160MHz or 320MHz, and the STA with smaller Tx power transmits the responding frame in 160MHz or 320 MHz BW, the AP may not be able to decode the frame.
  One restriction could be that the frame exchange that the responding frame uses narrower BW is the only frame exchange or last frame exchange of a TXOP.
The TXOP holder decides the BW and the other parameters of the responding frame transmitted by the TXOP responder where he responding frame can be transmitted in narrower BW.
    The AP can transmit a Trigger frame with other frames to solicit the responding frame, and the Trigger frame announces narrower BW for the TB PPDU.
    The AP can transmit a trigger information in HE Control field to solicit the responding frame in TB PPDU, and the trigger information announces the narrower BW for the TB PPDU.
160MHz BSS2
Primary 80MHz
Secondary 80MHz
Primary 20MHz
EHT/HE SU/MU PPDU
BA in 40MHz
HB PPDU
A-MPDU with Trigger frame
to STA 1

## Slide 8: Narrower BW of Responding Frame (Cont’d)
The TXOP responder decides the BW and the other parameters of the responding frame.
  The responding frame can be transmitted in narrower BW.
  The PPDU can be VHT/HE/EHT PPDU.
    Less Tx time that the time for non-HT duplicate PPDU is used.
160MHz BSS2
Primary 80MHz
Secondary 80MHz
Primary 20MHz
EHT/HE SU/MU PPDU
BA in 40MHz
HE SU PPDU
A-MPDU to STA 1

## Slide 9: Problem and Solution with STAs Parking in Secondary Subchannel
A STA that parks in secondary subchannel may miss the RU when dynamic puncture is applied to a MU PPDU or SU PPDU.
160MHz BSS2 without punctured
20MHz channels.
TXOP BW in BSS2
Primary 80MHz
Secondary 80MHz
STA1’s RU
80MHz STA1 decodes PPDU
starts at this 20MHz channel.
STA1 misses the PPDU.
A STA and the associated AP agree the 20MHz channel where the STA starts to decode the L-SIG and HE/EHT SIG.
  Various methods can be defined.

## Slide 10: Unpunctured 20MHz Channel
For each secondary subchannel, a unpunctured 20MHz channel is defined.
  The STAs park in secondary subchannel group detects PPDU start from the unpunctured 20MHz channel.
  The unpunctured 20MHz channel is never punctured.
160MHz BSS2 without punctured
20MHz channels.
Primary 80MHz
Secondary 80MHz
Primary 20MHz
unpunctured 20MHz
Allowed TXOP
BW in BSS2
Disallowed TXOP
BW in BSS2

## Slide 11: Announcement of Unpunctured 20MHz Channel
The unpunctured 20MHz channel can be one of the following
  1) announced by the AP,
  2) the 20MHz channel in a 20MHz channel set that is closest to the 20MHz primary channel (e.g. with smallest frequency difference).
For the announcing method, an AP announces the unpunctured 20MHz channel in the management frames, e.g. Beacon, Probe Response, (Re)Association Response frame, new defined action frame.
160MHz BSS2 without punctured
20MHz channels.
Primary 80MHz
Secondary 80MHz
Primary 20MHz
unpunctured 20MHz
Allowed TXOP
BW in BSS2
Disallowed TXOP
BW in BSS2
160MHz BSS1 with one 20MHz
channels being punctured

## Slide 12: Updating of Unpunctured Channel
The AP announces the future unpunctured 20MHz channel and the time when it will be used, e.g. the future TBTT.
unpunctured 20MHz
160MHz BSS2
160MHz BSS2
Announce the current and future unpunctured
20MHz channel being used after 4 BI
Announce the current and future unpunctured
20MHz channel being used after 3 BI
Announce the current and unpunctured
20MHz channel being used after 2 BI
Announce the current and future unpunctured
20MHz channel being used after 1 BI
Announce the current unpunctured
20MHz channel
160MHz BSS2
160MHz BSS2
160MHz BSS2

## Slide 13: Usage of Unpunctured 20MHz Channel
An AP can use one of the unpunctured 20MHz channels to do backoff.
  The change of 20MHz channel where backoff is done can be unannounced or announced.
  This can provide fairness between STAs parked in primary subchannel and STAs parked in secondary subchannels.
unpunctured 20MHz
160MHz BSS2
Primary 20MHz
40MHz TXOP
Punctured TXOP (40+20MHz)
AP decides to use unpunctured
20MHz channel to do backoff.
AP uses primary 20MHz
channel to do backoff.
Punctured TXOP (40+20MHz)

## Slide 14: STA’s Operating Parameter Change, TXOP BW
When a STA that parks in a secondary subchannel changes its operating BW, the STA’s operating BW always covers the unpunctured 20MHz channel.
When an AP announces a TXOP BW of a STA that parks in one secondary subchannel, the BW will always cover the unpunctured 20MHz channel.
160MHz BSS2 without punctured
20MHz channels.
Primary 80MHz
Secondary 80MHz
Primary 20MHz
unpunctured
20MHz
80MHz STA parking in secondary 80MHz
channel changes its operating BW to 40MHz.

## Slide 15: Straw Poll 1
Which one do you support that:
  Option 1: EHT Operation element includes: 1-bit Channel BW (320/160+160 or not), EHT CCFS.
  Option 2: An EHT AP/STA uses HT/VHT/EHT Operation element to announce the BW that is not more than 160/80+80MHz and doesn’t include punctured 20MHz channels
    an EHT AP/STA announces the BW of 320/160+160MHz and the BW that is less than 160/80+80MHz in EHT Operation element when the BW includes punctured 20MHz channels.

## Slide 16: Straw Poll 2
Do you support that:
  EHT Operation element includes: 1-bit Channel BW (320/160+160 or not), EHT CCFS.
  When some 20MHz channels in the BW announced by VHT/HE Operation element are punctured, the Operating Mode Notification combined with VHT/EHT Operation element is used to announce the BW for HE/VHT unpunctured TW.
  When both Operating Mode Notification and EHT Operation element are carried, the EHT Operation element is used for EHT operation.

## Slide 17: Straw Poll 3
Do you support that for a supported BW <=160MHz/80MHz+80MHz, the EHT MCS, NSS are no less than the HE MCS, NSS respectively.

## Slide 18: Straw Poll 4
Do you support that a PPDU with the frames addressed to a STA can carry the triggering information (Trigger frame or TRS) to solicit a BA or Ack in a TB PPDU whose BW is less than the soliciting PPDU if the soliciting PPDU is the only PPDU that carries the QoS Data frames in the TXOP?