## Slide 1: Efficient EHT Preamble Design
Date: 2019-11-18
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek |  |  | jianhan.liu@mediatek.com

## Slide 2: Introduction
Extreme high throughput (EHT) WLAN are based on the upcoming IEEE 802.11be standards.
EHT WLAN will enable 240MHz and 320MHz BW PPDU and multiple resource units aggregations.
  To enable such features, preamble design based on IEEE 802.11ax/ac is not efficient because the length of the preamble can be very long.
We propose an efficient preamble design that allows different signaling information conveyed on different 80MHz segment.

## Slide 3: Agreed format of EHT PPDU
In [1], the agreed format of an EHT PPDU is shown in the following figure.
  The detection of EHT PPDU based on The LENGTH field in L-SIG and RL-SIG to a value N such that mod(N, 3) = 0.
U-SIG:
  There shall be a 2 OFDM symbol long, jointly encoded U-SIG in the EHT preamble immediately after the RL-SIG.
    The U-SIG will contain version independent fields. The intent of the version independent content is to achieve better coexistence among future 802.11 generations.
    In addition, the U-SIG can have some version dependent fields.
EHT-SIG:
  A variable MCS and variable length EHT-SIG, immediately after the U-SIG, in an EHT PPDU.

## Slide 4: Per-80MHz preamble signaling
To reduce the length of EHT SIG, per-80MHz preamble signaling is preferred.
  U-SIG only duplicates within each 80MHz
  Each 80MHz can have different U-SIG and EHT-SIG
  EHT-SIG for each 80MHz segment has two or more content channels.
This implies that each STA must know in which 80MHz its content channels are located before receive this EHT PPDU.
  Each STA only need to process the preamble (including STFs and LTFs) in one 80MHz.
  HE subchannel selective transmission defined in IEEE 802.11ax can be used for 80MHz channel selection.

## Slide 5: Per-80MHz preamble signaling (cont’s)
EHT-SIG in one 80MHz segment can contain assigned RU larger than 80MHz and also can contain assigned RU in other 80MHz segment.
  For stations support 160/240and 320MHz BW.
  EHT-STF and EHT-LTFs are used to adjust AGC and channel estimation.
For 80MHz only STA, EHT-SIG in the 80MHz segment can only contain assigned RU within this 80MHz segment.
Stations operated on non-primary 80MHz channel can only receive DL PPDUs or be triggered for uplink transmission on this non-primary 80MHz channel.
  If stations operated on non-primary 80MHz channel wants to transmit by itself, these stations need to switch to primary channel and contend on primary channel.

## Slide 6: BW and Punctured Indication in U-SIG
“BW” and “Puncture” indications are contained within U-SIG and U-SIG content can be different for each 80MHz.
  “Puncture” indication only indicates the puncture of the corresponding 80MHz sub-channel, so 3 or 4 bits are enough for puncture indication.
  May allow “BW” is different for different 80MHz channel
    For example, in one 80MHz, the BW is 160MHz, for another 80MHz, the BW is 80MHz.
    This allows small BW STAs operate in large BW PPDU.
For BW and puncture indications, probably 6 or 7 bits are needed in U-SIG.

## Slide 7: EHT-SIG Content Channels
EHT-SIG can carry different contents in each 80MHz
  Each station knows the position of its content channels before reception the 11be PPDU.
  RU allocation, modulation informations for target stations are carried in the content channels in EHT-SIGs.
    EHT-SIG for each 80MHz segment can have two content channels similar to 11ax HE-SIGB.
    EHT-SIG for each 80MHz segment can also have more than two content channels similar to 11ax HE-SIGB.
  EHT-SIG efficiency significantly can be significantly improved.
    For 320MHz, even each 80MHz only have two content channels, there are 2X4=8 content channels in total.
Each STA only needs to process pre-EHT preambles in one 80MHz.

## Slide 8: Straw Poll #1
Do you agree that a STA only needs to process one 80MHz segment of the pre-EHT preamble?

## Slide 9: Straw Poll #2
Do you agree that content of U-SIG can be different for different 80MHz?

## Slide 10: Straw Poll #3
Do you agree that EHT-SIG can carry different content in each 80MHz?
  For PPDU BW larger than 80MHz.