## Slide 1: Group Addressed Frame Delivery for EHT
Date: 2020-02-06
Authors:

## Slide 2: Introduction
Currently, STAs associated with an AP receive frames that are:
  Individually addressed to that STA (TA = AP, and RA = STA)
  Group addressed to multiple STAs (TA = AP, and RA = group address)
    Group addressed DL BU delivery follows baseline DTIM/FMS mechanisms
      Note that broadcast frames fall into this category as well
Delivery of group addressed frames becomes less clear due to
  The presence of multiple links within the BSS and
  The existence of multiple MAC addresses at the AP side
We propose to clarify group delivery in a multi-link context
  Considering the different capabilities the STAs might have
  Preserving legacy operation, and covering different use cases of interest

## Slide 3: Considerations
The proposal covers different operation modes
  With the AP having different MAC addresses for each link (as per SFD)
    Generate Beacons in all of the active links (mode 1)
      First Mode: Multi-Link Group Addressed BU delivery
    Generate Beacons in one (subset) of the active links (mode 2)
      Second Mode: Single Link Group Addressed BU delivery
  With the STA having the following operating modes/capabilities:
    Single-Radio STA (i.e., STA can move from one link to another but cannot operate on more than one link at the same time)
    Multi-Radio STA (i.e., STA can operate in multiple links at the same time)
      Non-STR STA (i.e., cannot receive and transmit simultaneously)

## Slide 4: Mode 1: Multi Link (ML) Group delivery
An AP MLD schedules group delivery in every link
  Each AP generates own Beacons and schedules group DL BU delivery in its link
    Broadcast/group frames of the link are scheduled in this link as per baseline (DTIM etc.)
  An AP duplicates group addressed Data frames of other links in this link if:
    A member non-AP MLD belonging to the group is expected to only be awake in this link
    Note: This leads to duplicated group addressed DL BU delivery over multiple links
  Duplicate group addressed Data frames in other links satisfy the following
    TA is that of the AP transmitting the frames (of this link) and RA is the MAC address of the group
    Encryption uses the GTK of the AP transmitting the frames (not of other AP) (independent PNs as well)
  Sequence Number of the duplicated Data frames can be:
    Independent sequence Number w.r.t. original Data frame (enables duplicate avoidance)
      Preferred option as it preserves link independence (already separate GTKs, and PNs)
    Same sequence number as original Data frame (enables duplicate detection)

## Slide 5: Mode 1: ML Group delivery (cont.)
A non-AP STA wakes in any link to receive group addressed BUs
  Baseline protocols are used (e.g., DTIM/FMS) for wake/doze state transitions
    E.g., STA wakes to read DTIM beacon, and if group addressed DL BUs are present then
      Remain awake until RX of group addressed frame with MD=0 or until DTIM interval is over
  If non-AP STA is a Single Radio STA then
    STA needs to ensure not switch links during this period (possibility of frame losses)
      Link switching may lead to either frame losses or to duplicate receptions
  If non-AP STA is a Multi Radio STA then
    STA shall discard group addressed BUs RXed during this period in any link but one

## Slide 6: ML Group delivery-Summary
Pros:
  STAs can wake on any link to receive group addressed frames
  Provides legacy support in all links maintained by the MLD AP
  Improves reception reliability of group addressed frames to EHT MLD STAs
    MR STAs can receive group addressed frames in all links and discard duplicates
      This is possible only if Duplicate Detection is advertised
Cons:
  Requires replication of group addressed frames over multiple links
    Increased per-BSS airtime due to multiple beacons and group addressed frames
      This type of traffic is generally sent at lowest MCS/BWs etc., to increase likelihood of reception
    Not friendly to low latency and time sensitive traffic

## Slide 7: Mode 2: Single Link (SL) Group delivery
An AP MLD schedules group delivery only on one* link
  One AP* generates Beacons and schedules group delivery in this link
    No Beacons are generated in remaining links (including group BUs)
    May provide cross-link DTIM on other links (e.g., TIM broadcast, etc.)
  Can account for configuration requests from MLD STAs to elect the link
  Baseline protocols (e.g., DTIM/FMS) schedule group delivery in the link
    AP does not schedule delivery of individually addressed frames for an SR STA in other link(s) during group addressed DL BU delivery
    No particular considerations for individual frames for a MR STA unless
      MR STA is a non-STR STA in which case the AP should not cause the STA to transmit frames if the other STA of the MLD is receiving group addressed frames from the other AP of the MLD
*Here focusing on one link but AP MLD can elect more than one link of the set (e.g., use two links in this mode and keep one link free of Beacons etc.)

## Slide 8: Mode 2: Single Link (SL) Group delivery
Non-AP STA wakes to receive group addressed frames in one link
  Baseline protocols (e.g., DTIM/FMS) used for wake/doze state transitions
  E.g., STA reads DTIM beacon, and if group DL BUs are present then
    Stay awake until RX of group addressed frame with MD=0/until DTIM interval is over
    SR STA is assumed to be in doze state in other link(s) during this period
      And is expected to not be switching channel during this period
    MR STA can be in any state in other link(s) during this period
      Can receive individually addressed frames in other links while receiving other frames (including group addressed) in this link
      AP is expected to satisfy any non-STR limitation that the MR STA might have

## Slide 9: Single Link Group Addressed BU delivery
Pros:
  Simple extension of baseline rules for group addressed delivery
  No need to duplicate group addressed frames on other links
    No per-BSS airtime increase (single beacons and group addressed transmissions)
    Low latency and time sensitive friendly since other links are free from this type of traffic
Cons:
  Requires STAs to be awake in the anchor link during group addressed delivery
  No legacy support in links other than the anchor link

## Slide 10: Summary
We discuss two operation modes for group delivery in MLO BSS
  Mode 1: Multi-Link Group Addressed Delivery
    AP replicates group traffic over multiple links
    STA discards duplicated frames based on defined duplicate avoidance rules
  Mode 2: Single Link Group Addressed Delivery
    AP sends group traffic only on one link (or subset thereof)
    STA receives group traffic only on one link (or subset thereof)
We additionally propose that
  Mode 1 is added in Rel-1 (beneficial for legacy support)
  Mode 2 is added in Rel-2 (beneficial for low latency/time sensitive traffic)

## Slide 11: Straw Poll 1
Do you agree to add to the TGbe SFD the following
  For R1, each AP affiliated with an STR AP MLD shall follow the baseline rules for scheduling Beacon frame transmissions

## Slide 12: Straw Poll 2
Do you agree to add to the TGbe SFD the following
  A non-AP MLD shall follow the baseline rules to receive the group addressed data frames on one link that it may change at any time except during an ongoing group addressed delivery period.
    The link selected by the non-AP MLD is the group addressed data frames reception link
    The non-AP MLD shall discard any group addressed data frames that are not received in the selected link

## Slide 13: Straw Poll 3
Do you agree to add to the TGbe SFD the following
  An AP MLD shall schedule group addressed DL BU delivery in all the links at which its affiliated APs generate Beacon frames
    Group addressed DL BU delivery from each affiliated AP follow baseline group addressed delivery rules for that link (e.g., DTIM, FMS, etc)
    Group addressed DL BUs of another link shall be duplicated and scheduled for transmission in this link if at least one member non-AP MLD belonging to that group is expected to be awake on this link
      Duplicated MPDUs shall have configuration parameters (TA, security, sequence number, PN) of the affiliated AP transmitting the MPDU

## Slide 14: Straw Poll 4
Do you agree to add to the SFD:
  An AP MLD shall not cause a non-AP STA affiliated to a non-STR MLD STA to transmit an MPDU in a constrained link if another non-AP STA affiliated to the same STR MLD STA is scheduled to be receiving group addressed DL BUs in another link