## Slide 1: Priority Access Support Options for NS/EP Services
Date: 2020-03-15
Authors:

## Slide 2: Outline
This presentation covers the following:
  Overview of NS/EP Priority Services
  Assumptions
  Options for supporting priority access to NS/EP Priority Service non-AP STA(s) using OFDMA-based Triggered Uplink Access (TUA)

## Slide 3: Overview
Priority access support for National Security and Emergency Preparedness (NS/EP) priority services was approved as a work item in IEEE 802.11be during January 2020 meeting [1]
Objective Summary
  A standardized mechanism to support the NS/EP priority services in WLANs without requiring additional infrastructure
  Priority Access in IEEE 802.11be would also be beneficial to other services ( e.g., Public-Safety Mission-Critical Services, Critical medical applications)

## Slide 4: NS/EP Priority Services
Service Objective: Provide priority access to system resources for a limited set of authorized users during network congestion
  Priority Access: Allow preferred access to the wireless medium during network congestion and/or failures to establish a data session
  Limited Set: Number of users is generally a small fraction of the overall user base
  Authorized Users: Only available to some designated individuals who are identified to receive such service
Existing NS/EP Priority Services in the US provide priority voice calls over public networks
  Government Emergency Telecommunications Service (GETS): Legacy landline phone networks
  Wireless Priority Service (WPS): Wireless phone networks
  Next Generation Network Priority Services (NGN-PS): Providers’ IP-based communications networks
Many countries have similar priority telecommunications services, e.g.,
  Belgium: Blue Light Mobile, Canada: WPS, Czech Republic: Mobile Crisis Communications service, Great Britain: MTPAS
  GSM for Railway Communications deployed in multiple countries
NS/EP Priority Services are NOT Emergency Services (e.g., E911 in US; 112, 999, etc. in Europe)

## Slide 5: Assumptions
NS/EP Priority Service user’s non-AP STA is associated with BSS prior to invocation of priority capabilities
  Attachment, authentication, and authorization occur via standard procedures
After association, AP STA has the knowledge of which non-AP STAs are authorized to use NS/EP priority services
NS/EP Priority Service user’s non-AP STA will identify the need for priority and inform the AP STA
  Priority remains in effect until terminated by either party

## Slide 6: Use of OFDMA TUA for NS/EP Priority Services
Enabling priority in OFDMA scheduling (in presence of network congestion)
  AP sends Trigger Frame (e.g. BSRP) with periodic poll to non-AP STAs to determine data to be sent upstream
    Subsequent messages may not require the Trigger
  NS/EP-user non-AP STA reports access class and buffer status with priority indication
  AP STA verifies authorization of NS/EP Priority Service user
  AP STA incorporates higher priority flag into scheduling and RU-allocation decisions for NS/EP Priority Service non-AP STA

## Slide 7: Use of OFDMA TUA for NS/EP Priority Services
Options
  Option 1: Use existing Trigger Frame (e.g., BSRP) with periodic poll and extend QoS Control Field format to indicate the NS/EP Priority Service non-AP STA status in buffer status report
  Option 2: Define a new Trigger Frame and corresponding Report format exclusively for supporting the NS/EP Priority Services

## Slide 8: QoS Control Field Format for IEEE 802.11ax
QoS Control field
  QoS Control field enables non-AP STA to report the buffer status after receiving the Trigger Frame (e.g., BSRP) poll from an AP STA
    Non-AP STA can send multiple QoS Control fields to indicate requirements for multiple TCs
  Non-AP STA sends QoS Control field with TID and Queue Size in QoS Data or QoS Null frame
    TID (4 bits) maps to User Priority (UP) value
    UP Values 0-7 are assigned
      Values from 8 to 15 are not used in QoS frames since STAs do not use HCCA
QoS Control Field Format
1
A-MSDU Present
Queue Size
Ack Policy
TID

## Slide 9: Option 1: Extending QoS Control Field Format
Encode priority in QoS Control field TID
  Rationale: Only 0-7 is used for indicating the UP values
  Proposal: Assign bits 0-2 for TID and use bit 3 for indicating NS/EP Priority Service
    PS is set to 1 for NS/EP Priority Service and otherwise set to zero
  Impact: Non NS/EP Priority Service STAs will not be able to decode this information but this should not be an issue since MIB can be updated to address the backward compatibility
QoS Control field Format
1
A-MSDU Present
Queue Size
Ack Policy
TID
PS
bits 0-2
bit 3
bit 4
bit 7
bits 5-6
bits 8-15

## Slide 10: Option 2: Dedicated Trigger/Report for NS/EP Priority Services
Define a new Trigger Frame to request NS/EP Priority Services information
  Trigger asks NS/EP-aware and authorized non-AP STAs to report the need for NS/EP Priority Services
    Non-AP STAs can respond to enable/disable NS/EP Priority Services for specific ACs
  AP STA sends trigger periodically or based on some internal policy, for example,
    Sends only if at least one NS/EP-authorized STA is associated with BSS
    Sends only if BSS load exceeds specified threshold
  New Trigger frame can be a variant of existing Trigger frame format
    New trigger type subfield can be allocated from reserved set (8-15)

## Slide 11: Option 2: Dedicated Trigger for NS/EP Priority Services (Continued)
Need a reporting frame that will enable non-AP STAs to:
  Respond to NS/EP Priority Service trigger poll
    Can possibly make unsolicited requests for NS/EP Priority Service
  Specify ACs that require NS/EP Priority Service
    If possible include user’s NS/EP Priority level (one of five)
  Report queue size for each AC
Possible to define a format similar to the QoS Control field or BSR (with some modifications)
  Include multiple instances in an aggregate, one for each AC

## Slide 12: Option 2: Dedicated Trigger for NS/EP Priority Services (Continued)
Pros
  Flexibility to represent specific information related Priority Services
  No interference with existing features
Cons
    New Trigger Frame and report structure need to be defined to support the NS/EP Priority Service

## Slide 13: Summary
Described two possible approaches
  One leverages existing protocol constructs with updates
  Other one requires defining additional protocol elements
Feedback and comments ??

## Slide 14: References
[1] 11-19-1901-04-00be-priority-access-support-in-ieee-802-11be-what-and-why.pptx
[2] 11-20-0021-01-00be-Priority-Access-support_for_NS_EP_Services.pptx,
[2] IEEE P802.11ax™/D6.0, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, Amendment 1: Enhancements for High Efficiency WLAN”, November 2019
[3] IEEE Std 802.11™-2016, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 7 December 2016