## Slide 1: MLD Address Management Discussion
Date: 2020-03-19
Authors:
Name | Company | Address | Phone | Email
Harry Wang | Tencent | Tencent Building, Kejizhongyi Avenue, Hi-tech Park, Nanshan District, Shenzhen | +86-755-86013388 | harryhwang@tencent.com
Xin Zuo |  |  |  | 
Glenn Hu |  |  |  | 
Lander Li |  |  |  | 

## Slide 2: Background – Multiple Addresses
MLD address issues have been discussed in the group [1,2,3,4,5] as a function of MLO;
Some of general principles are summarized as follows,
  MAC SAP may need unique* address, which may be used to identify a MLD on DS, i.e the MLD address z;
  STAs may have separate addresses x/y i.e the STA/MAC/Link address, which may be the same or different as the MLD address z;
  AP MLD is preferred to have different STA address (x≠y) for the backward compatibility with legacy STAs;
  Non-AP MLD is therefore to use different STA addresses to enable symmetric operations, and to honor existing authentication process.
In nutshell, (x,y) is used for STA (low MAC) and (z) is for MLD (high MAC), if the MAC functions are separated in 11be.
With the support of Multiple BSSID, many more MAC addresses need to be managed by AP MLD.
MLD
MAC SAP
STA 1
STA 2
Addr(x)
Addr(z)
Addr(y)

## Slide 3: Address for Different Purposes
During MLD BSS setup,
  AP MLD needs to inform both its MLD address (z) and the STA addresses (x, y) to Non-AP MLD, and only the STA addresses (x or y) to the legacy;
  Non-AP MLD should present all its addresses to AP MLD as well, so that
  The connection being setup on one link works for all links;
After successful setup,
  TA/RA in MAC headers are preferred to use STA address (say x);
  SA/DA for MSDUs are preferred to use MLD address (z);
All MLD, both AP and Non-AP, should have at least a MLD address built-in or pre-installed by the network administrator, that is unique at some extent.
MLD
MAC SAP
STA 1
STA 2
Addr(x)
Addr(z)
Addr(y)

## Slide 4: Proposal
In this contribution, we propose to use dynamical allocation and management for the STA addresses for both AP and Non-AP.
With respect to the concept and protocols defined in 802c, 802.11aq and P802.1CQ.

## Slide 5: AP MLD (STA) Address Management
Option I
Option II
SME
STA 1
MLME
AP MLD
MLME-AddrAssign. request
MLME-AddrAssign. confirm
STA address generated
SME
STA 1
MLME
AP MLD
MLME-AddrAssign. request
MLME-AddrAssign. confirm
STA1 address assigned
Beacon (w/ STA1 address)
Beacon (w/ STA1 address)
The collision probability of STA address is low and can be solved by algorithm.
Better to use dedicated address management primitive e.g MLME-AddrAssign.request/confirm.
In current spec, MLME-RESET is used to reset MLME with an initial address.
w/ STA1 addresses
w/ STA1 addresses

## Slide 6: Non-AP MLD (STA) Address Management
Option I
Option II
STA 1
STA 2
AP MLD
STA 12
STA 11
STA MLD
Request w/ MLD address
Response w/ STA address assignment for STA12 and STA11
STA 1
STA 2
AP MLD
STA 12
STA 11
STA MLD
Request w/ self-assigned STA address and MLD address
Response w/confirm
Option I and II procedures take place during network discovery and selection, prior to association.
The STA addresses confirmed by the procedure will be used for authentication and association.

## Slide 7: Conclusion
The opinions for MLD and STA addresses so far are summarized.
Propose to support a dynamic STA/MAC/Link address (t.b.d term) management for MLD.

## Slide 8: SP#1
Do you agree that AP MLD should support dynamic address management for the affiliated STAs.

## Slide 9: SP#2
Do you agree that Non-AP MLD should support dynamic address management for the affiliated STAs.

## Slide 10: SP#3
Do you agree that 802.11be should support an address management protocol for AP MLD and Non-AP MLD.

## Slide 11: Reference
19-1899r7, MLA MAC Addresses Considerations;
20-0180r1, MLLE MAC addresses
20-0063r0, Non-AP MLD Link Address
19-1962r1, Multi-Link Device Instance & New Frame MAC Header
20-0054r0, MLD MAC Address and WM Address