## Slide 1: Multiple BSSID for Multi-link Operation
Date: 2020-05-10
Authors:

## Slide 2: Background
Multiple BSSID is a mandatory feature in 802.11ax, it is straight forward to implement it at EHT AP
  There exits only one transmitted BSSID and a few nontransmitted BSSIDs
  Only transmitted BSSID is allowed to send Beacon and Probe Response frames which contain Multiple BSSID element
  Nontransmtted BSSID info could be derived by Multiple BSSID element
For an AP MLD, each AP could operate in Multiple BSSID mode
  Multiple BSSID info at each AP could be shared with each other
In this contribution, we discuss the multi-link operation in case of Multiple BSSID

## Slide 3: Background
In the Spec [1], we agreed that a new element will be defined as a container to advertise and exchange capability information for multi-link setup.
Multi-link device element is proposed in [2] to be used for exchange the capability info between two MLDs
Like Multiple BSSID element, MLD element could use the same structure, containing common part and a few link parts
Common part
Link 1
Link 2
Link 2
…
Per link Part

## Slide 4: MLD with Multiple BSSID
There may exist two configurations for MLD with Multiple BSSID
One configuration: all the transmitted BSSIDs are from the same MLD
  Simplify the advertisement
  One MLD element, and Multiple BSSID element is present in a link part if the corresponding reported AP is in Multiple BSSID set
  But lack of link specific Multiple BSSID configuration flexibility
  An example is shown below, BSSID with “x” is transmitted BSSID

## Slide 5: MLD with Multiple BSSID
Another configuration: each AP in a MLD operates as transmitted or nontransmitted BSSID independently
  Advertisement is relative complex, but provide link specific Multiple BSSID configuration
  An example is shown below, BSSID with “x” is transmitted BSSID
  Base on the recent related straw poll result, TGbe group agreed this configuration （we call it Co-located AP MLD set）

## Slide 6: Advertisement for MLD with Multiple BSSID
During the discovery phase [3,4], the non-AP MLD could find the minimum info of all the APs in co-located AP MLD set through RNR element and/or Multiple BSSID element
Before multi-link association, non-AP MLD is expected to have full information of co-located AP MLD set to select a best AP MLD
  Non-AP MLD could request the full info of all the APs in the co-located AP MLD set through Probe Request frame
However, a MLD element can only carry full info of other APs in the same MLD as the reporting AP, and a gap exists
  Not every AP in Co-located AP MLD set can be advertised

## Slide 7: Advertisement for MLD with Multiple BSSID
We propose the following two options to advertise the co-located AP MLD set
  Opt1: One MLD element can carry the info of the reported APs in more than one MLD
  Opt2： One MLD element can only carry the info of the reported APs in a MLD, but it requires more than one MLD element
  Take the following figure for an example where BSSID with “x” is transmitted BSSID, and BSSID 1x sends this advertisement
  In opt1, a MLD element should carry the info of BSSID-2y, BSSID-2x, BSSID-2z and BSSID 3x and BSSID 3y while BSSID-1y is carried in Multiple BSSID element
  In opt 2, it has three MLD elements, describing the APs in MLD1, MLD2 and MLD 3 respectively

## Slide 8: Summary
In this contribution, we propose the AP could advertise the info of all other APs in the same co-located AP MLD set through one or more MLD elements

## Slide 9: References
[1] 11-19-1262-09-00be-specification-framework-for-tgbe
[2] 11-20-0396-00-00be-mlo-bss-information-transmission -and-multiple-bssid-support
[3] 11-20-0389-00-00be-multi-link-discovery-part-1
[4] 11-20-0615-00-00be-Discovery mechanism for MLD

## Slide 10: SP 1
Do you agree that the AP could advertise the info of all other APs in the same co-located AP MLD set
  The co-located AP MLD set includes
  All the APs in the same MLD as the reporting AP
  All the other APs in the same Multiple BSSID set (if any) as any AP in the same MLD as the reporting AP